## Slide 1: TSDSI Radio Interface Technology (RIT)

## Slide 2: Highlights
TSDSI RIT meets IMT 2020 requirements
  eMBB peak data rate ≅ 5 Gbps per component carrier
  URLLC Reliability ≅ 99.9999%
  mMTC connection density ≅ 2 million devices

## Slide 3: Supported Frequency Bands
FR1: 450 MHz – 6000 MHz; FR2: 24250 MHz – 52600 MHz
TDD and FDD bands supported (support for flexible duplexing)
Bandwidth supported: 5MHz to 400 MHz
Carrier aggregation supported
Band number | UL operating band | DL operating band
n1 | 1920 – 1980 MHz | 2110 – 2170 MHz
n2 | 1850 – 1910 MHz | 1930 – 1990 MHz
n3 | 1710 – 1785 MHz | 1805 – 1880 MHz
n5 | 824 – 849 MHz | 869 – 894MHz
n7 | 2500 – 2570 MHz | 2620 – 2690 MHz
n8 | 880 – 915 MHz | 925 – 960 MHz
n12 | 699-716 MHz | 729-746 MHz
n20 | 832 – 862 MHz | 791– 821MHz
n28 | 703 – 748 MHz | 758 – 803 MHz
n38 | 2570 – 2620 MHz | 2570 – 2620 MHz
n40 | 2300 -- 2400 MHz | 2300 – 2400 MHz
n41 | 2496 – 2690 MHz | 2496 – 2690 MHz
n50 | 1432 – 1517 MHz | 1432 – 1517 MHz
n51 | 1427 – 1432 MHz | 1427 – 1432 MHz
n66 | 1710 – 1780 MHz | 2110 – 2200 MHz
n70 | 1695 – 1710 MHz | 1995– 2020 MHz
n71 | 663 – 698 MHz | 617 – 652 MHz
n74 | 1427 –1470 MHz | 1475 – 1518 MHz
n75 | N/A | 1432 – 1517 MHz
n76 | N/A | 1427 – 1432 MHz
n77 | 3.3 – 4.2 GHz | 3.3 – 4.2 GHz
n78 | 3.3 – 3.8 GHz | 3.3 – 3.8 GHz
n79 | 4.4 – 5.0 GHz | 4.4 – 5.0 GHz
n80 | 1710 – 1785 MHz | N/A
n81 | 880 – 915 MHz | N/A
n82 | 832 – 862 MHz | N/A
n83 | 703 – 748 MHz | N/A
n84 | 1920 – 1980 MHz | N/A
n86 | 1710-1780 MHz | N/A
Band number | UL operating band | DL operating band
n257 | 26.5 –29.5 GHz | 26.5 –29.5 GHz
n258 | 24.25 – 27.5 GHz | 24.25 – 27.5 GHz
n260 | 37–40 GHz | 37–40 GHz
n261 | 27.5 – 28.350 GHz | 27.5 – 28.350 GHz
Operating Band | Uplink (UL) operating band |  |  |  | Downlink (DL) operating band |  |  |  | 
1 | 1920 MHz |  | – | 1980 MHz | 2110 MHz |  | – |  | 2170 MHz
2 | 1850 MHz |  | – | 1910 MHz | 1930 MHz |  | – |  | 1990 MHz
3 | 1710 MHz |  | – | 1785 MHz | 1805 MHz |  | – |  | 1880 MHz
4 | 1710 MHz |  | – | 1755 MHz | 2110 MHz |  | – |  | 2155 MHz
5 | 824 MHz |  | – | 849 MHz | 869 MHz |  | – |  | 894MHz
8 | 880 MHz |  | – | 915 MHz | 925 MHz |  | – |  | 960 MHz
11 | 1427.9 MHz |  | – | 1447.9 MHz | 1475.9 MHz |  | – |  | 1495.9 MHz
12 | 699 MHz |  | – | 716 MHz | 729 MHz |  | – |  | 746 MHz
13 | 777 MHz |  | – | 787 MHz | 746 MHz |  | – |  | 756 MHz
17 | 704 MHz |  | – | 716 MHz | 734 MHz |  | – |  | 746 MHz
18 | 815 MHz |  | – | 830 MHz | 860 MHz |  | – |  | 875 MHz
19 | 830 MHz |  | – | 845 MHz | 875 MHz |  | – |  | 890 MHz
20 | 832 MHz |  | – | 862 MHz | 791 MHz |  | – |  | 821 MHz
21 | 1447.9 MHz |  | – | 1462.9 MHz | 1495.9 MHz |  | – |  | 1510.9 MHz
25 | 1850 MHz |  | – | 1915 MHz | 1930 MHz |  | – |  | 1995 MHz
26 | 814 MHz |  | – | 849 MHz | 859 MHz |  | – |  | 894 MHz
28 | 703 MHz |  | – | 748 MHz | 758 MHz |  | – |  | 803 MHz
31 | 452.5 MHz |  | – | 457.5 MHz | 462.5 MHz |  | – |  | 467.5 MHz
41 | 2496 MHz |  |  | 2690 MHz | 2496 MHz |  |  |  | 2690 MHz
66 | 1710 MHz | – | 1780 MHz |  | 2110 MHz | – |  | 2200 MHz | 
70 | 1695 MHz | – | 1710 MHz |  | 1995 MHz | – |  | 2020 MHz | 
71 | 663 MHz | – | 698 MHz |  | 617 MHz | – |  | 652 MHz | 
72 | 451 MHz | – | 456 MHz |  | 461 MHz | – |  | 466 MHz | 
74 | 1427 MHz | – | 1470 MHz |  | 1475 MHz | – |  | 1518 MHz | 

## Slide 4: Modulation
Downlink
(BS to UE)
OFDM
QPSK
16QAM
64QAM
256 QAM
Uplink
(UE to BS)
DFT-S OFDM
OFDM
BPSK
QPSK
16QAM
64QAM
256 QAM
π/2-BPSK
BPSK
QPSK
16QAM
64QAM
256 QAM
Downlink
(BS to UE)
Uplink
(UE to BS)
eMBB and URLLC
MMTC
FEC: LDPC, Polar, Reed-Muller, Repetition coding
Asynchronous HARQ for reliability
FEC: Turbo coding
DFT-S OFDM
OFDM
QPSK
shaped- BPSK
π/2-BPSK
π/4-QPSK
QPSK

## Slide 5: Time-Frequency Resources
10 ms
Frame
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Subframe: 1ms
14 OFDM symbols
14 OFDM Symbols
14 OFDM
One slot: 1ms; 15KHz
One slot: 0.5 ms; 30KHz
One slot: 0.125 ms; 120KHz
38.211
  Sub carrier spacing: Multiple numerologies (15k, 30k, 60k, 120k);
    Special cases 1.25k, 5k, 240k (for specific transmissions)
  Long and short cyclic prefix supported

## Slide 6: MIMO Capabilities
Downlink: 12 MU-MIMO layers
  Max 4 layers per UE in MU-MIMO
  Max 8 layers per UE in SU-MIMO
Uplink: 12 MU-MIMO layers
  Max 4 layers per UE
32 CSI-RS antenna ports for enhanced CSI
Multiple beam operations
  coverage in high frequency bands
  Beam measurement, reporting etc. supported
Reference signals: DMRS, PTRS, CSI-RS, SRS
  UE specific, low over head
  Supports high frequency bands

## Slide 7: Other Salient Features
Power Saving
User specific pilots
DRX cycle
BWP adaptation
Mobility
Cell level and Beam level
Latency
Mini slots
RLC reordering is not required (moved to PDCP)
Mac enhancements for faster beam switching, failure recovery
QoS
New layer Service Data Adaptation Protocol
Mapping between QoS and data Radio bearer
Coverage
Low PAPR waveforms for uplink
-Removed RLC concatenation (from LTE)
- Asynchronous HARQ in UL & DL
- Scalable numerology in MAC scheduling
- Enhanced LCP
- Several deployment options

## Slide 8: Relevant Documents
[T3.9022.261] “Service requirements for next generation new services and markets” [T3.9037.340] “NR; Multi-connectivity; Overall description; Stage-2” [T3.9038.101-1] “NR; User Equipment (UE) radio transmission and reception; Part: Range 1 Standalone” [T3.9038.101-2] “NR; User Equipment (UE) radio transmission and reception; Part: Range 2 Standalone” [T3.9038.133] “NR; Requirements for support of radio resource management” [T3.9038.201] “NR; Physical layer; General description” [T3.9038.211] “NR; Physical channels and modulation” [T3.9038.212] “NR; Multiplexing and channel coding” [T3.9038.213] “NR; Physical layer procedures for control” [T3.9038.214] “NR; Physical layer procedures for data” [T3.9038.215] “NR; Physical layer measurements” [T3.9038.300] “NR; Overall description; Stage-2” [T3.9038.304] “NR; User Equipment (UE) procedures in idle mode” [T3.9038.321] “NR; Medium Access Control (MAC) protocol specification” [T3.9038.322] “NR; Radio Link Control (RLC) protocol specification” [T3.9038.401] “NG-RAN; Architecture description” [T3.9036.101] “Evolved Universal Terrestrial Radio Access (E-UTRA); User Equipment (UE) radio transmission and reception” | [T3.9036.133] “Evolved Universal Terrestrial Radio Access (E-UTRA); Requirements for support of radio resource management” [T3.9036.104] “Evolved Universal Terrestrial Radio Access (E-UTRA); Base Station (BS) radio transmission and reception” [T3.9036.201] “Evolved Universal Terrestrial Radio Access (E-UTRA); LTE physical layer; General description” [T3.9036.211] “Evolved Universal Terrestrial Radio Access (E-UTRA); Physical channels and modulation” [T3.9036.212] “Evolved Universal Terrestrial Radio Access (E-UTRA); Multiplexing and channel coding” [T3.9036.213] “Evolved Universal Terrestrial Radio Access (E-UTRA); Physical layer procedures” [T3.9036.214] “Evolved Universal Terrestrial Radio Access (E-UTRA); Physical layer; Measurements” [T3.9036.300] “Evolved Universal Terrestrial Radio Access (E-UTRA) and Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Overall description; Stage 2” [T3.9036.304] “Evolved Universal Terrestrial Radio Access (E-UTRA); User Equipment (UE) procedures in idle mode” [T3.9036.321] “Evolved Universal Terrestrial Radio Access (E-UTRA); Medium Access Control (MAC) protocol specification” [T3.9036.322] “Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Link Control (RLC) protocol specification” [T3.9036.331] “Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Resource Control (RRC); Protocol specification [T3.9036.401] “Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Architecture description”