## Slide 1
Service Experience Assured Network (SEAN) Introduction and Demo

## Slide 2
Category | Business | Bandwidth | Latency
Enhanced Mobile Broadband | UHD/Holographic, Virtual Reality & Augmented Reality | DL: 1 Gbps, UL: 500 Mbps | 10 ms
 | Tactile Internet | DL: 50 Mbps, UL: 25 Mbps | <1 ms
Mission Critical IoT | Autonomous Traffic Control / Driving | DL: 50 kbps～10 Mbps; UL: a few bps～10 Mbps | 1 ms
 | Robot Collaboration |  | 
 | Remote Motion Control /Telesurgery |  | 
 | eHealth: Telemedicine | DL: 10 Mbps, UL: 10 Mbps | 10 ms
 | Public Safety |  | 
 | 3D Connection: Packet delivery using drones |  | 
Massive IoT | Mobile Monitors | DL: 300 Mbps, UL: 50 Mbps | 10 ms
5G Use Case and Requirement
Maximum bandwidth requirement of single user >1Gbps
Latency requirement of some use cases (tactile internet, autonomous driving, motion control) <1ms

## Slide 3
Challenge of New Business
4K/8K Video
VR/AR
ITU-R BT.2020 4K/UHD video standard support 120p、60p、50p、30p、25p etc.
Bandwidth requirement:
  35Mbps for 4K, 75Mbps for Ultra 4K,
  140Mbps for 8K, 330Mbps for Ultra 8K
4K video require RTT(Round Trip Time ) below 35ms，even less for 8K video.
  People feel dizzy since users’ motion perception is not match with images(Motion sickness), need to get latency down to 20 ms, or possibly much less.
AR are more latency sensitive than immersive VR, because real world objects have no latency and delays of virtual objects can be seen directly.
Smart Grid
Smart grid is a generic label for the application of computer intelligence and networking abilities to a dumb electricity distribution system.
Latency requirements for smart grid vary from less than 10 ms for teleprotection, to about 20 ms for some synchrophasors applications, to 100-200 ms for smart grid control, to up to several seconds for smart metering.
Challenge: Need a solution to provide strictly assured service performance in 5G network

## Slide 4
  SEAN: Ultra-low Latency, Zero Packet Loss
  Bandwidth Guarantee
Interface
Interface
NPU
Heterogeneous NPU
Optimized forwarding Architecture
Latency Aware Traffic Manager
Ultra-low latency queuing technology
Latency Guaranteed Scheduling algorithms
Smart buffer management
A piece of pipe of zero packet loss and low latency(Router/Switch)
Pipe entrance
Pipe
fore part
Pipe
latter part
TM
Pipe
connection
Latency optimized switch fabric algorithms
Switch
Fabric
for
strict bandFlex Ethernet width guarantee

## Slide 5
Channelized FlexE
Channelized FlexEth can provide guaranteed bandwidth, low latency and jitter, and can support “L1 LAG” based high bandwidth interface
Key Technology 1：Flexible Ethernet for
Guaranteed Link Latency and Bandwidth

## Slide 6
Coprocessor
& Memory
Key Technology 2：Optimized NPU
and Forwarding Architecture
Pkt Dist
Pkt Agr
Processor
Priority mapping based on application
HP packets are guaranteed to be processed first and not dropped
Memory
Heterogeneous NPU Architecture：
  Less instructions and branches for lower latency
Optimized forwarding flow：
  Simplified forwarding table design
  Forwarding action optimization
By using optimized NPU and forwarding architecture, typical latency for IPv4 packet processing latency can be reduced from 5us to <2us
Chart: 
| 指令 执行 | 线程 切换 | 表项 查找
现状时延(us) | 0.6 | 2.68 | 2.47
优化时延(us) | 0.6 | 1.27 | 1.2
Pri Proc
Pri
Sch
Classification
Data path
Inst Exec
Pending
Lookup
Before
After

## Slide 7
Key Technology 3：Latency Aware Traffic Manager
Enq
Deq
Queue Manager
Guarantee QOS
Traffic Manager
Preemption of HP packets
Bypass data path for low latency application
Latency Guaranteed Scheduling Algorithms for HQoS
Smart Buffer：smart management of buffer to provide service guarantee for HP traffic
On chip buffer and off-chip buffer BW reduction algorithms
Guaranteed 1～5us latency and jitter for E2E FlexE Hard Pipe + low latency traffic manager
On chip Cache and Packet Buffer Manager
WRED
Scheduler
Packet Memory

## Slide 8
connector
Controller
Router-1
TesEngine
(sender)
TesEngine
(receiver)
VR Servers
FlexE Link
Router-2
SEAN PoC Environment

## Slide 9
THANK YOU
Copyright©2016 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.