## Slide 1: QUALITY OF SERVICE MEASUREMENTS OF BROADBAND INTERNET
SG12 Regional Group for Africa Meeting
18th to 19th of July, 2013
Ouagadougou, Burkinafaso
By Yvonne UMUTONI
Quality of Service Development Group (QSDG) Chair

## Slide 2: CONTENT
EXECUTIVE SUMMARY
REFERENCE ARCHITECTURE
QUALITY OF SERVICE CLASSES
QUALITY OF SERVICE MONITORING OF INTERNET SERVICES
QUALITY OF SERVICE MEASUREMENT METHODOLOGIES
INTERNATIONAL PRACTICES
CHALLENGES
KEY PERFORMANCE INDICATORS
CONCLUSION AND RECOMMENDATION

## Slide 3: EXECUTIVE SUMMARY
This presentation focusses on the quality of service measurements for the fixed broadband internet networks from the Regulator point of view.
QoS Classes and reference architecture for IP-based networks standardized by ITU are highlighted.
Advantages and disadvantages of the two QoS measurement methodologies (Passive & Active) adopted worldwide in order to evaluate the quality of service performance of internet networks are explained.
International practices in line with the QoS measurement of broadband internet services are presented.
Lastly, most utilized KPIs in evaluating the quality of service of internet are also illustrated.

## Slide 4: REFERENCE ARCHITECTURE

## Slide 5: QUALITY OF SERVICE CLASSES
Table 1: QoS Classes of IP based networks [ITU-T Rec. Y.1541]
QoS Class | Service/Application | Network Performance Parameters |  | 
 |  | IP TD | IPDV | IPLR
Class 0 | Voice over IP (VoIP) Video Teleconference (VTC) Note 1: PSTN Voice quality | ≤100 ms | ≤50 ms | ≤10–3
Class 1 | Voice over IP (VoIP) Video Teleconference (VTC) Note 2: Satellite Voice quality | ≤400 ms | ≤50 ms | ≤ 10–3
Class 2 | Transaction data Note 3: Highly Interactive data (Signalling) | ≤100 ms | U | ≤10–3
Class 3 | Transaction data Note 4: Interactive data (Business data) | ≤400 ms | U | ≤10–3
Class 4 | Video streaming | ≤1 s | U | ≤10–3
Class 5 | Traditional applications of Default IP networks | U | U | U

## Slide 6: QUALITY OF SERVICE MONITORING OF INTERNET SERVICES
Generally, the Internet QoS Monitoring Framework is set/identified by the Regulator at national level in collaboration with Operators and Consumers. For QoS enforcement purposes, Regulators require to have legal and regulatory tools.
However, QoS expectations of internet users vary from service to service.
Web browsing, File transfer, Video Streaming and VoIP are the most popular internet services around the world.
Therefore, in order to measure the quality of service experienced by internet users, QoS parameters of each internet-based service have to be identified and measured separately as the QoS for real time applications differ from QoS for non-real-time applications.
Two types of methodology for measuring the quality of service of internet services are the following:
  Passive Testing and
  Active Testing.
Notes: Operators are especially consulted during deployment of monitoring tools, setting QoS parameters targets and auditing.
- While consumers may be involved during deployment of monitoring tools and collecting test results.

## Slide 7: QUALITY OF SERVICE MEASUREMENT METHODOLOGIES
a) Passive Testing (Ref: http://www.epitiro.com/):
  Sniffs traffic (user data) as it is routed through a device;
  Performs analysis based on monitoring network traffic between two destinations.
Advantages:
  The probe only needs 1 connection point to the network which mean less hardware
  Does not ‘take over’ the line under test so is never an inconvenience to end users.
Disadvantages:
  Unknown traffic type makes it difficult to test maximum line capability
  Difficult to average different tests as the data traffic is not consistent

## Slide 8
b) Active Testing (Ref: http://www.epitiro.com/):
Performs analysis based on sending traffic (probing packets) between two destinations;
Probing packets are injected in the network connection in order to measure the quality of service (QoS) of different services (web browsing, file transfer, VoIP, etc) over Internet connections.
Advantage:
  The data (probing packets) is originated from a controlled source with predefined settings and therefore types of services can be fully controlled
  Easy benchmarking / comparison between measurements obtained from different internet connections provided by different ISPs.
Disadvantage:
  Requires that the line under test be fully available
  Test design must be sure the line is idle before testing
  Requires both sending & receiving probes (monitoring tools)
  Cost implications

## Slide 9: INTERNATIONAL PRACTICES
Most of Regulators use the “Active Testing” methodology in order to measure the QoS of Broadband Internet provided by ISPs. The Active Testing allows them to produce a benchmarking report regularly.
On 2nd of February 2012 , OFCOM published a research report on the Fixed line broadband performance in the UK. For data collection, a number of hardware monitoring tools (probes) has been distributed to the selected panellists. Download/Upload speed, packet loss, DNS resolution time, DNS failure ratio, jitter QoS parameters have been assessed.
Ref: http://stakeholders.ofcom.org.uk/binaries/research/broadband-research/Fixed_bb_speeds_Nov_2011.pdf.

## Slide 10
July 2011, Commerce Commission in New Zealand published a report on “New Zealand Broadband Quality”.
According to http://ebookbrowse.com/gdoc.php?id=304111847&url=661ac119290f8f340e8387fe2105d103,
New Zealand has adopted the Active data collection measurement methodology and the assessed quality parameters for the broadband internet are the following : web browsing speed, DNS response times, international browsing, internet robust & browsing availability and service speed variability.
Reference made to http://www.ida.gov.sg/doc/Policies%20and%20Regulation/Policies_and_Regulation_Level2/20060424141236/Qos_webpage_bb.pdf ;
IDA utilizes the following QoS parameters to evaluate the QoS of Broadband Internet accessed by Users in Singapore: Network Availability, Latency (national and international), bandwidth utilization, service activation time and customer service support.

## Slide 11
Telecommunications Regulatory Authority (TRA) of Bahrain adopted the active testing methodology ( through Epitiro Ltd solution) so as to measure continuously the quality of service performance of broadband internet provided by ISPs.
According to http://www.tra.org.bh/en/pdf/FixedBroadbandAnalysisReportQ22012.pdf,
QoS parameters evaluated are the TCP Download/Upload speed, HTTP download speed (cached and non-cached), ping time and DNS time.
Rwanda Utilities Regulatory Authority (RURA) adopted the active testing methodology in order to measure continuously the QoS performance of Fixed Broadband Internet provided by ISPs. The tested QoS parameters are, but not limited to: HTTP Download speed, TCP Upload/Download speed, DNS Resolution time, and latency.

## Slide 12: CHALLENGES
Although the active testing is mostly adopted by many Regulators for data collection measurements of broadband internet , but this methodology does have some challenges during implementation as follows:
    The cost of implementing this methodology is quite high.
    For benchmarking/ comparison of QoS performance of various ISPs, the sampling methodology is very critical. QoS monitoring tools (probes) have to be deployed in a manner to replicate a “like to like” or “apple to apple” QoS performance comparison of ISPs.
    It requires as well a very close collaboration with ISPs and internet consumers.

## Slide 13: KEY PERFORMANCE INDICATORS
Key Performance Indicator | value
HTTP Download speed | Kbytes/s
TCP Download/Upload speed | Mbits/s
Latency (network round trip time) | milliseconds
Packet loss | Number of Packets/s
DNS Response times | milliseconds
Following table is presenting the most adopted key performance indicators world wide so as to measure the QoS performance of broadband internet.
Table 2: Key Performance Indicators

## Slide 14: Conclusion and Recommendation
For benchmarking purposes of ISPs, active QoS measurement is adopted by numerous Regulators during data collection.
QoS parameters of internet services like web browsing, file transfer, video streaming and VoIP are mostly evaluated by Regulators in order to rank the quality of broadband internet provided by ISPs in their respective countries. But the most evaluated internet services currently are web browsing and file transfer.
Also for benchmarking purposes, QoS monitoring tools should be deployed in a manner to replicate a “like-to-like” QoS performance comparison of ISPs.