MOD	IAP/5/182

# 3	Limits to the change in the power flux-density to protect the broadcasting-satellite service in Regions 1 and 2 in the band 12.2-12.5 GHz and in Region 3 in the band 12.5-12.7 GHz

With respect to § 4.1.1 c) of Article 4, an administration in Region 2 shall be considered as being affected if the proposed new or modified assignment in the Regions 1 and 3 List would result in exceeding the following power flux-density limits, at any test point in the service area affected:

–147 	dB(W/(m2 ( 27 MHz)) 			for  0°		( θ < 0.23°

–135.7 + 17.74 log θ 		dB(W/(m2 ( 27 MHz))		for  0.23°	( θ < 1.8°

–134.0 + 0.89 θ2 	dB(W/(m2 ( 27 MHz))		for  1.8°	( θ < 5.0°

–129.2 + 25 log θ 		dB(W/(m2 ( 27 MHz))		for  5.0°	( θ < 10.57°

–103.6		dB(W/(m2 ( 27 MHz))			for  10.57°	( θ

where ( is the minimum geocentric orbital separation in degrees between the longitudes of the broadcasting-satellite space station in Region 1 or 3 and the broadcasting-satellite space station affected in Region 2 taking into account the respective East-West station keeping errors.

With respect to § 4.2.3 a), 4.2.3 b) or 4.2.3 f) of Article 4, as appropriate, an administration in Region 1 or 3 shall be considered as being affected if the proposed modification to the Region 2 Plan would result in exceeding the following power flux-density limits, at any test point in the service area affected:

–147 		dB(W/(m2 ( 27 MHz)) 			for 0°		( θ < 0.23°

–135.7 + 17.74 log θ 		dB(W/(m2 ( 27 MHz))		for 0.23°	( θ < 2.0°

–136.7 + 1.66 θ2 	dB(W/(m2 ( 27 MHz))		for 2.0°	( θ < 3.59°

–129.2 + 25 log θ 		dB(W/(m2 ( 27 MHz))		for 3.59°	( θ < 10.57°

–103.6 		dB(W/(m2 ( 27 MHz))			for  10.57°	( θ

where ( is the minimum geocentric orbital separation in degrees between the longitudes of the broadcasting-satellite space station in Region 2 and the broadcasting-satellite space station affected in Region 1 or 3 taking into account the respective East-West station keeping errors.

Reasons:	Based on ITU-R studies, provides protection to Region 2 BSS assignments employing antenna sizes in the range 0.45-2.4 m from new or modified BSS assignments of the Regions 1 and 3 List; and provides protection to Regions 1 and 3 BSS assignments employing antenna sizes in the range 0.6-2.4 m from modifications to the Region 2 Plan.