ADD	EUR/13A12/15

5.XXX	In the band 35.5-36.0 GHz, the mean power flux-density generated by any EESS/SRS (active) spaceborne sensor at the Earth’s surface for any angle greater than 0.8º from the beam centre shall not exceed (73.3 dB(W/m2) in any 2 GHz band.

Reasons:	ITU-R studies have shown that sharing is feasible between the EESS/SRS (active) and the radiolocation service if the pfd level radiated in the spaceborne sensor side lobes is limited, and that sharing with the fixed service in the 35.5-36 GHz band is feasible without any constraint on the EESS/SRS (active).