MOD	EUR/13A12/4

5.460	The use of the band 7 145-7 190 MHz by the space research service (Earth-to-space) is restricted to deep space; no emissions to deep space shall be effected in the band 7 190-7 235 MHz.

Reasons:	Footnote 5.460 allocates the band 7 145-7 235 MHz on a primary basis to the space research service (Earth-to-space), subject to agreement under No. 9.21. This is the companion band for the primary space research service allocation in the band 8 400-8 500 MHz, which is coordinated under No. 9.17. This causes a cumbersome double coordination procedure for earth stations supporting satellite missions in these bands. The original requirement for coordination under No. 9.21 was the lack of coordination parameters in Appendix 7. WRC-2000 has revised Appendix 7 to include space research station parameters and coordination methodologies in the band 7 145-7 235 MHz so that there is no longer any requirement to impose the added administrative burden of No. 9.21. There are no geostationary satellites operated in the band 7 145-7 190 MHz, restricted to deep space missions, and potentially very few in the band 7 190-7 235 MHz, restricted to near Earth missions. ENG/OB systems are operated by some administrations and cannot accept constraints regarding deployment and mobility. However, the very low number of earth stations and their deployment in remote and well-shielded locations will in practice not constrain ENG/OB operations. The required coordination for the space research service under No. 9.17 will also provide a means for those administrations concerned with the protection of existing systems.

ARTICLE  21