MOD	EUR/13A27/64

4.2.14	An administration which has not notified its comments either to the administration seeking agreement or to the Bureau within a period of four months following the date of the BR IFIC referred to in § 4.2.8 shall be deemed to have agreed to the proposed modification. The Bureau shall send reminder telegrams 30 days before the expiry of the above four-month period. This time-limit may be extended by up to three months for an administration which has requested additional information under § 4.2.12 or for an administration which has requested the assistance of the Bureau under § 4.2.22. In the latter case, the Bureau shall inform the administrations concerned of this request. Upon expiry of the deadline for comments, the Bureau shall, according to its records, publish a Special Section, indicating the list of administrations having submitted their disagreement or other comments within the regulatory deadline.

Reasons:

–	First modification: to convert the Rule of Procedure on paragraphs 4.1.10 and 4.2.14 of Article 4 of Appendices 30 and 30A into regulatory provisions.

–	Second modification: to provide administrations with a clear picture of the coordination requirements and to avoid any uncertainties in that respect, similarly to No. 9.53A.

APPENDIX  4  (WRC-2000)

Consolidated list and tables of characteristics for use in the 
application of the procedures of Chapter III

ANNEX  2A

Characteristics of satellite networks’ earth stations 
or radio astronomy stations2     (WRC-2000)

# C	Characteristics to be provided for each group of frequency assignments for a satellite antenna beam or an earth station or radio astronomy station antenna

## C.9	Information on modulation characteristics

...