MOD	EUR/13A27/17

### 1.4.5	Broadcasting-satellite service earth stations

For earth stations in the broadcasting-satellite service, the coordination area is determined by extending the periphery of the specified service area within which the earth stations are operating by the coordination distance based on a typical BSS earth station. In calculating the coordination distance, no additional protection can be assumed to be available from the earth station horizon elevation angle, i.e. Ah  0 dB in Annex 1, for all azimuth angles around the earth station.

Reasons:	To broaden the scope of Appendix 7 to planned BSS.

ANNEX  7

System parameters and predetermined coordination distances for
determination of the coordination area around an earth station