MOD	EUR/13A27/18

TABLE  8c

Parameters required for the determination of coordination distance for a receiving earth station

| Receiving space radiocommunication service designation | ... | Broadcasting-satellite | Broadcasting-satellite | ... |
| --- | --- | --- | --- | --- |
| Frequency bands (GHz) |  | 11.7-12.5 13 | 12.2-12.7 14 |  |
| Transmitting terrestrial service designations |  | Fixed, broadcasting, mobile | Fixed, broadcasting, mobile |  |
| Method to be used |  | § 1.4.5 | § 1.4.5 |  |
| Modulation at earth station 1 |  | N | A | N |  |
| Earth station interference parameters and criteria | p0 (%) |  | 0.003 | 0.03 | 0.003 |  |
|  | n |  | 1 | 1 | 1 |  |
|  | p (%) |  | 0.003 | 0.03 | 0.003 |  |
|  | NL (dB) |  | 1 | 1 | 1 |  |
|  | Ms (dB) |  | 4 | 7 | 4 |  |
|  | W (dB) |  | 0 | 4 | 0 |  |
| Terrestrial station parameters | E (dBW) in B 2 | A |  | 55 | 55 | 55 |  |
|  |  | N |  | 42 | 42 | 42 |  |
|  | Pt (dBW) in B | A |  | 10 | 10 | 10 |  |
|  |  | N |  | –3 | –3 | –3 |  |
|  | Gx (dBi) |  | 45 | 45 | 45 |  |
| Reference band- width 6 | B (Hz) |  | 27  106 | 24  106 | 24  106 |  |
| Permissible interference power | Pr( p) (dBW) in B |  | –131 | –131 | –131 |  |

Notes to Table 8c: