MOD	EUR/13A27/4

# 6	Limits to the change in the power flux-density of assignments in the Regions 1 and 3 Plan or List to protect the fixed-satellite service (space-to-Earth) in the band 11.7-12.2 GHz in Region 2 or in the band 12.2-12.5 GHz in Region 3, and of assignments in the Region 2 Plan to protect the fixed-satellite service (space-to-Earth) in the band 12.5-12.7 GHz in Region 1 and in the band 12.2-12.7 GHz in Region 3

With respect to § 4.1.1 e) of Article 4, an administration is considered as being affected if the proposed new or modified assignment in the Regions 1 and 3 List would result in an increase in the power flux-density over any portion of the service area of its overlapping frequency assignments in the fixed-satellite service in Region 2 or Region 3 of 0.25 dB or more above that resulting from the frequency assignments in the Plan or List for Regions 1 and 3 as established by WRC-2000.

With respect to § 4.2.3 e), an administration is considered as being affected if the proposed modification to the Region 2 Plan would result in an increase in the power flux-density over any portion of the service area of its overlapping frequency assignments in the fixed-satellite service in Region 1 or Region 3 of 0.25 dB or more above that resulting from the frequency assignments in the Region 2 Plan at the time of entry into force of the Final Acts of the 1985 Conference.

With respect to § 4.1.1 e) or 4.2.3 e) of Article 4, an administration is considered as not being affected if the proposed new or modified assignment in the Regions 1 and 3 List, or if the proposed new frequency assignment in the Region 2 Plan, gives a power flux-density anywhere over any portion of the service area of its overlapping frequency assignments in the fixed-satellite service in Region 1, 2 or 3 of less than:

–186.5    dB(W/(m2 ( 40 kHz)) 	for  0°	(  < 0.054°

–164.0 + 17.74 log     dB(W/(m2 ( 40 kHz))	for  0.054°	(  < 2.0°

–165.0 + 1.66 2 dB(W/(m2 ( 40 kHz))	for  2.0°	(  < 3.59°

–157.5 + 25 log dB(W/(m2 ( 40 kHz))	for  3.59°	(  < 10.57°

–131.9 dB(W/(m2 ( 40 kHz))	for  10.57°	( 

where  is the minimum geocentric orbital separation between the wanted and interfering space stations taking into account the respective East-West station-keeping accuracies.

Reasons:	Europe considers that 60 cm should be taken as the minimum diameter to be protected in order to ensure a more efficient use of the spectrum/orbit resources and facilitate access to these resources by future users. Therefore, it is proposed to adopt the pfd mask given in Section 3.2.2.3 a) of the CPM Report. As the FSS also uses narrow-band transmissions the pfd is expressed in units of dB(W/(m2/40 kHz)).

# Footnotes

21 	In place of these values, the values given in the Annex to Resolution 540 (WRC-2000) shall be applied by administrations and the Bureau until this section is revised by a subsequent conference.