MOD	EUR/13A27/5

# 7	Limits to the change in equivalent noise temperature to protect the fixed-satellite service (Earth-to-space) in Region 1 from modifications to the Region 2 Plan in the band 12.5-12.7 GHz

With respect to § 4.2.3 e) of Article 4, an administration of Region 1 is considered as being affected if the proposed modification to the Region 2 Plan would result in:

–	the value of T / T resulting from the proposed modification is greater than the value of T / T resulting from the assignment in the Region 2 Plan as of the date of entry into force of the Final Acts of the 1985 Conference; and

–	the value of T / T resulting from the proposed modification exceeds 6%,

using the method of Appendix 8 (Case II).

Reasons:	ITU-R studies have concluded that the current (T/T limit of 4% to protect FSS receive space stations in Region 1 against BSS Plan modifications in Region 2 could be relaxed to 6%.