MOD	EUR/13A27/7

ANNEX  4     (WRC-03)

Need for coordination of a transmitting space station in the fixed-satellite service or in the broadcasting-satellite service where this service is not
subject to a Plan: in Region 2 (11.7-12.2 GHz) with respect to the
Plan, the List or proposed new or modified assignments in the List for Regions 1 and 3, in Region 1 (12.5-12.7 GHz) and in
Region 3 (12.2-12.7 GHz) with respect to the Plan or proposed modifications to the Plan for Region 2, in Region 3 (12.2-12.5 GHz) with respect to the Plan, the List or proposed new or modified assignments in the List for Region 1

(See Article 7)

With respect to § 7.1 and 7.2 of Article 7, coordination of a transmitting space station in the fixed-satellite service or in the broadcasting-satellite service not subject to a Plan is required when, under assumed free-space propagation conditions, the power flux-density over any portion of the service area of the overlapping frequency assignments in the broadcasting-satellite service of an administration exceeds the value derived from the expressions given below:

–147	dB(W/(m2 ( 27 MHz))	for  0° 	(  < 0.23°

–135.7 + 17.74 log  	dB(W/(m2 ( 27 MHz))	for  0.23°	(  < 2.0°

–136.7 + 1.66 2	dB(W/(m2 ( 27 MHz))	for  2.0° 	(  < 3.59°

–129.2 + 25 log 	dB(W/(m2 ( 27 MHz))	for  3.59° 	(  < 10.57°

–103.6	dB(W/(m2 ( 27 MHz))	for  10.57°	( 

where  is the minimum geocentric orbital separation between the wanted and interfering space stations taking into account the respective East-West station-keeping accuracies.Reasons:	Europe considers that 60 cm should be taken as the minimum diameter to be protected in order to ensure a more efficient use of the spectrum/orbit resources and facilitate access to these resources by future users. Therefore, it is proposed to adopt the pfd mask given in Section 3.2.2.3 a) of the CPM Report.

ANNEX  639

Criteria for sharing between services

# Footnotes

39 	Sections 1 and 2 of Part A of this Annex are applicable when the services of Regions 1 or 3 are involved. Section 3 of Part A is applicable to all Regions.