MOD	EUR/13A37/15

5 830-7 550 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 5 830-5 850 FIXED-SATELLITE (Earth-to-space) ADD 5.484A RADIOLOCATION Amateur Amateur-satellite (space-to-Earth) | 5 830-5 850 RADIOLOCATION Amateur Amateur-satellite (space-to-Earth) |
| 5.150 5.451 5.453 5.455 5.456 | 5.150 5.453 5.455 |
| 5 850-5 925 FIXED FIXED-SATELLITE (Earth-to-space) ADD 5.484A MOBILE | 5 850-5 925 FIXED FIXED-SATELLITE (Earth-to-space) ADD 5.484A MOBILE Amateur Radiolocation | 5 850-5 925 FIXED FIXED-SATELLITE (Earth-to-space) ADD 5.484A MOBILE Radiolocation |
| 5.150 | 5.150 | 5.150 |
| 5 925-6 700 FIXED FIXED-SATELLITE (Earth-to-space) ADD 5.484A MOBILE 5.149 5.440 5.458 |
| 6 700-7 075 FIXED FIXED-SATELLITE (Earth-to-space) ADD 5.484A (space-to-Earth) 5.441 MOBILE 5.458 5.458A 5.458B 5.458C |

Reasons:	Consequential to the modification of No. 5.484A.

ARTICLE  22

Space services1