ADD	EUR/13A37/18

TABLE  22-1E

Limits to the epfd( radiated by non geostationary-satellite systems in
the fixed-satellite service in certain frequency bands12bis

| Frequency band (GHz) | epfd( (dB(W/m2)) | Percentage of time during which epfd( may not be exceeded | Reference bandwidth (kHz) | Reference antenna diameter and reference radiation pattern |
| --- | --- | --- | --- | --- |
| 3 400-4 200 | –194.7 | 100 | 4 | 1.8 m13ter |
|  | –197.2 | 100 | 4 | 2.4 m13ter |
|  | –200.9 | 100 | 4 | 3.7 m13ter |
|  | –202.6 | 100 | 4 | 4.5 m13ter |
|  | –203.8 | 100 | 4 | 5.5 m13ter |
|  | –206.8 | 100 | 4 | 8 m13ter |
|  | –207.8 | 100 | 4 | 10 m13ter |
|  | –211.3 | 100 | 4 | 15 m13ter |

_______________

13ter	The associated reference radiation pattern is defined as follows:

a)	for values of     100:

G(φ)  =  Gmax  –  2.5 × 10–3  	for	0	≤  φ  <  φm

G(φ)  =  G1		for	φm	≤  φ  <  φr

G(φ)  =  29  –  25 log φ	for	φr	≤  φ  <  20°

G(φ)  =  –3.5	for	20°	≤  φ  <  26.3°

G(φ)  =  32  –  25 log φ	for	26.3°	≤  φ  <  48°

G(φ)  =  –10	for	48°	≤  φ  ≤  180°

where:

D:	antenna diameter; (: wavelength } expressed in the same unit

φ:	off-axis angle of the antenna (degrees)

G1:	gain of the first side lobe    2    15 log

φm    	degrees

φr    15.85 	degrees

Gmax  =  7.7 + 20 log

b)	for values of 42   < 100:

G(φ)  =  Gmax  –  2.5 × 10–3  	for	0	≤  φ  <  φm

G(φ)  =  G1		for	φm	≤  φ  <  100

G(φ)  =  29  –  25 log φ	for	100 	≤  φ  <  20°

G(φ)  =  –3.5	for	20°	≤  φ  <  26.3°

G(φ)  =  32  –  25 log φ	for	26.3°	≤  φ  <  48°

G(φ)  =  –10	for	48°	≤  φ  ≤  180°

c)	for values of      42:

G(φ)  =  Gmax  –  2.5 × 10–3  	for	0	≤  φ  <  φm

G(φ)  =  G1		for	φm	≤  φ  <  100

G(φ)  =  32  –  25 log φ	for	100  	≤  φ  <  48°

G(φ)  =  –10	for	48°	≤  φ  ≤  180°

Reasons:	To insert the provisional epfd limits in the downlink bands as well as the appropriate reference antenna radiation pattern.