MOD	EUR/13A37/20

TABLE  22-2     (WRC-03)

Limits to the epfd( radiated by non-geostationary-satellite systems in the
fixed-satellite service in certain frequency bands14, 16bis

| Frequency band | epfd( (dB(W/m2)) | Percentage of time epfd( level may not be exceeded | Reference bandwidth (kHz) | Reference antenna beamwidth and reference radiation pattern15 |
| --- | --- | --- | --- | --- |
| 5 725-5 850 MHz (Region 1) 5 850-6 725 MHz | –182.3 | 100 | 4 | 1.5° Recommendation ITU-R S.672-4, Ls  –20 |
| 12.50-12.75 GHz 12.75-13.25 GHz 13.75-14.5 GHz | –160 | 100 | 40 | 4° Recommendation ITU-R S.672-4, Ls  –20 |
| 17.3-18.1 GHz (Regions 1 and 3) 17.8-18.1 GHz (Region 2) 16 | –160 | 100 | 40 | 4° Recommendation ITU-R S.672-4, Ls  –20 |
| 27.5-28.6 GHz | –162 | 100 | 40 | 1.55° Recommendation ITU-R S.672-4, Ls  –10 |
| 29.5-30 GHz | –162 | 100 | 40 | 1.55° Recommendation ITU-R S.672-4, Ls  –10 |

Reasons:	To insert the provisional epfd limits in the uplink bands.