ADD	EUR/13A6/2

5.XX	Use of the 5 150-5 250 MHz band by the mobile service is for the implementation of wireless access systems, including RLANs. Stations in the mobile service shall be operated in accordance with the conditions below:

–	in the band 5 150-5 250 MHz, the use of stations shall be restricted to indoor use with a maximum mean e.i.r.p. of 200 mW (averaged over the transmission burst at the highest power setting), with a mean e.i.r.p. density not exceeding 0.04 mW/4 kHz in any 4 kHz bandwidth.