MOD	UGA/63/8

Uganda, in recognizing the importance of services such as the observation of significant tropical biomass, desert moisture, the assessment of forest cover and degradation, supports frequency allocation to the Earth exploration-satellite service (active) in the band 420-470 MHz under the footnote in RR Article 5, taking into account Recommendation ITU-R SA.1260.

Reasons:

1)	The amateur services, which operate in the band 430-440 MHz, play an important role in the provision of disaster communications, particularly in developing countries to which group Uganda belongs. Studies have shown that synthetic aperture radars (SARs) in the EESS and amateur services can co-exist as long as the technical and operational constraints given in Recommendation ITU-R SA.1260 are met by the EESS (active).

2)	Some studies have shown that the co-existence of SARs with fixed and mobile service, radiolocation services, aeronautical services and radionavigation services in some portions in 420-470 MHz is constrained and for some services, it is not feasible at certain times. However, a portion of this band, which is not constrained, could be availed to the Earth exploration-satellite service (active).