NOC	CHN/86/2

5.271	Additional allocation:  in Azerbaijan, Belarus, China, Estonia, India, Latvia, Lithuania, Kyrgyzstan and Turkmenistan, the band 420-460 MHz is also allocated to the aeronautical radionavigation service (radio altimeters) on a secondary basis.     (WRC-2000)

Reasons:	In the People’s Republic of China, the band 420-460 MHz is allocated to the aeronautical radionavigation service (radio altimeters) on the basis of No. 5.271. There are many aeroplanes using this kind of radio altimeters. We are concerned about a potential harmful interference from EESS (active) to radio altimeters.

The current draft of the CPM Report does not give the result on the compatibility between EESS (active) and aeronautical radionavigation service in the band 420-470 MHz while sharing work.

We have made some research on this issue, the initial results of which show that 6 MHz allocation to EESS (active) within the range of 420-450 MHz will cause harmful interference to radionavigation services, to our radio altimeters in particular.