| INTERNATIONAL TELECOMMUNICATION UNION |  |
| --- | --- |
|  | WRC-03 | WORLD RADIOCOMMUNICATION CONFERENCE | Document 348-E |
|  |  |  | 1 July 2003 |
|  |  |  | Original: English |
| GENEVA, 9 JUNE – 4 JULY 2003 |  |
|  | COMMITTEE 8 |
| fifteenth series of texts submitted by committee 6 to the editorial committee |

Note by the Secretariat: For reasons of economy, this document contains only text and examples of tables to be entirely reproduced in a “blue” document (~93 pages).

APPENDIX  30*  (WRC-03)

Provisions for all services and associated Plans and List** for
the broadcasting-satellite service in the frequency bands
11.7-12.2 GHz (in Region 3), 11.7-12.5 GHz (in Region 1)
             and 12.2-12.7 GHz (in Region 2)     (WRC-03)

(See Articles 9 and 11 of the Radio Regulations)

SUP	COM6/348/1

  - TEXT  FOR  NOTES  IN  THE  REMARKS  COLUMN  OF  THE  PLAN

SUP	COM6/348/2

11.3

Note by the Secretariat: The text, starting from page 489 (Section 11.2) up to page 508, is to be deleted and replaced with the following:

ADD	COM6/348/3

11.2	TEXT  FOR  NOTES  IN  THE  REMARKS  COLUMN  OF  THE  PLAN

1	To be dedicated to the Islamic programme envisaged in WARC SAT-77 documents.

2	Not used.

3	Provisional beam. These assignments have been included in the Plan by WRC-97. These assignments are for exclusive use by Palestine, subject to the Israeli-Palestinian Interim Agreement of 28 September 1995, Resolution 741 of the Council notwithstanding and Resolution 99 (Minneapolis, 1998) of the Plenipotentiary Conference.

4	Assignment intended to ensure coverage of Algeria, Libya, Morocco, Mauritania and Tunisia, with the agreement of the countries concerned. If required, it may be used with the characteristics of the beam TUN15000.

5	This assignment shall be brought into use only when the limits given in Table 1 are not exceeded or with the agreement of the administrations identified in Table 2, whose networks/beams listed in this Table may be affected, with respect to (see also the Note to § 11.2):

a)	assignments in the Region 2 Plan on 12 May 2000; or

b)	assignments in the terrestrial services which are recorded in the Master Register with a favourable finding or received by the Bureau prior to 12 May 2000 for recording in the Master Register and which subsequently receive a favourable finding based on the Plan as it existed on 12 May 2000; or

c)	assignments in the fixed-satellite service which:

–	are recorded in the Master Register prior to 12 May 2000 with a favourable finding; or

–	have been coordinated under the provisions of No. 9.7 (or No. 1060) or § 7.2.1 of Article 7 prior to 12 May 2000; or

–	are in process of coordination under the provisions of No. 9.7 (or No. 1060) or § 7.2.1 of Article 7 prior to 31 July 2000 for which complete Appendix 4 data (or Appendix 3 data, as appropriate) have been received by the Bureau under the relevant provisions of Article 9 (or Article 11, as appropriate):

–	filings received by the Bureau prior to 12 May 2000 at 1700 h (Istanbul time) shall be taken into account in the pertinent compatibility analysis by applying the pfd criteria shown in Table 1; or

–	filings received by the Bureau after 12 May 2000 at 1700 h (Istanbul time), but before 31 July 2000, shall be taken into account by applying the sharing criteria of _138 dB(W/(m2 · 27 MHz)) or the pfd criteria shown in Table 1, whichever is higher.

6	This assignment shall not claim protection from interference caused by the assignments which pertain to networks/beams identified in Table 3 which are in conformity with the Region 2 Plan on 12 May 2000 (see also the Note to § 11.2).

7	This assignment shall not claim protection from interference caused by assignments in the fixed-satellite service which pertain to networks/beams identified in Table 3 (see also the Note to § 11.2); and

a)	either are recorded in the Master Register with a favourable finding prior to 12 May 2000; or

b)	for which complete Appendix 4 data (or Appendix 3 data, as appropriate) under the relevant provisions of Article 9 (or No. 1060, or § 7.2.1 of Article 7, as appropriate) have been received prior to 12 May 2000, which have been brought into use prior to 12 May 2000 and for which the complete due diligence information, in accordance with Annex 2 to Resolution 49 (WRC-97), has been received prior to 12 May 2000.

8	This assignment shall not claim protection from the assignments of administrations for terrestrial services identified in Table 4 which are recorded in the Master Register with a favourable finding, or received by the Bureau prior to 12 May 2000 for recording in the Master Register and which subsequently receive a favourable finding based on the Plan as it existed on 12 May 2000 (see also the Note to § 11.2).

9	Provisional beam. These assignments have been included in the Plan by WRC-2000. These assignments are for exclusive use by East Timor.

TABLE  1

| Symbol | Criteria |
| --- | --- |
| a | § 3 of Annex 1 1 |
| b | § 4 of Annex 1 1 |
| c | § 6 of Annex 1 1 |
| 1 These paragraphs and this Annex are contained in the Radio Regulations as adopted by WRC-03.. |

NOTE – In cases where assignments from the WRC-97 Plan without remarks were included in the WRC-2000 Regions 1 and 3 Plan without change, or with conversion of modulation from analogue to digital, or a change from normal roll-off to fast roll-off antenna characteristics, the coordination status afforded by the WRC-97 Plan shall be preserved.

In cases where assignments from the WRC-97 Plan with remarks were included in the WRC-2000 Regions 1 and 3 Plan without change, or with conversion of modulation from analogue to digital, or a change from normal roll-off to fast roll-off antenna pattern, the compatibility will be reassessed using the revised criteria and methodology of WRC-2000 and the remarks of the WRC-97 Plan assignment will either be maintained or reduced on the basis of the results of this analysis.

In other cases the methodology described in Notes 5 to 8 shall be applied.

TABLE 2

Affected administrations and corresponding networks/beams identified based on Note 5 in Section 11.2 of Article 11 of Appendix 30

| Beam name | Channels | Ref. Table 1 | Affected administrations* | Affected networks/beams/terrestrial stations* |
| --- | --- | --- | --- | --- |
| AFS02100 | 23 | c | F, F/EUT, MLA | MEASAT-SA1, VIDEOSAT-8-KU-C, EUTELSAT 3-4E |
| AGL29500 | 1, 3, 5, 7, 9, 11, 13 | c | USA | INTELSAT7 335.5E, INTELSAT8 335.5E |
| ARM06400 | 26 | c | BLR/IK, CHN, D, F/EUT, G, HOL, J, PAK, TON, UAE, USA | ASIASAT-AKX, ASIASAT-BKX, ASIASAT-CK1, ASIASAT-CKX, ASIASAT-DKX, ASIASAT-EK1, ASIASAT-EKX, EMARSAT-1B, EMARSAT-1F, EMARSAT-1G, EUROPE*STAR-2G-1, EUROPE*STAR-2G-2, EUROPE*STAR-2G-3, EUTELSAT 3-25.5E, EUTELSAT 3-33E, EUTELSAT 3-36E, EUTELSAT 3-44E, EUTELSAT 3-48E, EUTELSAT 3-70.5E, EUTELSAT 3-73.5E, EUTELSAT 3-76E, EUTELSAT 3-80.5E, EUTELSAT 3-83.5E, EUTELSAT 3-86E, EUTELSAT 3-88.5E, INTELSAT KFOS 85E, INTELSAT7 66E, INTERSPUTNIK-27E-Q, N-SAT-102.5E, N-SAT-103.5E, N-SAT-106.5, N-SAT-110E, N-SAT-117, N-SAT-120E, N-SAT-122.5E, N-SAT-65.5, N-SAT-73E, N-SAT-74.5E, N-SAT-76.5E, N-SAT-79.5E, N-SAT-82.5E, N-SAT-84E, N-SAT-86E, N-SAT-94E, NSS-21, NSS-22, NSS-23, NSS-24, NSS-8, NSS-9, PAKSAT-1, PAKSAT-2, PAKSAT-C, PAKSAT-D, SKYSAT-A1, SKYSAT-A2, SKYSAT-B2, SKYSAT-C1, SKYSAT-C2, SKYSAT-C3, SKYSAT-C4, TONGASAT AP-KU-4 |
| ARM06400 | 30, 34, 38 | c | BLR/IK, CHN, D, F/EUT, G, HOL, J, LAO, MLA, PAK, PNG, THA, TON, UAE, USA | APSTAR-3, APSTAR-4, ASIASAT-AKX, ASIASAT-BKX, ASIASAT-CK1, ASIASAT-CKX, ASIASAT-DKX, ASIASAT-EK1, ASIASAT-EKX, EMARSAT-1B, EMARSAT-1F, EMARSAT-1G, EUROPE*STAR-2G-1, EUROPE*STAR-2G-2, EUROPE*STAR-2G-3, EUTELSAT 3-25.5E, EUTELSAT 3-33E, EUTELSAT 3-36E, EUTELSAT 3-44E, EUTELSAT 3-48E, EUTELSAT 3-70.5E, EUTELSAT 3-73.5E, EUTELSAT 3-76E, EUTELSAT 3-80.5E, EUTELSAT 3-83.5E, EUTELSAT 3-86E, EUTELSAT 3-88.5E, INTELSAT KFOS 85E, INTELSAT7 66E, INTERSPUTNIK-27E-Q, L-STAR-1, L-STAR-2, L-STAR-3, L-STAR-5, L-STAR-6, MEASAT-1, MEASAT-3, MEASAT-91.5E, MEASAT-95E, MEASAT-SA3, MEASAT-SA4, N-SAT-102.5E, N-SAT-103.5E, N-SAT-106.5, N-SAT-110, N-SAT-110E, N-SAT-117, N-SAT-120E, N-SAT-122.5E, N-SAT-65.5, N-SAT-73E, N-SAT-74.5E, N-SAT-76.5E, N-SAT-79.5E, N-SAT-82.5E, N-SAT-84E, N-SAT-86E, N-SAT-94E, NSS-21, NSS-22, NSS-23, NSS-24, NSS-8, NSS-9, PACSTAR-L1, PACSTAR-L2, PAKSAT-1, PAKSAT-2, PAKSAT-C, PAKSAT-D, SKYSAT-A1, SKYSAT-A2, SKYSAT-B2, SKYSAT-C1, SKYSAT-C2, SKYSAT-C3, SKYSAT-C4, THAICOM-A2B, THAICOM-A3B, THAICOM-A5B, THAICOM-C1, THAICOM-G1K, TONGASAT AP-KU-4 |
| * Administrations and corresponding networks/beams/terrestrial stations whose assignment(s) may receive interference from the beam shown in the left-hand column. |

TABLE 3

Affecting administrations and corresponding networks/beams identified based on Notes 6 and 7 in Section 11.2 of Article 11 of Appendix 30

| Beam name | Channels | Note | Affecting administrations* | Affecting networks/beams* |
| --- | --- | --- | --- | --- |
| AFG__100 | 1, 3, 5, 7, 9, 11, 13 | 7 | USA | INTELSAT7 342E, INTELSAT7 359E |
| AGL29500 | 1, 3, 5, 7, 9, 11, 13 | 7 | HOL, USA | INTELSAT7 307E, INTELSAT7 310E, INTELSAT7 328.5E, INTELSAT7 338.5E, INTELSAT7 342E, INTELSAT7 359E, INTELSAT8 338.5E, INTELSAT8 328.5E |
| AND34100 | 2, 6, 10, 12 | 7 | HOL, USA | INTELSAT7 307E, INTELSAT7 310E, INTELSAT7 319.5E, INTELSAT7 328.5E, INTELSAT7 342E, INTELSAT7 359E, INTELSAT IBS 319.5E, INTELSAT8 319.5E, USASAT-26A INTELSAT8 328.5E |
| AND34100 | 14, 16, 18, 20 | 7 | USA | USASAT-26A |
| ARM06400 | 26 | 7 | J | JCSAT-3B |
| ARM06400 | 28, 30, 32, 34, 36, 38, 40 | 7 | J, KOR | JCSAT-3B, KOREASAT-2 |
| ARS34000 | 40 | 7 | J, KOR | JCSAT-3A, JCSAT-3B, KOREASAT-2 |
| ARS__100 | 26 | 7 | J | JCSAT-3A, JCSAT-3B |
| ARS__100 | 28, 30, 32, 34, 36, 38, 40 | 7 | J, KOR | JCSAT-3A, JCSAT-3B, KOREASAT-2 |
| AUSA_100 | 1, 5, 9 | 7 | USA | INTELSAT7 174E, INTELSAT7 177E, INTELSAT7 180E |
| AUSB_100 | 4, 8, 12 | 7 | USA | INTELSAT7 174E, INTELSAT7 177E, INTELSAT7 180E, INTELSAT8 174E |
| AZE06400 | 25, 27 | 7 | J | JCSAT-3A, JCSAT-3B |
| AZE06400 | 29, 31, 33, 35, 37, 39 | 7 | J, KOR | JCSAT-3A, JCSAT-3B, KOREASAT-2 |
| BEN23300 | 1, 3, 5, 7, 9, 11, 13 | 7 | HOL, USA | INTELSAT7 307E, INTELSAT7 310E, INTELSAT7 328.5E, INTELSAT7 338.5E, INTELSAT7 342E, INTELSAT7 359E, INTELSAT IBS 342E, INTELSAT8 338.5E, INTELSAT8 328.5E |
| BFA10700 | 22, 24 | 7 | E | HISPASAT-1, HISPASAT-2C3 KU |
| BHR25500 | 25, 27 | 7 | J | JCSAT-3A, JCSAT-3B |
| BHR25500 | 29, 31, 33, 35, 37, 39 | 7 | J, KOR | JCSAT-3A, JCSAT-3B, KOREASAT-2 |
| BIH14800 | 1, 3, 5, 7, 9, 11, 13 | 7 | USA | INTELSAT7 307E, INTELSAT7 310E, INTELSAT7 328.5E, INTELSAT7 342E, INTELSAT7 359E |
| BLR06200 | 1, 3, 5, 7, 9, 11, 13 | 7 | USA | INTELSAT7 310E, INTELSAT7 328.5E, INTELSAT7 342E, INTELSAT7 359E |
| BRM29800 | 1, 3, 5, 7, 9, 11, 13 | 7 | USA | INTELSAT7 174E, INTELSAT7 177E, INTELSAT7 180E |
| BRU33000 | 2, 4, 6, 8, 10 | 7 | USA | INTELSAT7 174E, INTELSAT7 177E, INTELSAT7 180E |
| CBG29900 | 2, 4, 6, 8, 10, 12 | 7 | USA | INTELSAT7 174E, INTELSAT7 177E, INTELSAT7 180E |
| CHN15500 | 1, 3, 5, 7, 9, 11, 13 | 7 | USA | INTELSAT7 174E, INTELSAT7 177E, INTELSAT7 359E |
| CHN15800 | 2, 4, 6, 8, 10, 12 | 7 | USA | INTELSAT7 174E, INTELSAT7 177E, INTELSAT7 180E |
| * Administrations and corresponding networks/beams whose assignment(s) may cause interference to the beam shown in the left-hand column. |

TABLE 4

Affecting administrations and corresponding terrestrial stations identified based on Note 8 in Section 11.2 of Article 11 of Appendix 30

| Beam name | Channels | Affecting administrations* | Affecting terrestrial stations* |
| --- | --- | --- | --- |
| EGY02600 | 2 | ISR | HERZILIYA |
| F 09300 | 24, 26 | SUI | GENEVE STUDIO C VOGT |
| F 09300 | 38, 40 | AUT | EHRWALD |
| I 08200 | 38, 40 | AUT | EHRWALD |
| JOR22400 | 2 | ISR | HERZILIYA, JERUSALEM |
| RUS-4 | 25, 26, 27, 28, 29, 31, 33, 35, 37, 39 | J1 |  |
| * Administrations and corresponding terrestrial stations whose assignment(s) may cause interference to the beam shown in the left-hand column. 1 The identification of this administration is based on its typical terrestrial station assignments as recorded in the Master Register. |

TABLE 5

TABLE  SHOWING  CORRESPONDENCE  BETWEEN  CHANNEL
	NUMBERS  AND  ASSIGNED  FREQUENCIES

| Channel No. | Assigned frequency (MHz) | Channel No. | Assigned frequency (MHz) |
| --- | --- | --- | --- |
| 1 | 11 727.48 | 21 | 12 111.08 |
| 2 | 11 746.66 | 22 | 12 130.26 |
| 3 | 11 765.84 | 23 | 12 149.44 |
| 4 | 11 785.02 | 24 | 12 168.62 |
| 5 | 11 804.20 | 25 | 12 187.80 |
| 6 | 11 823.38 | 26 | 12 206.98 |
| 7 | 11 842.56 | 27 | 12 226.16 |
| 8 | 11 861.74 | 28 | 12 245.34 |
| 9 | 11 880.92 | 29 | 12 264.52 |
| 10 | 11 900.10 | 30 | 12 283.70 |
| 11 | 11 919.28 | 31 | 12 302.88 |
| 12 | 11 938.46 | 32 | 12 322.06 |
| 13 | 11 957.64 | 33 | 12 341.24 |
| 14 | 11 976.82 | 34 | 12 360.42 |
| 15 | 11 996.00 | 35 | 12 379.60 |
| 16 | 12 015.18 | 36 | 12 398.78 |
| 17 | 12 034.36 | 37 | 12 417.96 |
| 18 | 12 053.54 | 38 | 12 437.14 |
| 19 | 12 072.72 | 39 | 12 456.32 |
| 20 | 12 091.90 | 40 | 12 475.50 |
| Note – Assigned frequency = 11 708.30 + 19.18 n, where n is the channel number. |

TABLE 6a

Basic characteristics of the Regions 1 and 3 Plan (sorted by administration)

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Admin. symbol | Beam identification | Orbital position | Boresight | Space station antenna characteristics | Space station antenna code | Shaped beam | Space station antenna gain | Earth station antenna | Polarization | e.i.r.p. | Designation of emission | Identity of the space station | Group code | Sta- tus | Remarks |
|  |  |  | Long. | Lat. | Major axis | Minor axis | Orien- tation |  |  | Co-polar | Cross- polar | Code | Gain | Type | Angle |  |  |  |  |  |  |
| AFG | AFG__100 | 50.00 | 65.88 | 33.86 |  |  |  | CB_TSS_AFGA |  | 42.71 |  | MODRES | 35.50 | CL |  | 58.4 | 27M0G7W |  |  | P | 7 |
| AFS | AFS02100 | 4.80 | 24.50 | -28.00 | 3.13 | 1.68 | 27.00 | R13TSS |  | 37.24 |  | MODRES | 35.50 | CL |  | 59.1 | 27M0G7W |  |  | P | 5 |
| AGL | AGL29500 | -24.80 | 16.06 | -12.45 | 2.42 | 1.88 | 77.88 | R13TSS |  | 37.87 |  | MODRES | 35.50 | CL |  | 59.1 | 27M0G7W |  |  | P | 5, 7 |
| ALB | ALB29600 | 62.00 | 20.04 | 41.23 | 0.60 | 0.60 | 61.32 | R13TSS |  | 48.88 |  | MODRES | 35.50 | CL |  | 58.9 | 27M0G7W |  |  | P |  |
| ALG | ALG__100 | -24.80 | 1.86 | 27.60 |  |  |  | CB_TSS_ALGA |  | 39.59 |  | MODRES | 35.50 | CL |  | 54.5 | 27M0G7W |  |  | P |  |
| AND | AND34100 | -37.00 | 1.60 | 42.50 | 0.60 | 0.60 | 0.00 | R13TSS |  | 48.88 |  | MODRES | 35.50 | CL |  | 56.5 | 27M0G7W |  |  | P | 7 |
| ARM | ARM06400 | 22.80 | 44.99 | 39.95 | 0.73 | 0.60 | 148.17 | R13TSS |  | 48.02 |  | MODRES | 35.50 | CR |  | 58.9 | 27M0G7W |  |  | P | 5, 7 |
| ARS | ARS__100 | 17.00 | 44.72 | 23.76 |  |  |  | CB_TSS_ARSA |  | 37.81 |  | MODRES | 35.50 | CL |  | 57.7 | 27M0G7W |  | 54 | P | 5, 7 |
| ARS | ARS34000 | 17.00 | 52.30 | 24.80 | 2.68 | 0.70 | 143.00 | R13TSS |  | 41.71 |  | MODRES | 35.50 | CL |  | 59.2 | 27M0G7W |  | 54 | P | 5, 7 |
| AUS | AUS00400 | 152.00 | 123.00 | -24.20 | 3.06 | 2.17 | 102.00 | R13TSS |  | 36.22 |  | MODRES | 35.50 | CR |  | 58.2 | 27M0G7W |  | 30 | P |  |
| AUS | AUS0040A | 152.00 | 96.83 | -12.19 | 0.60 | 0.60 | 0.00 | R13TSS |  | 48.88 |  | MODRES | 35.50 | CR |  | 58.9 | 27M0G7W |  | 30 | P |  |
| AUS | AUS0040B | 152.00 | 105.69 | -10.45 | 0.60 | 0.60 | 0.00 | R13TSS |  | 48.88 |  | MODRES | 35.50 | CR |  | 58.9 | 27M0G7W |  | 30 | P |  |
| AUS | AUS0040C | 152.00 | 110.52 | -66.28 | 0.60 | 0.60 | 0.00 | R13TSS |  | 48.88 |  | MODRES | 35.50 | CR |  | 58.9 | 27M0G7W |  | 30 | P |  |
| AUS | AUS00500 | 152.00 | 133.90 | -18.40 | 2.82 | 1.74 | 105.00 | R13TSS |  | 37.53 |  | MODRES | 35.50 | CL |  | 59.4 | 27M0G7W |  |  | P |  |
| AUS | AUS00600 | 152.00 | 136.60 | -30.90 | 2.41 | 1.52 | 161.00 | R13TSS |  | 38.80 |  | MODRES | 35.50 | CL |  | 58.4 | 27M0G7W |  |  | P |  |
| AUS | AUS00700 | 164.00 | 145.20 | -38.10 | 2.12 | 1.02 | 147.00 | R13TSS |  | 41.09 |  | MODRES | 35.50 | CR |  | 58.5 | 27M0G7W |  | 31 | P |  |
| AUS | AUS0070A | 164.00 | 158.94 | -54.50 | 0.60 | 0.60 | 0.00 | R13TSS |  | 48.88 |  | MODRES | 35.50 | CR |  | 58.9 | 27M0G7W |  | 31 | P |  |
| AUS | AUS00800 | 164.00 | 145.90 | -21.70 | 3.62 | 1.63 | 136.00 | R13TSS |  | 36.73 |  | MODRES | 35.50 | CL |  | 58.8 | 27M0G7W |  |  | P |  |
| AUS | AUS00900 | 164.00 | 147.50 | -32.10 | 2.31 | 1.43 | 187.00 | R13TSS |  | 39.25 |  | MODRES | 35.50 | CR |  | 59.3 | 27M0G7W |  | 32 | P |  |
| AUS | AUS0090A | 164.00 | 159.06 | -31.52 | 0.60 | 0.60 | 0.00 | R13TSS |  | 48.88 |  | MODRES | 35.50 | CR |  | 58.9 | 27M0G7W |  | 32 | P |  |
| AUS | AUS0090B | 164.00 | 167.93 | -29.02 | 0.60 | 0.60 | 0.00 | R13TSS |  | 48.88 |  | MODRES | 35.50 | CR |  | 58.9 | 27M0G7W |  | 32 | P |  |
| AUS | AUSA_100 | 152.00 | 132.38 | -38.37 |  |  |  | CB_TSS_AUSA |  | 48.88 |  | MODRES | 35.50 | CR |  | 58.9 | 27M0G7W |  |  | P | 5, 7 |
| AUS | AUSB_100 | 164.00 | 132.38 | -38.37 |  |  |  | CB_TSS_AUSB |  | 48.88 |  | MODRES | 35.50 | CL |  | 58.9 | 27M0G7W |  |  | P | 7 |
| AUT | AUT01600 | -18.80 | 10.31 | 49.47 | 1.82 | 0.92 | 151.78 | MOD13FRTSS |  | 42.19 |  | MODRES | 35.50 | CR |  | 59.1 | 27M0G7W |  |  | P |  |

COLUMN  HEADINGS  OF  THE  PLAN

Col. 1	Nominal orbital position, in degrees and hundredths of a degree from the Greenwich meridian (negative values indicate longitudes which are west of the Greenwich meridian; positive values indicate longitudes which are east of the Greenwich meridian).

Col. 2	Notifying administration symbol.

Col. 3	Beam identification (Column 2, normally, contains the symbol designating the administration or the geographical area taken from Table B1 of the Preface to the International Frequency List, followed by the symbol designating the service area).

Col. 4	Polarization (CL – circular left, CR – circular right).

Col. 5	Channel number/Indication of minimum equivalent protection margin (EPM) for a given assignment derived from the set of values for all test points belonging to the given beam (dB).

Table 6B

Minimum equivalent protection margin of assignments in the Regions 1 and 3 Plan (sorted by orbital position)

| 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Orbital position | Admin. symbol | Beam Identifica- tion | Polar- ization type | Channel number |
|  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 |
|  |  |  |  | Minimum EPM |
| -178.00 | FJI | FJI19300 | CR | 6.1 |  | 6.1 |  | 6.1 |  | 6.1 |  | 6.1 |  | 6.1 |  | 6.1 |  | 6.1 |  | 6.1 |  | 6.1 |  | 6.1 |  | 6.1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -178.00 | SMO | SMO05700 | CR | 1.6 |  | 1.6 |  | 1.6 |  | 1.6 |  | 1.6 |  | 1.6 |  | 1.6 |  | 1.6 |  | 1.6 |  | 1.6 |  | 1.6 |  | 1.6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -160.00 | F | OCE10100 | CL |  | 99.9 |  | 99.9 |  | 99.9 |  | 99.9 |  | 99.9 |  | 99.9 |  | 99.9 |  | 99.9 |  | 99.9 |  | 99.9 |  | 99.9 |  | 99.9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.20 | GMB | GMB30200 | CL | 4.6 |  | 1.9 |  | 1.9 |  | 1.9 |  | 1.9 |  | 1.9 |  | 1.9 |  | 1.9 |  | 1.9 |  | 1.9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.20 | IRL | IRL21100 | CL | 2.6 |  | 0.6 |  | 0.6 |  | 0.6 |  | 0.6 |  | 0.6 |  | 0.6 |  | 0.6 |  | 0.6 |  | 0.6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.20 | NGR | NGR11500 | CL |  | 6.8 |  | 6.8 |  | 6.8 |  | 6.8 |  | 6.8 |  | 6.8 |  | 6.8 |  | 6.8 |  | 6.8 |  | 6.9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.00 | AND | AND34100 | CL |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.00 | GUI | GUI19200 | CR |  | 0.9 |  | 0.9 |  | 0.9 |  | 0.9 |  | 0.9 |  | 0.9 |  | 0.9 |  | 0.9 |  | 0.9 |  | 1.5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.00 | POR | POR__100 | CR | 2.4 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.00 | SEN | SEN22200 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -0.3 |  | 4.7 |  | 4.7 |  | 4.7 |  | 4.7 |  | 4.7 |  | 4.7 |  | 4.7 |  | 4.7 |  | 4.7 |  |
| -36.80 | MTN | MTN__100 | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 1.1 |  | 3.9 |
| -36.80 | SMR | SMR31100 | CR | 4.4 |  | 3.2 |  | 3.2 |  | 3.1 |  | 3.1 |  | 3.1 |  | 3.2 |  | 3.2 |  | 3.2 |  | 3.2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | CPV | CPV30100 | CL |  | 9.5 |  | 9.5 |  | 9.5 |  | 9.5 |  | 9.5 |  | 9.5 |  | 9.5 |  | 9.5 |  | 9.5 |  | 8.8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | DNK | DNK090XR | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.9 |  |  |  | 0.9 |  |  |  |  |  |  |  |
| -33.50 | DNK | DNK091XR | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -0.9 |  |  |  | -0.9 |  |  |  |  |  |
| -33.50 | G | G 02700 | CR |  | -0.1 |  | 0.1 |  | -0.1 |  | -0.1 |  | -0.1 |  | -0.1 |  | 0.2 |  | -0.1 |  | 0.1 |  | 0.3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | ISL | ISL04900 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8.8 |  | 7.2 |  | 7.2 |  | 10.1 |  | 14.8 |  | 3.6 |  | 14.8 |  | 3.6 |  | 21.7 |  | 21.7 |  |
| -33.50 | ISL | ISL05000 | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.1 |  | 0.1 |  | 0.1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | LBR | LBR24400 | CR | 3.3 |  | 0.4 |  | 0.4 |  | 0.4 |  | 0.4 |  | 0.4 |  | 0.4 |  | 0.4 |  | 0.4 |  | 0.4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | SRL | SRL25900 | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -0.4 |  | 1.0 |  | 1.0 |  | 1.0 |  | 1.0 |  | 0.9 |  | 1.0 |  | 0.9 |  | 1.0 |  | 1.0 |  |
| -30.00 | BFA | BFA10700 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.5 |  | 1.5 |  | 1.5 |  | 1.5 |  | 1.5 |  | 1.5 |  | 1.5 |  | 1.5 |  | 1.5 |  | 2.4 |
| -30.00 | E | E____100 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8.3 |  | 5.9 |  | 5.9 |  | 5.9 |  | 5.9 |  | 5.9 |  | 5.6 |  | 5.9 |  | 5.6 |  | 5.9 |  |
| -30.00 | E | HISP33D1 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -0.4 |  |  |  | -0.4 |  |  |  | -0.4 |  |  |  | -0.4 |  |  |  | -0.4 |  |
| -30.00 | E | HISP33D2 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | -1.0 |  |  |  | -1.0 |  |  |  | -1.0 |  |  |  | -1.0 |  |  |  | -1.0 |  |
| -30.00 | E | HISPA27D | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.3 |  |  |  | 1.3 |  |  |  | 1.3 |  |  |  | 1.3 |  |  |  | 1.3 |  |
| -30.00 | E | HISPASA4 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.3 |  |  |  | 1.3 |  |  |  | 1.3 |  |  |  | 1.3 |  |  |  | 1.3 |  |

APPENDIX  30A*  (Rev.WRC-03)

Provisions and associated Plans and List1 for feeder links for the broadcasting-satellite service (11.7-12.5 GHz in Region 1, 12.2-12.7 GHz 
in Region 2 and 11.7-12.2 GHz in Region 3) in the frequency bands 
14.5-14.8 GHz2 and 17.3-18.1 GHz in Regions 1 and 3,
           and 17.3-17.8 GHz in Region 2     (WRC-03)

(See Articles 9 and 11 of the Radio Regulations)     (WRC-03)

ARTICLE  9A     (WRC-03)

Plan for feeder links for the broadcasting-satellite service in the
fixed-satellite service in the frequency bands 14.5-14.8 GHz
and 17.3-18.1 GHz in Regions 1 and 3

SUP	COM6/348/4

9A.2	TEXT  FOR  NOTES  IN  THE  REMARKS  COLUMN  OF  THE
	REGIONS  1  AND  3  FEEDER-LINK  PLAN

SUP	COM6/348/5

9A.3

Note by the Secretariat: The text, starting from page 625 (Section 9A.2) up to page 648, is to be deleted and replaced with the following:

ADD	COM6/348/6

9A.2	TEXT  FOR  NOTES  IN  THE  REMARKS  COLUMN  OF  THE
	REGIONS  1  AND  3  FEEDER-LINK  PLAN

1	(Not used.)

2	(Not used.)

3	(Not used.)

4	(Not used.)

5	This assignment shall be brought into use only when the limits given in § 5 of Annex 1 are not exceeded, or with the agreement of administrations identified in Table 1A, whose networks/beams listed in this Table may be affected with respect to assignments which are in conformity with the Region 2 feeder-link Plan on 12 May 2000 (see also Note to § 9A.2).

6	This assignment shall not claim protection from interference caused by the assignments which pertain to networks/beams identified in Table 1B which are in conformity with the Region 2 feeder-link Plan on 12 May 2000 (see also Note to § 9A.2).

7	This assignment shall not claim protection from interference caused by the assignments which pertain to networks/beams identified in Table 1B which are recorded in the Master Register with a favourable finding prior to 12 May 2000 (see also Note to § 9A.2).

The methodology and criteria for this analysis shall be those contained in § 1 of Annex 4, modified to take into consideration the system noise temperature of the received space station to be 600 K and to apply a (T/T criterion of 6%.

8	Provisional beam. These assignments have been included in the Regions 1 and 3 feeder-link Plan by WRC-97. These assignments are for exclusive use by Palestine, subject to the Israeli-Palestinian Interim Agreement of 28 September 1995, Resolution 741 of the Council notwithstanding and Resolution 99 (Minneapolis, 1998) of the Plenipotentiary Conference.

9	(Not used.)

10	Provisional beam. These assignments have been included in the Regions 1 and 3 feeder-link Plan by WRC-2000. These assignments are for exclusive use by East Timor.

NOTE – In cases where assignments from the WRC-97 Plans without Remarks were included in the WRC-2000 Regions 1 and 3 feeder-link Plan without change, or with conversion of modulation from analogue to digital, or a change from normal roll-off to fast roll-off antenna characteristics, the coordination status afforded by the WRC-97 Plans shall be preserved.

In cases where assignments from the WRC-97 Plans with Remarks were included in the WRC-2000 Regions 1 and 3 feeder-link Plan without change, or with conversion of modulation from analogue to digital, or a change from normal roll-off to fast roll-off antenna pattern, the compatibility will be reassessed using the revised criteria and methodology of WRC-2000 and the Remarks of the WRC-97 Plans assignment will either be maintained or reduced on the basis of the results of this analysis.

In other cases, the methodology described in Notes 5 to 7 shall be applied.

TABLE 1A

Affected administrations and corresponding networks/beams identified based on Note 5 in Section 9A.2 of Article 9A of Appendix 30A

| Beam name | Channels | Affected administrations* | Affected networks/beams* |
| --- | --- | --- | --- |
| CPV30100 | 2, 4, 8, 10, 12 | GUY JMC | GUY00302, JMC00005 |
| CPV30100 | 6 | JMC | JMC00005 |
| G 02700 | 2, 4, 8, 10, 12 | GUY JMC | GUY00302, JMC00005 |
| G 02700 | 6 | JMC | JMC00005 |
| LBR24400 | 1 | GUY | GUY00302 |
| LBR24400 | 3, 9, 13 | JMC | JMC00005 |
| LBR24400 | 5, 7, 11 | GUY JMC | GUY00302, JMC00005 |
| * Administrations and corresponding networks/beams whose assignment(s) may receive interference from the beam shown in the left-hand column. |

TABLE 1B

Affecting administrations and corresponding networks/beams identified based on Notes 6 and 7 in Section 9A.2 of Article 9A of Appendix 30A

| Beam name | Channels | Note | Affecting administrations* | Affecting networks/beams* |
| --- | --- | --- | --- | --- |
| CPV30100 | 2, 4, 8, 10, 12 | 6 | GUY JMC | GUY00302, JMC00005 |
| CPV30100 | 6 | 6 | JMC | JMC00005 |
| E__100 | 1, 3, 5, 7, 9, 11, 13 | 6 | G | BERBER02 |
| G 02700 | 2, 4, 8, 10, 12 | 6 | GUY JMC | GUY00302, JMC00005 |
| G 02700 | 6 | 6 | JMC | JMC00005 |
| LBR24400 | 1 | 6 | GUY | GUY00302 |
| LBR24400 | 3, 9, 13 | 6 | JMC | JMC00005 |
| LBR24400 | 5, 7, 11 | 6 | GUY JMC | GUY00302, JMC00005 |
| NZL__100 | 24 | 7 | J | SUPERBIRD-A |
| * Administrations and corresponding networks/beams whose assignment(s) may cause interference to the beam shown in the left-hand column. |

TABLE  2A

Table showing correspondence between channel numbers and assigned frequencies1
for the feeder links in the frequency band 14.5-14.8 GHz

| Channel No. | Assigned feeder-link frequency (MHz) |
| --- | --- |
| 1 | 14 525.30 |
| 2 | 14 544.48 |
| 3 | 14 563.66 |
| 4 | 14 582.84 |
| 5 | 14 602.02 |
| 6 | 14 621.20 |
| 7 | 14 640.38 |
| 8 | 14 659.56 |
| 9 | 14 678.74 |
| 10 | 14 697.92 |
| 11 | 14 717.10 |
| 12 | 14 736.28 |
| 13 | 14 755.46 |
| 14 | 14 774.64 |
| 1 Assigned frequency = 14 506.12 + 19.18 n, where n is the channel number. |

TABLE  2B

Table showing correspondence between channel numbers and assigned frequencies1
for the feeder links in the frequency band 17.3-18.1 GHz

| Channel No. | Assigned feeder-link frequency (MHz) | Channel No. | Assigned feeder-link frequency (MHz) |
| --- | --- | --- | --- |
| 1 | 17 327.48 | 21 | 17 711.08 |
| 2 | 17 346.66 | 22 | 17 730.26 |
| 3 | 17 365.84 | 23 | 17 749.44 |
| 4 | 17 385.02 | 24 | 17 768.62 |
| 5 | 17 404.20 | 25 | 17 787.80 |
| 6 | 17 423.38 | 26 | 17 806.98 |
| 7 | 17 442.56 | 27 | 17 826.16 |
| 8 | 17 461.74 | 28 | 17 845.34 |
| 9 | 17 480.92 | 29 | 17 864.52 |
| 10 | 17 500.10 | 30 | 17 883.70 |
| 11 | 17 519.28 | 31 | 17 902.88 |
| 12 | 17 538.46 | 32 | 17 922.06 |
| 13 | 17 557.64 | 33 | 17 941.24 |
| 14 | 17 576.82 | 34 | 17 960.42 |
| 15 | 17 596.00 | 35 | 17 979.60 |
| 16 | 17 615.18 | 36 | 17 998.78 |
| 17 | 17 634.36 | 37 | 18 017.96 |
| 18 | 17 653.54 | 38 | 18 037.14 |
| 19 | 17 672.72 | 39 | 18 056.32 |
| 20 | 17 691.90 | 40 | 18 075.50 |
| 1 Assigned frequency = 17 308.3 + 19.18 n, where n is the channel number. |

Table 3A1

Basic characteristics of the Regions 1 and 3 feeder-link Plan in the frequency band 14.5-14.8 GHz (sorted by administration)

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Admin. symbol | Beam identifi- cation | Orbital position | Boresight | Space station antenna characteristics | Space station antenna code | Shaped beam | Space station antenna gain | Earth station antenna | Polarization | e.i.r.p. | Power control | Designation of emission | Identity of the space station | Group code | Sta- tus | Remarks |
|  |  |  | Long. | Lat. | Major axis | Minor axis | Orien- tation |  |  | Co-polar | Cross-polar | Code | Gain | Type | Angle |  |  |  |  |  |  |  |
| AFS | AFS02101 | 4.80 | 24.50 | -28.00 | 3.13 | 1.68 | 27.00 | MODRSS |  | 37.24 |  | MODTES | 57.00 | CL |  | 82.0 |  | 27M0G7W |  | 4L | P |  |
| AFS | AFS02102 | 4.80 | 24.50 | -28.00 | 3.13 | 1.68 | 27.00 | MODRSS |  | 37.24 |  | MODTES | 57.00 | CR |  | 82.0 |  | 27M0G7W |  | 4L | P |  |
| CHN | CHN19001 | 122.00 | 114.17 | 23.32 | 0.91 | 0.60 | 2.88 | MODRSS |  | 47.08 |  | MODTES | 57.00 | CL |  | 84.0 |  | 27M0G7W |  | 4C | P |  |
| CHN | CHN19002 | 122.00 | 114.17 | 23.32 | 0.91 | 0.60 | 2.88 | MODRSS |  | 47.08 |  | MODTES | 57.00 | CR |  | 84.0 |  | 27M0G7W |  | 4C | P |  |
| CME | CME30001 | -13.00 | 12.70 | 6.20 | 2.54 | 1.68 | 87.00 | MODRSS |  | 38.15 |  | MODTES | 57.00 | CL |  | 84.0 |  | 27M0G7W |  | 4I | P |  |
| CME | CME30002 | -13.00 | 12.70 | 6.20 | 2.54 | 1.68 | 87.00 | MODRSS |  | 38.15 |  | MODTES | 57.00 | CR |  | 84.0 |  | 27M0G7W |  | 4I | P |  |
| ETH | ETH09201 | 36.00 | 40.49 | 9.20 | 2.83 | 2.26 | 174.44 | MODRSS |  | 36.40 |  | MODTES | 57.00 | CL |  | 82.0 |  | 27M0G7W |  | 4P | P |  |
| ETH | ETH09202 | 36.00 | 40.49 | 9.20 | 2.83 | 2.26 | 174.44 | MODRSS |  | 36.40 |  | MODTES | 57.00 | CR |  | 82.0 |  | 27M0G7W |  | 4P | P |  |
| GHA | GHA10801 | -25.00 | -1.20 | 7.90 | 1.48 | 1.06 | 102.00 | MODRSS |  | 42.49 |  | MODTES | 57.00 | CR |  | 83.0 |  | 27M0G7W |  | 4F | P |  |
| GHA | GHA10802 | -25.00 | -1.20 | 7.90 | 1.48 | 1.06 | 102.00 | MODRSS |  | 42.49 |  | MODTES | 57.00 | CL |  | 83.0 |  | 27M0G7W |  | 4F | P |  |
| IND | INDA_101 | 55.80 | 76.16 | 14.72 |  |  |  | CB_RSS_INDA |  | 45.66 |  | MODTES | 57.00 | CR |  | 82.0 |  | 27M0G7W |  | 4U | P |  |
| IND | INDA_102 | 55.80 | 76.16 | 14.72 |  |  |  | CB_RSS_INDA |  | 45.66 |  | MODTES | 57.00 | CL |  | 82.0 |  | 27M0G7W |  | 4U | P |  |
| IRN | IRN10901 | 34.00 | 54.20 | 32.40 | 3.82 | 1.82 | 149.00 | MODRSS |  | 36.03 |  | MODTES | 57.00 | CR |  | 82.0 |  | 27M0G7W |  | 4S | P |  |
| IRN | IRN10902 | 34.00 | 54.20 | 32.40 | 3.82 | 1.82 | 149.00 | MODRSS |  | 36.03 |  | MODTES | 57.00 | CL |  | 82.0 |  | 27M0G7W |  | 4S | P |  |
| IRQ | IRQ25601 | 50.00 | 43.86 | 32.86 | 1.82 | 1.34 | 162.65 | MODRSS |  | 40.58 |  | MODTES | 57.00 | CL |  | 82.0 |  | 27M0G7W |  | 4M | P |  |
| IRQ | IRQ25602 | 50.00 | 43.86 | 32.86 | 1.82 | 1.34 | 162.65 | MODRSS |  | 40.58 |  | MODTES | 57.00 | CR |  | 82.0 |  | 27M0G7W |  | 4M | P |  |
| KOR | KO11201D | 116.00 | 127.50 | 36.00 | 1.24 | 1.02 | 168.00 | R13RSS |  | 43.40 |  | R13TES | 57.30 | CL |  | 82.0 |  | 27M0G7W | KOREASAT-1 | 03 | PE |  |
| KOR | KOR11201 | 116.00 | 127.50 | 36.00 | 1.24 | 1.02 | 168.00 | R13RSS |  | 43.40 |  | R13TES | 57.30 | CL |  | 82.0 |  | 27M0F8W | KOREASAT-1 | 03 | PE |  |
| MOZ | MOZ30701 | -1.00 | 34.00 | -18.00 | 3.57 | 1.38 | 55.00 | MODRSS |  | 37.52 |  | MODTES | 57.00 | CL |  | 82.0 |  | 27M0G7W |  | 4K | P |  |
| MOZ | MOZ30702 | -1.00 | 34.00 | -18.00 | 3.57 | 1.38 | 55.00 | MODRSS |  | 37.52 |  | MODTES | 57.00 | CR |  | 82.0 |  | 27M0G7W |  | 4K | P |  |
| NIG | NIG11901 | -19.20 | 7.80 | 9.40 | 2.16 | 2.02 | 45.00 | MODRSS |  | 38.05 |  | MODTES | 57.00 | CR |  | 82.0 |  | 27M0G7W |  | 4G | P |  |
| NIG | NIG11902 | -19.20 | 7.80 | 9.40 | 2.16 | 2.02 | 45.00 | MODRSS |  | 38.05 |  | MODTES | 57.00 | CL |  | 82.0 |  | 27M0G7W |  | 4G | P |  |
| NMB | NMB02501 | -18.80 | 17.50 | -21.60 | 2.66 | 1.90 | 48.00 | MODRSS |  | 37.41 |  | MODTES | 57.00 | CL |  | 82.0 |  | 27M0G7W |  | 4H | P |  |
| NMB | NMB02502 | -18.80 | 17.50 | -21.60 | 2.66 | 1.90 | 48.00 | MODRSS |  | 37.41 |  | MODTES | 57.00 | CR |  | 82.0 |  | 27M0G7W |  | 4H | P |  |
| NPL | NPL12201 | 50.00 | 83.70 | 28.30 | 1.72 | 0.60 | 163.00 | MODRSS |  | 44.31 |  | MODTES | 57.00 | CR |  | 82.0 |  | 27M0G7W |  | 4N | P |  |

Table 3A2

Basic characteristics of the Regions 1 and 3 feeder-link Plan in the frequency band 17.3-18.1 GHz (sorted by administration)

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Admin. symbol | Beam identifi- cation | Orbital position | Boresight | Space station antenna characteristics | Space station antenna code | Shaped beam | Space station antenna gain | Earth station antenna | Polarization | e.i.r.p. | Power control | Designation of emission | Identity of the space station | Group code | Sta- tus | Remarks |
|  |  |  | Long. | Lat. | Major axis | Minor axis | Orien- tation |  |  | Co-polar | Cross- polar | Code | Gain | Type | Angle |  |  |  |  |  |  |  |
| AFG | AFG24501 | 50.00 | 67.00 | 34.30 | 1.89 | 1.19 | 18.00 | MODRSS |  | 40.93 |  | MODTES | 57.00 | CL |  | 84.0 |  | 27M0G7W |  | 7I | P |  |
| AFG | AFG24502 | 50.00 | 67.00 | 34.30 | 1.89 | 1.19 | 18.00 | MODRSS |  | 40.93 |  | MODTES | 57.00 | CR |  | 84.0 |  | 27M0G7W |  | 7I | P |  |
| AGL | AGL29500 | -24.80 | 16.43 | -12.37 | 2.66 | 1.75 | 77.43 | MODRSS |  | 37.77 |  | MODTES | 57.00 | CR |  | 84.0 |  | 27M0G7W |  |  | P |  |
| ALB | ALB29600 | 62.00 | 19.50 | 41.37 | 0.60 | 0.60 | 69.35 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CL |  | 82.6 |  | 27M0G7W |  |  | P |  |
| ALG | ALG25152 | -24.80 | 1.50 | 27.60 | 3.65 | 2.94 | 135.00 | MODRSS |  | 34.14 |  | MODTES | 57.00 | CL |  | 84.0 |  | 27M0G7W |  |  | P |  |
| AND | AND34100 | -37.00 | 1.60 | 42.50 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CL |  | 83.0 |  | 27M0G7W |  |  | P |  |
| ARM | ARM06400 | 22.80 | 44.99 | 39.95 | 0.73 | 0.60 | 148.17 | MODRSS |  | 48.02 |  | MODTES | 57.00 | CR |  | 84.0 |  | 27M0G7W |  |  | P |  |
| ARS | ARS00375 | 17.00 | 44.60 | 23.40 | 4.21 | 2.48 | 145.00 | MODRSS |  | 34.26 |  | MODTES | 57.00 | CL |  | 84.0 |  | 27M0G7W |  | 54 | P |  |
| ARS | ARS34000 | 17.00 | 44.60 | 23.40 | 4.21 | 2.48 | 145.00 | MODRSS |  | 34.28 |  | MODTES | 57.00 | CL |  | 84.0 |  | 27M0G7W |  | 54 | P |  |
| AUS | AUS00400 | 152.00 | 135.00 | -24.20 | 7.19 | 5.20 | 140.00 | MODRSS |  | 28.71 |  | MODTES | 57.00 | CL |  | 87.0 |  | 27M0G7W |  | 30 | P |  |
| AUS | AUS00401 | 152.00 | 96.83 | -12.19 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CL |  | 87.0 |  | 27M0G7W |  | 30 | P |  |
| AUS | AUS00402 | 152.00 | 105.69 | -10.45 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CL |  | 87.0 |  | 27M0G7W |  | 30 | P |  |
| AUS | AUS00403 | 152.00 | 110.52 | -66.28 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CL |  | 87.0 |  | 27M0G7W |  | 30 | P |  |
| AUS | AUS00404 | 152.00 | 158.94 | -54.50 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CL |  | 87.0 |  | 27M0G7W |  | 30 | P |  |
| AUS | AUS00405 | 152.00 | 159.06 | -31.52 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CL |  | 87.0 |  | 27M0G7W |  | 30 | P |  |
| AUS | AUS00406 | 152.00 | 167.93 | -29.02 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CL |  | 87.0 |  | 27M0G7W |  | 30 | P |  |
| AUS | AUS0040A | 152.00 | 135.36 | -23.95 | 6.89 | 4.83 | 141.15 | R123FR |  | 29.23 |  | MODTES | 57.00 | CL |  | 87.0 |  | 27M0G7W |  | 30 | P |  |
| AUS | AUS00500 | 152.00 | 135.00 | -24.20 | 7.19 | 5.20 | 140.00 | MODRSS |  | 28.71 |  | MODTES | 57.00 | CR |  | 87.0 |  | 27M0G7W |  | 41 | P |  |
| AUS | AUS00501 | 152.00 | 96.83 | -12.19 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CR |  | 87.0 |  | 27M0G7W |  | 41 | P |  |
| AUS | AUS00502 | 152.00 | 105.69 | -10.45 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CR |  | 87.0 |  | 27M0G7W |  | 41 | P |  |
| AUS | AUS00503 | 152.00 | 110.52 | -66.28 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CR |  | 87.0 |  | 27M0G7W |  | 41 | P |  |
| AUS | AUS00504 | 152.00 | 158.94 | -54.50 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CR |  | 87.0 |  | 27M0G7W |  | 41 | P |  |
| AUS | AUS00505 | 152.00 | 159.06 | -31.52 | 0.60 | 0.60 | 0.00 | MODRSS |  | 48.88 |  | MODTES | 57.00 | CR |  | 87.0 |  | 27M0G7W |  | 41 | P |  |

COLUMN  HEADINGS

Col. 1	Nominal orbital position, in degrees and hundredths of a degree from the Greenwich meridian (negative values indicate longitudes which are west of the Greenwich meridian; positive values indicate longitudes which are east of the Greenwich meridian).

Col. 2	Notifying administration symbol.

Col. 3	Beam identification (Column 2, normally, contains the symbol designating the administration or the geographical area taken from Table B1 of the Preface to the International Frequency List, followed by the symbol designating the service area).

Col. 4	Polarization (CL – circular left, CR – circular right).

Col. 5	Channel number/indication of minimum equivalent protection margin (EPM) for a given assignment derived from the set of values for all test points belonging to the given beam.

Table 3B1

Minimum equivalent protection margin in the Regions 1 and 3 feeder-link Plan in
the frequency band 14.5-14.8 GHz (sorted by orbital position)

| 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Orbital position | Admin. symbol | Beam Identification | Polari- zation type | Channel number |
|  |  |  |  | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 |
|  |  |  |  | Minimum equivalent protection margin |
| -37.00 | SEN | SEN22201 | CL |  |  |  | 40.8 |  | 39.6 |  | 39.6 |  | 39.6 |  | 39.6 |  |
| -37.00 | SEN | SEN22202 | CR |  |  |  |  | 39.6 |  | 39.6 |  | 39.6 |  | 39.6 |  | 40.7 |
| -30.00 | TGO | TGO22601 | CL |  |  |  | 15.0 |  | 14.1 |  | 14.1 |  | 14.1 |  | 14.1 |  |
| -30.00 | TGO | TGO22602 | CR |  |  |  |  | 14.1 |  | 14.1 |  | 14.1 |  | 14.1 |  | 15.0 |
| -25.00 | GHA | GHA10801 | CR |  |  |  | 14.9 |  | 14.1 |  | 14.1 |  | 14.1 |  | 14.1 |  |
| -25.00 | GHA | GHA10802 | CL |  |  |  |  | 14.1 |  | 14.1 |  | 14.1 |  | 14.1 |  | 14.9 |
| -19.20 | NIG | NIG11901 | CR |  |  |  | 6.4 |  | 4.2 |  | 4.2 |  | 4.2 |  | 4.2 |  |
| -19.20 | NIG | NIG11902 | CL |  |  |  |  | 4.2 |  | 4.2 |  | 4.2 |  | 4.2 |  | 6.4 |
| -18.80 | NMB | NMB02501 | CL |  |  |  | 6.9 |  | 4.5 |  | 4.5 |  | 4.5 |  | 4.5 |  |
| -18.80 | NMB | NMB02502 | CR |  |  |  |  | 4.5 |  | 4.5 |  | 4.5 |  | 4.5 |  | 6.9 |
| -13.00 | CME | CME30001 | CL |  |  |  | 17.2 |  | 16.3 |  | 16.3 |  | 16.3 |  | 16.3 |  |
| -13.00 | CME | CME30002 | CR |  |  |  |  | 16.3 |  | 16.3 |  | 16.3 |  | 16.3 |  | 17.2 |
| -7.00 | SDN | SDN__101 | CL |  |  |  | 27.1 |  | 26.1 |  | 26.1 |  | 26.1 |  | 26.1 |  |
| -7.00 | SDN | SDN__102 | CR |  |  |  |  | 26.1 |  | 26.1 |  | 26.1 |  | 26.1 |  | 27.1 |
| -1.00 | MOZ | MOZ30701 | CL |  |  |  | 16.6 |  | 15.7 |  | 15.7 |  | 15.7 |  | 15.7 |  |
| -1.00 | MOZ | MOZ30702 | CR |  |  |  |  | 15.7 |  | 15.7 |  | 15.7 |  | 15.7 |  | 16.6 |
| 4.80 | AFS | AFS02101 | CL |  |  |  | 11.9 |  | 11.0 |  | 11.0 |  | 11.0 |  | 11.0 |  |
| 4.80 | AFS | AFS02102 | CR |  |  |  |  | 11.0 |  | 11.0 |  | 11.0 |  | 11.0 |  | 11.9 |
| 11.00 | YEM | YEM__101 | CR |  |  |  | 47.8 |  | 47.3 |  | 47.3 |  | 47.3 |  | 47.3 |  |
| 11.00 | YEM | YEM__102 | CL |  |  |  |  | 47.3 |  | 47.3 |  | 47.3 |  | 47.3 |  | 47.8 |
| 34.00 | IRN | IRN10901 | CR |  | 15.2 |  | 13.9 |  | 13.9 |  | 13.9 |  | 13.9 |  | 13.9 |  |
| 34.00 | IRN | IRN10902 | CL |  |  | 14.3 |  | 13.9 |  | 13.9 |  | 13.9 |  | 13.9 |  | 14.8 |
| 36.00 | ETH | ETH09201 | CL |  |  |  | 2.3 |  | 1.4 |  | 1.4 |  | 1.4 |  | 1.4 |  |
| 36.00 | ETH | ETH09202 | CR |  |  |  |  | 1.4 |  | 1.4 |  | 1.4 |  | 1.4 |  | 2.3 |
| 37.80 | SOM | SOM31201 | CL |  |  |  | 0.0 |  | -0.3 |  | -0.3 |  | -0.3 |  | -0.3 |  |
| 37.80 | SOM | SOM31202 | CR |  |  |  |  | -0.3 |  | -0.3 |  | -0.3 |  | -0.3 |  | 1.6 |
| 38.20 | PAK | PAK12701 | CR |  | 14.2 |  | 3.2 |  | 0.9 |  | 0.9 |  | 0.9 |  | 0.9 |  |
| 38.20 | PAK | PAK12702 | CL |  |  | 4.2 |  | 0.9 |  | 0.9 |  | 0.9 |  | 0.9 |  | 3.3 |
| 42.50 | SEY | SEY00001 | CL |  |  |  | 36.3 |  | 35.3 |  | 35.3 |  | 35.3 |  | 35.3 |  |
| 42.50 | SEY | SEY00002 | CR |  |  |  |  | 35.3 |  | 35.3 |  | 35.3 |  | 35.3 |  | 36.4 |
| 50.00 | IRQ | IRQ25601 | CL |  |  |  | -0.1 |  | -0.1 |  | -0.1 |  | -0.1 |  | -0.1 |  |
| 50.00 | IRQ | IRQ25602 | CR |  |  |  |  | -0.1 |  | -0.1 |  | -0.1 |  | -0.1 |  | 2.4 |
| 50.00 | NPL | NPL12201 | CR |  | 38.2 |  | 3.9 |  | 1.2 |  | 1.2 |  | 1.2 |  | 1.2 |  |
| 50.00 | NPL | NPL12202 | CL |  |  | 4.6 |  | 1.2 |  | 1.2 |  | 1.2 |  | 1.2 |  | 3.9 |
| 55.80 | IND | INDA_101 | CR |  | 25.7 |  | 24.7 |  | 24.7 |  | 24.7 |  | 24.7 |  | 24.7 |  |
| 55.80 | IND | INDA_102 | CL |  |  | 24.7 |  | 24.7 |  | 24.7 |  | 24.7 |  | 24.7 |  | 25.6 |

Table 3B2

Minimum equivalent protection margin in the Regions 1 and 3 feeder-link Plan 
in the frequency band 17.3-18.1 GHz (sorted by orbital position)

| 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Orbital position | Admin. symbol | Beam identification | Pola- riza- tion type | Channel number |
|  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 |
|  |  |  |  | Minimum equivalent protection margin |
| -178.00 | FJI | FJI19300 | CR | 3.3 |  | 3.3 |  | 3.3 |  | 3.3 |  | 3.3 |  | 3.3 |  | 3.3 |  | 3.3 |  | 3.3 |  | 3.3 |  | 3.3 |  | 3.3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -178.00 | SMO | SMO05700 | CL | 12.2 |  | 12.2 |  | 12.2 |  | 12.2 |  | 12.2 |  | 12.2 |  | 12.2 |  | 12.2 |  | 12.2 |  | 12.2 |  | 12.2 |  | 12.2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -160.00 | F | OCE10100 | CL |  | 999.9 |  | 999.9 |  | 999.9 |  | 999.9 |  | 999.9 |  | 999.9 |  | 999.9 |  | 999.9 |  | 999.9 |  | 999.9 |  | 999.9 |  | 999.9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.20 | GMB | GMB30200 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.3 |  | 3.2 |  | 3.2 |  | 3.2 |  | 3.2 |  | 3.2 |  | 3.2 |  | 3.2 |  | 3.2 |  | 3.2 |  |
| -37.20 | IRL | IRL21100 | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9.2 |  | 10.2 |  | 10.2 |  | 10.2 |  | 10.2 |  | 10.3 |  | 10.2 |  | 10.2 |  | 10.3 |  | 10.3 |  |
| -37.20 | NGR | NGR11500 | CL | 1.8 |  | -0.4 |  | -0.4 |  | -0.4 |  | -0.4 |  | -0.4 |  | -0.4 |  | -0.4 |  | -0.4 |  | -0.4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.00 | AND | AND34100 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 13.3 |
| -37.00 | GUI | GUI19200 | CR |  | 0.8 |  | 0.8 |  | 0.8 |  | 0.8 |  | 0.8 |  | 0.8 |  | 0.8 |  | 0.8 |  | 0.8 |  | 1.5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -37.00 | POR | POR__100 | CR | 2.4 |  | 0.0 |  | -0.1 |  | 0.0 |  | -0.1 |  | 0.0 |  | -0.1 |  | 0.0 |  | -0.1 |  | 0.0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -36.80 | MTN | MTN__100 | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 0.3 |  | 2.0 |
| -36.80 | SMR | SMR31100 | CL |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 10.6 |  | 12.0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | CPV | CPV30100 | CL |  | 14.3 |  | 14.3 |  | 14.3 |  | 14.3 |  | 14.3 |  | 14.3 |  | 14.3 |  | 14.3 |  | 14.3 |  | 11.6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | DNK | DNK09000 | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 5.1 |  |  |  |  |  | 5.1 |  |  |  |  |  |  |
| -33.50 | DNK | DNK09100 | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.1 |  |  |  | 1.1 |  |  |  |  |
| -33.50 | G | G 02700 | CR |  | 6.4 |  | 6.4 |  | 6.4 |  | 6.4 |  | 6.4 |  | 6.4 |  | 6.4 |  | 6.4 |  | 6.4 |  | 4.2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | ISL | ISL04900 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.5 |  | -0.1 |  | -0.1 |  | 1.8 |  | 7.5 |  | 2.8 |  | 1.8 |  | 1.8 |  | 2.8 |  | 14.1 |  |
| -33.50 | ISL | ISL05000 | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.1 |  | 1.1 |  | 1.1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | LBR | LBR24400 | CR | 10.6 |  | 7.7 |  | 7.7 |  | 7.7 |  | 7.7 |  | 7.7 |  | 7.7 |  | 7.7 |  | 7.7 |  | 7.7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -33.50 | SRL | SRL25900 | CR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9.7 |  | 11.8 |  | 11.8 |  | 11.4 |  | 13.1 |  | 13.7 |  | 11.4 |  | 11.4 |  | 13.7 |  | 17.1 |  |
| -30.00 | BFA | BFA10700 | CL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 12.0 |  | 12.0 |  | 12.0 |  | 12.0 |  | 12.0 |  | 12.0 |  | 12.0 |  | 12.0 |  | 12.0 |  | 14.9 |
| -30.00 | E | E____100 | CR | 7.9 |  | 7.6 |  | 7.6 |  | 7.6 |  | 7.6 |  | 7.6 |  | 7.6 |  | 7.6 |  | 7.6 |  | 7.6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -30.00 | E | HISP27D4 | CR | 10.2 |  |  |  | 10.1 |  |  |  | 10.1 |  |  |  | 10.1 |  |  |  | 10.1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| -30.00 | E | HISP27D6 | CR | 11.2 |  |  |  | 11.1 |  |  |  | 11.1 |  |  |  | 11.1 |  |  |  | 11.1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

____________