## Slide 1: C-Band Now and Tomorrow THE FIJIAN EXPERIENCE
Spectrum Management Symposium
1 November 2013 @ the Tanoa International Hotel (Nadi)
Prepared By Igor Zukina

## Slide 2: C-Band
Downlink: 3.7 – 4.2 GHz
Uplink: 5.9 – 6.4 GHz
ADVANTAGES:
Less disturbance from heavy rain fade
Cheaper Bandwidth
DISADVANTAGES:
Needs a larger satellite dish (diameters of minimum 1-3m)
Powerful (=expensive) RF unit
More expensive hardware
Possible Interference from microwave links
THE FIJIAN EXPERIENCE

## Slide 3: C-Band Challenges
Down link reception Interference level significantly increased by:
  wireless radio links (last mile broadband delivery) in some cases spreading without management and licencing
  many cases of reported interferences
  interferences can get reduced by cost intensive microwave filters or more directional antennas = most costly for service provider
  difficult interference problem resolution as there is no spectrum licences with specific operational parameters
THE FIJIAN EXPERIENCE

## Slide 4: Immediate Commitment:
Reorganise and reengineer the 2000 – 5000 MHz bands
Strictly regulate operating parameters for WiMax , LTE
Enforce spectrum management and precise licencing for all operating devices
Equipment type approval (possible mandatory)
Protect the C-band for Satellite service – continue to be primary service
THE FIJIAN EXPERIENCE

## Slide 5: Future commitment:
Continue to analyse new technologies and user demand for the services in C-band
  currently very high utilisation of SAT services:
  All fixed SAT tele communications depend on C-Band,
  Most of broadcast linking and distribution services are in C-band
THE FIJIAN EXPERIENCE

## Slide 6: C-band Likelihood for the future :
  Demand of SAT service may decrease because of presence of Fibre communication providing equal performance/cost or cheaper service.
  Ku band receiving equipment using statistical signal processing (using DSP), and modern dynamically controllable satellite transponders will increase availability of the service equal to the C-band – in this case it would be more advantages for the region – smaller dishes less wind load
  A large demand for last mile wireless delivery may overturn the C-band as primarily service purely based on commercial value of the spectrum and use.
                OR
  New technology satellite focused on switched data, last mile delivery which may replace current legacy constructed satellites – may create continuum for SAT spectrum demand and protection (like 03b)
THE FIJIAN EXPERIENCE

## Slide 7: THANK YOU