| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-C-0168 |
|  | Original: English |
| WG(s): 4 | 2nd FG IPTV meeting: Busan, 16-20 October 2006 |
| CONTRIBUTION |
| Source: | ZTE Corporation |
| Title: | Multicast user authentication and authorization function and procedure for IPTV network |

# Abstract

This contribution provides an overview of Multicast user authentication and authorization function  and procedure for IPTV network.

# discussion

As the current multicast protocol(i.e IGMP) does not consider Multicast user authentication and authorization  ,  it is a little  difficult for us to develop  the IPTV services efficiently . So it  is very necessary for  the IPTV bearer network  to restructures the multicast and make it easy to provide authentication function for  the multicast users.

Multicast User authentication function controls the authority for users to receive multicast flows. and Through authentication of multicast users,  the network can distinguish legal multicast users from the illegal ones and then distribute the multicast traffic to the reasonable receivers.

i) The network components for IPTV Multicast User authentication and authorization function

There are three function modules which are relative to Multicast user management, they are  Multicast duplication point, Multicast Authentication Point and  Account Information Database . The location of  the three components in the IPTV network are illustrated and described in the following  figure (figure 1):

figure 1: Multicast user management function  components

- Multicast duplication Point. This function module contains the multicast traffic distribution table, which can control direction of the duplication traffic and be used to avoid  forwarding the multicast traffic to the illegal users. Only the users who have passed authentication can exist in this table .

- Multicast Authentication Point. This function module will inquire  the Account information Database and return the result to Multicast duplication Point, the Multicast duplication Point will use the result to construct distribution table.

- Account Information Database.  this function module has  all the accounts, which contain the user’s multicast properties. Especially, the values of multicast properties may depend on the result of the service layer authentication.

- Procedure of IPTV multicast user authentication and authorization

- When a user initiates a multicast “join” request to join a certain multicast group with a account,  the duplication point will not accept the request and make him join the group at once, it will sent the request to the authentication point.

- The authentication point inquire  the Account information Database and return the result to Multicast duplication Point. The value of the user’s multicast property in the account could be set by the service layer system.

- According to the authentication result returned from the authentication point, the Multicast duplication Point will decide whether it allow the user to join the group or not. If   allow the user to  join the group , the duplication will add it to distribution table.  Whereas it will refuse the user to join the group.

# Proposal

According to the features of the IPTV service and the discussion above, there are two proposals as follows:

  - the IPTV network  should support multicast user authentication function.

  - The procedure of  multicast user authentication  discussed in this contribution could be take into consideration.

_______________