| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-C-0184 |
|  | English only |
| WG(s): 1 | 2nd FG IPTV meeting: Busan, 16 – 20 October 2006 |
| CONTRIBUTION |
| Source: | Korea (Republic of) |
| Title: | Classification of IPTV services |

1. Introduction

This contribution proposes a description and classification of the IPTV services. From the 1st FG IPTV meeting, a list of the IPTV services to be considered in the activities of the ITU FG IPTV has been discussed. The list covers most of the possible IPTV services but it is unordered and has some duplication for the similar services. Therefore, we classified the list of IPTV services into five services: IPTV-Communication, IPTV-Interactive, IPTV-Commerce, IPTV-VoD and IPTV-Channel by their service characteristic and gave description of each service. In addition, we tried to map the services by required functional features such as QoS/QoE, Storage & security, Network control including mobility, Media processing & control and Navigation & Discovery as sub-classification.

2. IPTV Service classifications and descriptions

- IPTV-Communication

IPTV-Communication is the IPTV-based communication service that provides methods for video, audio and data (text) information exchange. This service includes SMS (Short Message Service), T-mail (sending e-mail by TV terminals), VoIP, Video Conference, TV Messaging (instance messaging or chatting through TV terminal) and so on.

- IPTV-Interactive

IPTV-Interactive is the IPTV-based interactive service which provides contents or information service with interactive communications between service providers and users. This service includes network games, Information services (news, weather, traffic, movie/theater ticket query), e-Learning (real-time, distance learning), TV Voting (TV survey, TV quiz), TV karaoke and so on.

- IPTV-Commerce

IPTV-Commerce is the IPTV-based commerce service which allows users to purchase goods and use financial services by providing means of payment and secured financial service supporting programs through the TV terminal. This service includes shopping, Interactive Advertisement (interactive-AD: TV banner, PIP Advertisements), T-Banking, stock market service and so on.

- IPTV-VOD

IPTV-VOD is the IPTV-based Video-on-demand service that provides video, audio and data service triggered by user’s selection. This service includes SVoD (subscribtion-VoD), FVoD (Free-VoD), Push VoD, NVoD (Near Vod), Time-shift TV and so on.

- IPTV-Channel

IPTV-Channel is the IPTV-based channel service that provides video, audio and data linear broadcasting service.

Table 1. IPTV service classifications

| Classifications | Example Services | Sub-classifications | Features |
| --- | --- | --- | --- |
| IPTV-Communication | SMS, T-mail, VoIP, Video Conference, TV Messaging (instance messaging or chatting) |  | QoS/QoE |
|  |  |  | Storage & security |
|  |  | Mobile IPTV service | Network control including mobility |
|  |  | EPG/IPG | Media processing & control |
|  |  | Portal Service | Navigation & Discovery |
| IPTV-Interactive | Information services (news, weather, traffic, movie/theater ticket query), e-Learning, TV Voting (TV survey, TV quiz), Games, TV karaoke |  | QoS/QoE |
|  |  | Download service | Storage & security |
|  |  | Mobile IPTV service | Network control including mobility |
|  |  | EPG/IPG | Media processing & control |
|  |  | Portal Service | Navigation & Discovery |
| IPTV-Commerce | Shopping, T-Banking, Stock market service, Interactive Ad. (Picture-in-picture Advertisement, banner) |  | QoS/QoE |
|  |  |  | Storage & security |
|  |  | Mobile IPTV service | Network control including mobility |
|  |  | EPG/IPG | Media processing & control |
|  |  | Portal Service | Navigation & Discovery |
| IPTV-VOD | SVoD, FVoD, PPV |  | QoS/QoE |
|  |  | PVR, Push VoD, Download service | Storage & security |
|  |  | Mobile IPTV service | Network control including mobility |
|  |  | EPG/IPG, Multi angle/channel service, Time-shift TV, NVoD | Media processing & control |
|  |  | Portal Service | Navigation & Discovery |
| IPTV-Channel | Linear Audio/Video/data broadcast, PPV |  | QoS/QoE |
|  |  | PVR | Storage & security |
|  |  | Mobile IPTV service | Network control including mobility |
|  |  | Linear broadcast with trick mode, Multi angle/channel service | Media processing & control |
|  |  | Portal Service | Navigation & Discovery |

3. Proposal

In this contribution, we have proposed IPTV service descriptions and classification by their characteristics and technical features. We hope that this service description and classification will be adopted for the relevant section of the IPTV service standardization.

___________________