| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-C-0327 |
|  | English only |
| WG(s): 1 | 3rd FG IPTV meeting: Mountain View, USA, 22 – 26 January 2007 |
| CONTRIBUTION |
| Source: | BT, UK (Simon T Jones) |
| Title: | Reference Model and Definitions for IPTV |
| Doc: | FG IPTV- INTERIM -DOC-002 Rev2, Section 7 also FG IPTV-C-0261 and FG IPTV-DOC-056 |

Authors note: The following text is intended for inclusion in the Architecture Document. The role definitions are based on those in the ATIS IIF Architecture Requirements document.

# IPTV Reference Model

The following figure shows the main roles that are involved in the provision of an IPTV Service.

Figure X: Basic IPTV Service and IPTV Roles

The four roles are as described below:

[These descriptions are based upon those in the ATIS IIF Architecture Requirements]

Content Provider: The entity that owns or is licensed to sell content or content assets.

Service Provider: The entity that providing the IPTV Service to the Customer.

Typically, the Service Provider acquires or licenses content from Content Providers and packages this into a service that is sold to the Customer.

Network Provider: The entity providing that connects the Customers and the Service Providers.

Customer: The entity that consumes and pays for the IPTV Service.

## IPTV Service Types

These roles are useful for the description of the basic IPTV Service types.

### Linear IPTV with Local PVR

A key part of a typical IPTV Service is the delivery of Linear TV. This is received, from the existing broadcast transmission from a Content Provider, trans-coded and multicast by the Service Provider. The multicast streams are delivered by the Network Provider, via the Consumer’s Network to the Customer’s IPTV device.

Figure X: Linear IPTV with Local PVR

### Content on Demand

The second part of a typical IPTV Service is the delivery of On-Demand Content. The content is normally received from a Content Provider in the form of physical media, such as a digital video-tape. This trans-coded and stored by the Service Provider and made available as unicast streams. The unicast streams are delivered by the Network Provider, via the Consumer’s Network to the Customer’s IPTV device.

Figure X: Content on Demand

### Hybrid: Online and Off-air TV Delivery

An alternative approach for the delivery of Liner TV is to enable the customers IPTV device to directly receive the broadcast signal from the Content Provider. This will then be combined with On-Demand content delivered over the network from the Network Provider.

Figure X: Hybrid: Online and Off-air TV Delivery

## IPTV Definitions

In the description of IPTV Services a number of different terms, such as service, application, and component are often used. For consistency the following definitions are to be used

The IPTV Service is the total proposition offered to the customer, if offers a set of

Applications that provide different Service features to the customer

Live TV

On Demand Video

Communications

Games

These make use of a set of underlying support services that provide common facilities these include.

Unicast Video Delivery

Multicast Video Delivery

An IPTV component provides part of a service, examples are

Video streamer

___________

# Footnotes

Based on the definitions in the ATIS IIF Architecture Requirements document ATIS-0800002