| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-C-1098 |
|  | English only |
| WG(s): 5 | 7th FG IPTV meeting: Qawra, St Paul’s Bay, Malta, 11-18 December 2007 |
| CONTRIBUTION |
| Source: | ZTE Corporation |
| Title: | Proposal on the document 0159 and 0160. |

Introduction

This contribution provides text enhancement for document “FG IPTV-DOC-0159(15-19 Oct. 2007), Working Document: Aspects of IPTV End System – Terminal Device”.

# Discussion

# .

Reference

[1] FG IPTV-DOC-0160 (15-19 Oct. 2007), Working Document: Aspects of IPTV End System – Terminal Device

[2] FG IPTV-DOC-0160 (15-19 Oct. 2007), Working Document: Aspects of Home Network supporting

Proposal

- Add the requirement like “Supporting provisioning and management remotely” in 7.1.2  Provisioning and Management

- change “PAN” to “WPAN” in 7.2.2.3 TD-HN interface

- change “100BASE-TX” to “10/100BASE-TX” in 7.2.2.3 TD-HN interface

- Editing work for the document 0159.

- Add some contents to the section of Network Security  in document 0160:

The section 6.3.1 may be read as following:

The security for Home Network includes the following at least:

- The management system and Access Gateway both need to be authenticated;

- Access Gateway authentication must be non service specific;

- Support a specified list of ALGs, and the list can be upgraded;

- Provide a Firewall which is remotely configurable;

- Provide a unique  hardware ID which can be remotely read;

- Support different classes of user with regard to management access rights;

- Pairing is required for non physically attached devices.

6. Editing work for document 0160

_________________