|  | INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-IL-0121 |
|  |  | English only |
| WG: 2 |  | 7th FG IPTV meeting: Qawra, St. Paul’s Bay, Malta, 11–18 December 2007 |
| INCOMING LIAISON STATEMENT (Ref.: xxx) |
| Source: | Digital Video Broadcasting Project; Technical Module subgroup on IP Infrastructure (DVB TM-IPI) |
| Title: | Updated Information on Ongoing Work in DVB-IPI |

The Digital Video Broadcasting Project (DVB) Technical Module group on IP Infrastructure (TM-IPI) wishes to continue the successful exchange of information with the ITU-T Focus Group on IPTV (ITU-T FG IPTV) in the spirit of the successful communication on Application Layer Forward Error Correction (AL-FEC). This exchange helped you in the decision to accept the DVB AL-FEC mechanism as your application layer error recovery mechanism based on FEC.

The DVB project strongly believes that this continuous exchange of information will help to avoid conflicting specifications and foster industry harmonization also for other areas. Following up on some on your status request on working areas in DVB-IPI we would like to inform you as follows:

DVB has progressed the work on retransmission (RET) and on content download services (CDS), but still no mature specification is available on any of the two work areas. Nevertheless, to continuously support the collaboration offer of ITU-T FG IPTV WG2 with DVB, we would at least like to provide you the following information on these two matters.

For CDS, based on multiple requests by external organizations on the status of the work, DVB-IPI has decided to compile a slide set which provides more insight into the work. The slide set (referenced IPI2510r2) is attached to this letter and Digital Fountain chairing this Task Force in DVB-IPI has offered to present this slide set to your experts at the upcoming meeting of the ITU-T FG on IPTV in December 2007, if appropriate for you. Any feedback on this information from your side is very welcome.

With respect to the progress on RET, the major aspects of the RET solution have been agreed upon, with some further work left dealing with protocol details.  As previously communicated, the RET solution is based on RTP/RTCP both for linear TV and on-demand TV services.

More specifically, from the HNED (Home Network End Device) point of view, the DVB RET solution will adhere to the following rules:

-The retransmission requests issued by the HNED are RTCP Generic NACK messages, formatted as specified in RFC 4585, S. 6.2.1. These are always sent out by the HNEDs in unicast, even for linear TV services, on a dedicated port-IP address.

-The feedback message formats and the reporting rules specified in RFC 4585 are relaxed in order to allow for more timely reporting. In particular, RTCP packets containing only Generic NACK messages are allowed, in addition to the RTCP Compound packets as per RFC 4585.

-Retransmission packets are sent over unicast but, for linear TV, may also be sent over multicast, e.g., in case of packet loss on a branch higher up in the MC tree. In the latter case, the same Multicast Group Address is used as for the original multicast RTP stream, and the RET packets use SSRC multiplexing. For on-demand TV services, SSRC multiplexing with the original RTP stream is recommended for the RET packets, as well.

-The HNED must support the RET packet format as defined in RFC 4588. The HNED may also support for RET packets to be sent as exact copies of the original packets. However, in that case the HNED will have to adhere to specific rules when calculating the metrics (packet loss, jitter) that are inserted in the RTCP RR messages; RTP network monitors will require additional rules to detect «exact copy" retransmission packets.

-For Linear TV, the HNED may expect to receive an RTCP Generic NACK message coming from nodes in the network (a.k.a., RET proxies). In that case, the HNED should behave in a standard way and so refrain from reporting itself that lost packet.  This will assist in reducing or eliminating any NACK flooding that may arise when a packet was lost on a branch of the multicast tree in e.g. the aggregation network.

-In general, an HNED is allowed to send multiple retransmission requests for the same packet loss event to cope with loss of RET and RTCP FB packets, as long as it does not exceed a certain bandwidth limit for the RTCP messaging. DVB will address such aspects concerning HNED RET client behavior in an informative way.

We appreciate your collaboration on any of these subjects, and we look forward to being informed on updates of related work items within the ITU-T Focus Group on IPTV.

___________________

# Footnotes

Contact: 
Mark Jeffrey (Microsoft Corporation, mark.jeffrey@microsoft.com) 
Thomas Stockhammer (Digital Fountain, stockhammer@digitalfountain.com)