| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On Future Networks |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2009-2012 | FG-FN OD - 55 |
|  | Original: English |
|  |  | 6th FG-FN meeting: Geneva, 6-9 September 2010 |
| OUTPUT DOCUMENT 55 |
| Source: | Editors |
| Title: For: | Draft Deliverable on “Future Networks : Design Goals and Promising Technologies” Output Document |

This is a revised text of draft deliverable on “Future Networks: Design Goals and Promising Technologies” based on contributions and discussions of 6th FG-FN meeting in Geneva, 6-9 September 2010.

Future Networks : Design Goals and Promising Technologies

Summary

This document describes the objectives, design goals, promising technologies, and target date of Future Networks.

Table of Contents

1. Scope

2. References

3. Definitions

4. Abbreviations and Acronyms

5. Convention

6. Introduction

7. Objectives

8. Design Goals

8.1. Energy Saving

8.2. Service Diversity

8.3. Programmability for Service Awareness

8.4. Data-Oriented Design

8.5. Accessibility/Reduction of Digital Gap

8.6. Economic Incentives

8.7. Network Management

8.8. Mobility

8.9. Identification

8.10. Reliability and Security

9. Promising Technologies

9.1. Network Virtualization

9.2. In-system Network Management

9.3. Energy Saving of Networks

9.4. Identification

9.5. Mobility-enhanced Distributed Networking

9.6. Self-optimization Networking

9.7. Data-centric Networking

9.8. Programmable Network supporting Economic Incentives

10. Target Date

Bibliography

Future Networks: Design Goals and Promising 	Technologies

1. Scope

This document describes

- background information including social aspects to do research and standardization of Future Networks as ‘introduction’,

- fundamental issues that are not paid enough attention in designing today’s networks and should be the objective of FNs as ‘objectives’,

- capabilities that should be supported by future networks as ‘design goals’,

- ideas and research topics of future networks that are important and may be relevant to future ITU-T standardization as ‘promising technologies’, and

- target date of Future Networks.

2. References

3. Definition

Component network: A component network consists of a single homogeneous network, which by itself does not provide a single seamless end-to-end global telecommunication infrastructure.

Federation:  Federation is a technology that enables a heterogeneous collection of component networks to be operated as a single seamless network that shares network resources with other networks, while the networks are geographically dispersed and managed by different providers. Note: A federation of networks is sometimes known as a “network of networks”.

Future Network (FN): A future network is a network which is able to provide revolutionary services, capabilities, and facilities that are hard to provide using existing network technologies.

A future network is either:

- a new component network or an enhancement to an existing one;

or

b)	a federation of new component networks or federation of new and existing component networks.

Notes:

1	A network of type b) may also include networks of type a).

2	The label assigned to the final federation may or may not include the word “future” depending on its nature relative to any preceding network and similarities thereto.

Future Networks (FNs): Future Networks is a plurality of Future Network. It is usually used to express that there may be more than one network that fits in the definition of “Future Network”,

New: In the context of this document the word “new” component network means that the component network is able to provide revolutionary services, capabilities, and facilities that are difficult or impossible to provide using existing network technologies.

EdNote: Definition for term ‘data’ may be added.4. Abbreviations and Acronyms

FG-FN		Focus Group on Future Networks

FN 		Future Network

QoS		Quality of Service

NGN 		Next Generation Network

EdNote: The list will be completed in the final draft.

5. Conventions

This document does not provide specific requirements. To avoid mandatory/optional aspect, ‘should’ is used to allow flexibilities.

6. Introduction

The requirements for the networks in total are always changing. There are requirements that do not change while new requirements arise, and the balance between them changes, which evolves the networks and their architecture.

As for the requirements for the networks of the future, traditional requirements such as reliability or “promote fair competition” [1], a requirement that reflect the value of our society, will remain as important as that of today.

At the same time, new requirements are emerging. Various research projects proposed requirements considering the society of the future [2][3], and though there are no consensus yet, it is obvious that sustainability or environmental issues will become a consideration of vital importance for the long-term future. Also new application areas such as machine-to-machine communications, smart grid, and cloud computing are emerging, and there are new implementation technologies such as new silicon process or optical fibre that will enable development of new network architectures. All these new factors will bring new requirements to networks.

The basic architecture of large-scale public networks such as telecommunication networks is difficult to change because they require enormous amount of resources to build, operate and maintain. Their architecture is therefore carefully designed to be flexible enough to satisfy ever-changing requirements. For instance, TCP/IP absorbs and hides the difference among transport layer, and with its simple addressing and other features it has succeeded to adapt to the enormous changes in scalability as well as QoS, security, etc.

However, it is not known if the current networks can continue to fulfil the changing requirements in the future. And the growing market of new application areas may have the potential to finance the enormous investment required to change the networks if the new architecture pays enough attention on backward compatibility and migration cost. Also research communities have long been working on various architectures and supporting technologies such as network virtualization, energy savings of networks, data-centric network, etc.

It is therefore reasonable to expect that some requirements can be realized by new network architecture and supporting technologies of ongoing research activities, and that they could be the foundation of networks of the future whose prototyping and phased deployment may fall roughly between 2015 and 2020. We call networks based on such new architecture Future Networks (FNs). Standardization of architecture of a network takes at least a few years, and more time is necessary for supporting standards, so it seems appropriate to start pre-standardization discussion of FN.

We ITU-T Focus Group on Future Networks (FG-FN) have conducted a survey of FNs related research activities, collected contributions and made discussions. As our survey results and initial rough consensus, in this document we will describe high-level FNs objectives that may differentiate FNs from existing networks, candidate design goals that FNs should satisfy, promising technologies that are potential technologies to achieve design goals, and target date of FNs.

7. Objectives

As described in the introduction, new requirements are emerging thanks to the new social environment, new application areas, etc. Considering these backgrounds, we selected the following four objectives as the ones that are not considered or not satisfactory satisfied in current networks. These objectives can be the candidate characteristics that clearly differentiate FNs and motivate the development and investigation for FNs.

EdNote: Figure illustrating these four objectives will be reviewed for the next meeting.

Environment awareness

Future Networks should be environment friendly. The architecture design, the resulting implementation and operation of Future Networks should minimize its environmental footprint, e.g., to minimize the usage of materials, energy consumption and Greenhouse Gas (GHG) emissions. Future Networks should be designed and implemented so that it can easily be used to reduce other sector’s environmental footprint, e.g., by making it machine-to-machine ready.

Service awareness

Future Networks should provide services that are customized for users with the appropriate functionalities to meet the needs of applications under consideration. Service explosion, i.e., creation and distribution of enormous amount and wide range of services, will occur, and Future Networks should accommodate these services by enabling creation of multiple networks that has optimal or customized functions to realize these services efficiently.

Data awareness

Future Networks should have architecture that is optimized to handling enormous amount of data. Main objective of the current networks are to establish connection between terminals, and so the architectures were designed as location base network. The essential demand of the users of the network, however, is to retrieve desired information or data from the network. Therefore, Future Networks should be designed so that the user can easily retrieve data regardless of its location.

Social-economic awareness

Future Networks should have social-economic incentives to reduce barriers to entry for the various participants of telecommunication sector. Also, each participant should be able to receive proper return according to their contribution.

8. Design Goals

FN should support capabilities described below to realize the objectives mentioned in Chapter 6. A single FN may support all of the capabilities, or it may support some of the capabilities. It should be noted that some of the capabilities are extremely difficult to support in a single network. Whether these capabilities are mandatory or optional is for further study.

8.1. Energy Saving

FN should have device, system, and network level technologies to improve power efficiency and to reduce unnecessary traffic. These technologies do not stand alone, but cooperate each other as a total solution for power saving of networks.

Explanation: FN should provide a solution for environmental issues. Among environmental issues, here we focus on power saving of networks themselves on various technology levels.

In the future, the maximum bandwidth of user used will be increased with the appearance of various new services and applications. In the future, network has the possibility that cannot offer services because the transmission capacity of networks exceeds the physical limit which includes capacity of optical fibre, operation frequency of electrical devices and power consumption especially.

From the view of power reduction of devices, we can use the process integration of electrical devices, but this approach has some problem such as high standby power and physical limit of operation frequency. Therefore not only devices level approach, such as power reduction of electrical and optical devices, but also system level and network (architecture) level approaches are indispensable.

Networking nodes such as switches and routers should be designed considering smart sleep mechanism like existing mobile phones. This is an example of system level approaches. As for network (architecture) level approaches, energy effective traffic control should be considered. Routing method which reduces peak amount of traffic, caching and filtering which prevent unnecessary data transmission are typical examples of them.

These devices level, system level and network level energy saving considering both improving power efficiency and reducing unnecessary traffic are the key of energy saving of future networks.

8.2. Service Diversity

FN should accommodate a wide variety of traffic and support diversified network services and applications. FN should support a huge number and wide variety of terminal devices.

Explanation: In the future, network services and applications will become diversified with the appearance of various new services and applications that have quite different characteristics such as bandwidth, latency, and security level. Future network services will include those ranging from mission-critical ones to less important data transmission ones. Therefore, future networks should support various services that require a wide variety of QoS, security, reliability, and availability levels.

In addition, FN will need to support a huge number and a wide variety of terminal devices and have flexible mobility to achieve an all-encompassing communication environment. Especially in the field of ubiquitous sensor networks, there will be a huge number of networked devices such as sensors and IC tag readers that communicate using very small bandwidth. On the other hand, there will be some high-end application such as high quality video conference application with high realistic sensation. These terminal systems may be not so many, however huge bandwidth will be required for the communication. Major network services and applications of current Internet will obviously grow in the future.

8.3. Programmability for Service Awareness

FN should have capability to support and sustain new technologies derived from future user demands. For this, FN should have programmable network architecture that enables implementation of various types of network service.

Explanation: FN should be able to accommodate both established and experimental technologies and should enable migration between different types of network services. These technologies should be laid on the single Future network infrastructure without interferences between each other. Future network is expected to have environment to operate various network services. For example, video trans-coding and/or aggregation of sensor data in network processing could be possible. New protocol implementation for new type of service may also be required.

8.4. Data-Oriented Design

EdNote: Candidates for the title are: information, media, data, content, knowledge.

FN should enable users to access desired data easily, quickly, and accurately. FN should handle enormous amounts of data or contents efficiently and safely.

Explanation: The main purpose of legacy telephone networks was to connect two or more subscribers to enable them to communicate. The Internet as well as TCP/IP based packet networks, were designed for transmitting data between specified locations such as those of clients and servers. Currently, various network applications are provided as Web services. Most Internet users search for desired digital contents or services by using certain keywords at the beginning of the search. Then they access the data or contents by making use of appropriate Web services. In general, it can be said that networks will be used mainly as a tool for accessing certain data or contents. In the future, network users should be able to access desired data easily without tremendous and difficult procedure. FN should provide quick data search and transmission. In addition, accuracy and correctness of the data itself is also important.

The future will see explosive growth in the amount of digital content accessed, e.g., CGM (Consumer Generated Media). Some quasi-real-time messaging applications provided by SNS (Social Networking Services) will create huge volumes of blog articles instantaneously. In addition, ubiquitous sensor networks will continuously generate huge amounts of digital data second-by-second. When we get some data through the current Internet, we need to find address and port number of the host which can provide the target data. More simple and efficient networking technology dedicated for data handling will be expected in the future.  Some of this data and content related to privacy or digital assets will require high-performance security mechanisms. In order to handle these data safely, security issues will be essential in FN.

8.5. Accessibility/Reduction of Digital Gap  (EdNote: Proper title is needed.)

FN should facilitate and accelerate the provision of convergent facilities in various areas such as town or countryside, developed or developing countries.

Explanation: FN should be designed to reduce its life-cycle costs of telecommunication providers, in particular its deployment and management costs. FN should support simple design in terms of provisioning, operation and management. FN should be designed for easier development and manufacturing of infrastructure. Multi-owner, multi-layer and multi-technology principles should be substantially implemented.

EdNote: The detail explanation will be provided by original contributors.

8.6. Economic Incentives

FN should provide mechanisms to exchange incentives between various participants, e.g., users, telecommunication providers, governments, IPR holders.

Explanation: Participants of FN could be grouped in terms of industrial fields and/or nations. Firstly, in terms of industrial fields, participants could include users, commercial ISPs, private sectors network providers, governments, intellectual property rights holders, and providers of content and/or higher level services.[1] Secondly, in terms of nations, participants could include the telecommunications sector in not only developed but also developing countries so that operation, provisioning and management capabilities of FN would be simple enough to be supported by all participants. This also means that FN should be deployable as well as operable even in a less economic attractive area. Barriers to entry for participants would be almost nonexistent in FN.

EdNote: The detail explanation will be provided by original contributors.

8.7. Network Management

FN should be able to operate the complicated networks efficiently and economically for reducing the OpEx (Operation Expense) by designing the common interface of operation and management system. FN should be able to monitor and acquire accurate and real-time information of the network and service with complete, consistent, unambiguous, correlated, and filtered management data. FN should also support statistical intelligent learning mechanisms to process massive management data and information. FN should support network and service management automation such as self-stabilization and self-management functions.

Explanation: FN will be large-scaled and complicated for supporting various services with different characteristics. Therefore network infrastructure and network service management in the future will become more complicated and hard task. In previous network systems, operation, management and maintaining system has been designed and constructed in a manner specific to each other because of economical problems. Proliferation of management functionality increases complexity and operational cost. For this reason, integrated and unified in-built functionality will be needed. So FN should support false-positive and negative free fault detection, diagnosis, and isolation of network and service resources from the view point of self-stabilization. FN should support effective utilization of networked ICT resources by controlling the resources according to changes in demand from the view point of self-management. Furthermore, the dependency of the network operation and management to the skill of network manager, so how to make easy network management tasks and inherit to worker’s knowledge is large problem. However, in the process of network management and operation, there will remain the tasks which require human’s skill such as high-level decision based on accumulated know-how. For these tasks, it is important that even novice operator can manage large scale network easily without special skills. In addition, at the same time, effective inheritance of knowledge and know-how should be well considered.

8.8. Mobility

FN should provide mobility architectures that facilitate dynamic control and management, and high levels of reliability, availability and quality for the dynamic nature of Future Networks environments, where a huge number of terminals can be dynamically moved across the heterogeneous networks.

Explanation: Mobile Networks are continuously evolving by incorporating new technologies. Thus, Future Mobile Networks are expected that it will consist of combination of heterogeneous networks which range from macro to micro, pico and even femtocell and diverse types of terminals with multiple interfaces, since a single access network cannot provide ubiquitous coverage and continuous high QoS level communications [4]. From the this prospective, seamless mobility over heterogeneous mobile networks and  spectrum efficiency which equates to the maximum number of terminals per access network that can be provided while maintaining an acceptable QoS are considered as the requirements of  Future Mobile  Networks.

Therefore, considering mobility in the Future Networks, highly scalable architecture for distributed access nodes, a creating mechanism of operator manageable distributed network, and route optimization for application data and signalling data should be supported regardless of wireless system.

8.9. Identification

FN should provide a new identity structure, which specifies how to identify/locate/access communication objects and communicating objects.

Explanation: Internet was originally designed under limited assumptions, e.g. fixed-oriented, single interface, and IP address has been used as almost a single identity (or identifier) of Internet over most layers. Future networks are expected to have quite different features from the original assumptions of Internet. First of all, it will be mobile-oriented environment according to current ubiquitous trend. Also multi-homing will be a very common requirement. In addition, note that content-centric network is currently considered as promising candidate architecture for future Internet, in which communication is a matter of contents, not of nodes. The envisioned future network environments are a background why we should consider future Internet in revolutionary manner rather than evolutional one.

EdNote: Modifications for this section will be provided by the original contributor in next meeting.

8.10. Reliability and Security

FN should support services that require extremely high reliability and accurate time and location information. FN should also be equipped with advanced security mechanisms that are effective against distributed attacks, tapping, impersonation, etc. FN should be able to manage digital assets such as digital content copyrights.

Explanation: FN should support any kind of mission critical services such as intelligent traffic (road-, air-, marine- and space traffic), smart-grid, e-health, e-security, etc. In these services, devices will communicate to ensure the safety of humans and to enable the automation of human activities (driving, flying, office-home control, medical inspection and supervision, etc.). This is extremely important in disaster situations (earthquake, military or other confrontations, natural disasters, mass traffic collisions, etc.) where a huge number of devices or humans are affected or by remote operation.

Emergency situation also requests time and location information with associated accuracy information (for time and location coordinates). This will dramatically improve the service in a disaster/emergency environment.

The privacy of human and machines/objects/devices (we still do not have a consistent policy for all of these) should be ensured with a multilayer identification scheme. For these reasons, FN should have information about network-device identification, location and time, including accuracy (“location stamp”) available for safety applications.

EdNote: The explanation regarding security needs to be added.

9. Promising Technologies

This section describes some of the promising technologies that are emerging in the recent research efforts. These technologies are likely to be used as an enabling technology for FNs and may play an important role in development of FN. It should be noted that most of the technologies are in their early research stage, and the success of these technologies cannot be accurately projected at this time.

9.1. Network Virtualization

The FN should provide a broad range of applications, services, and network architectures and network virtualization is one of the key technologies to support diversity of applications, services and architectures. The logically isolated network partitions created by network virtualization are independently customizable and can utilize different applications, services, and architectures while sharing physical network infrastructures [1][2].

The definition and framework of network virtualization are described in [3]. Network virtualization is the technology that enables the creation of logically isolated network partitions over shared physical network infrastructures so that multiple heterogeneous virtual networks can simultaneously coexist over the shared infrastructures. Also, network virtualization allows the aggregation of multiple resources and makes the aggregated resources appear as a single resource.

The logically isolated network partitions can be completely isolated each other, users of logically isolated network partitions can program the network elements on any layers by leveraging programmability that enables users to dynamically import and re-configure new invented technologies into virtualized equipments (e.g., routers/switches) in networks. Another property of network virtualization is aggregation of multiple network elements in order to obtain increased capability and federation of networks so that multiple networks can be operated as being part of a single network with sharing network resources, even though the networks are geographically dispersed and managed by different providers. In order to support programmability and federation, it is necessary to support dynamic movement of logical network elements, services and capabilities among the logically isolated network partitions. The dynamic movement of virtual entities is defined as virtual mobility [4] and is one of the key features that enable the creation of logically isolated network partitions with sharing network resources which are not only physical resources but also virtual resources and allocating programmable functions. In other words, it is possible to remove a service or an element in logically isolated network partitions and reoffer it in a different network partitions in order to provide the continued service or connection to the end users. By doing so, the end users are able to locate and access such remote services and elements.

9.2. In-system Network Management

In the future, network will be large-scaled and complicated for supporting various services with different characteristics, so network infrastructure and network service management will become more complicated and hard task. Previously, various approaches have been proposed to standard the network management system by defining the common interface for operation system such as SOA (Service Oriented Architecture) concept and so on, but not operated due to various problems such as cost and so on. In the future, there is the possibility not to manage the networks due to increase of different management systems caused by increase of services, so new operation and management technologies are needed. Furthermore, the dependency of the network operation and management to the skill of network manager, so how to make easy network management tasks and inherit to worker’s knowledge is large problem.

EdNote: Is this expert system to aid operation or sophisticated UI for novice operators? Original contributor needs to clarify this.

For resolving the above problems, FN should consider two functions.

First is ‘Unified operation and management system’ from the view point of high-efficient management, the other is ‘Sophisticated control interface and inheritance system of operator knowledge and know-how’ form the view point of skill free network.

FN has new function which is different from current networks mainly in the following points.

- Unified operation and management system [1]

This system provides the high-efficient operation for adapting all of network systems which provide different services. Unified: system? Interface?

- Sophisticated control interface and inheritance system of operators knowledge and know-how [2][3]

In order to control and manage various networks and network services easily, operation system for FN should have autonomous control and self-stabilizing mechanisms at a certain level. In the future, even novice worker should be able to control and manage target network without special skill. For some network management tasks which should be done manually by human, sophisticated and friendly control interface should be designed. One of the reasonable approaches is ‘Visualization’ of various statuses of network as follows;

(Visualization of system management (Software technology level)

Network visualizing technology supports the work of system administrator and improves the work efficiency by visualizing the state of network easily. Visualizing technology includes monitoring of networks, fault localization and network system automation. It will be important and necessary technology for managing and maintaining the FN which will be expected to become large-scaled and complicated more and more.

(Visualization of infrastructure management (Hardware technology level)

It is important to construct the network system configuration and the work’s environment in which the field workers can work efficiently. Hardware technology based on visualization includes monitoring of fibre and states of communications, fault localization and fibre identification without high level technical skill and experiences of field workers.

In addition, database construction technology for succeeding worker’s knowledge and know-how which based on knowledge and experience is needed.

9.3. Energy Saving of Networks

Ways of resolving environmental issues that include reduction of GHG (Greenhouse Gas) emissions are becoming increasingly important [1]. The use of networks is considered a prospective means to reduce GHG emissions in various fields, such as telework and supply chain management (SCM). However, as networks carry more traffic, their electric power consumption will increase [2]. Future Networks should provide technologies that contribute to environmental conservation from network perspective.

In this context, energy saving of networks means a set of technologies that reduce total power consumption of network equipments such as routers and switches systematically. It includes a variety of technologies: device level, system (equipment) level, and network level. Each technology does not stand alone, but cooperates each other among different levels as a total solution, in order to minimize total power consumption.

Energy saving of networks is distinguished from current networks mainly in the following three points:

( Forward the traffic with less power

Conventional data transmission is usually carried out with power-consuming devices and systems. On the contrary, energy saving of networks will transmit datawith less power, usinglow-power devices/systems, light protocol, and so on [3]. It reduces the necessary power to get unit data speed, that is, W/bps.

( Control device/system operation for traffic dynamics

Conventional network devices or systems always operate at full spec and full speed. On the contrary, energy saving of networks will control the operation of them according to the traffic, using sleep control, dynamic voltage scaling (DVS), dynamic clock operation technique, and so on [4]. It reduces total power consumption needed.

( Reduce the unnecessary traffic

Conventional network basically transmits all traffic as requested. On the contrary, energy saving of networks will have a capability to reduce unnecessary traffic. That is, it can reduce the unnecessary traffic such as excess keep alive messages and duplicate user messages on multicast, using filtering, caching, redirect, and so on. It reduces the maximum traffic, and then the total power consumption needed.

According to the above characteristics, energy saving of networks can reduce total power consumption, and can be one solution to environmental issues from network perspective.

9.4. Identification

With growth of Internet, it’s facing many problems which come from the limited ID capability and new protocols to solve them are being proposed. ID/Locator separation protocols, e.g. HIP [1], LISP [2], HIMALIS [3], are typical examples. However, note that those are only temporary solutions which are still based on existing Internet concept so we cannot fundamentally meet the requirements for future networks. That would be the background why future networks need development of new identification architecture.

Identification means what objects should be identified and how to identify the objects for communication. Its scope includes structure of identifiers, their formats and relevant processes. In addition, note that identification should be a global issue to make global communication possible.

Identification in future networks is distinguished from existing Internet, especially in the following points:

EdNote: Needs to clarify the standpoint of view. Standpoint means e.g., difference from NGN or the Internet, providing particular service such as telephony, such and such. This will clarify the difference with existing technologies as well as the necessity/motivation of the new identification system.

EdNote: One way might be Alex’s comment (service is important in FN), and the other may be Keith’s last comment (current identification system is so limited, in FN we should expand the limitation)

- Mobile-oriented network environment

Internet was basically designed on the assumption of fixed environment. It is expected that future networks will be mobile-oriented network [4] and identification architecture of future networks should efficiently support the envisioned future environment.

- Multiple interfaces

Internet basically assumes single interface hosts. In future networks, multiple interfaces will be common. It means we need different approach from current Internet in which an IP address is allocated to a network interface rather than host itself.

- Content-centric networking

Internet is basically node-based communication. Content-centric network is currently considered as promising candidate architecture for future Internet, in which communication is a matter of contents, not of nodes [5]. How to identify the contents is an important issue in future content-centric network.

9.5. Mobility-enhanced Distributed Networking

In the current network, main functions such as physical mobility management, authentication, and application servers are installed in the centralized system for supporting mobility. Therefore, any data between end-user and application servers, and between end-users is exchanged through the centralized system, which is also known as the mobile core network. In this architecture, however, scalability issue will arise due to higher-speed access network and increase in the number of terminals. To address this scalability issue, a small and portable wireless access node has been drawing wide attention as an alternative access method especially for residential and enterprise deployment [3].

EdNote: Explanation of what the technology is, is needed.

In this context, mobility refers to the physical movement of the end users while continuing to be reachable for incoming requests and maintaining ongoing connections.

By flexibly locating functionalities, which conventionally resided in the mobile core network, at any part of the network in a distributed fashion, a highly efficient and scalable mobile network can be realized. To achieve this goal, the Future Networks should provide at least the following points:

- The Future Networks should support localization and optimization of the signalling and data paths.

- The Future Networks should enable the network administrator to control the signalling and data path

- The Future Networks should be able to locate the functional entities (e.g., mobility management) anywhere in the network (both in the mobile core and access networks).

- The Future Networks should be able to provide the discovery function (network resources and devices) of the connected devices in both centralized and distributed fashions.

- The Future Networks should be able to connect devices that are not fully capable of mobility and/or security without degradation of those features.

By supporting above functionalities, the Future Networks can provide always-on and always-best connected access with guaranteed end-to-end services.

EdNote: ‘Should’ is not appropriate for section 8 because this section is the one to describe candidate technology.

9.6. Self-optimization Networking

Maximum bandwidth of user used will be increased with the appearance of various new services and applications in the future. Furthermore, the differential of bandwidth used by each user, that is, the dynamic range of bandwidth among users will be expanded. But previous network was designed to meet maximum user needs, so equipment is over specified for most services, this leads to high energy consumption of networks. In the future, network has the possibility that cannot offer services because the transmission capacity of networks exceeds the physical limit which includes capacity of optical fibre, operation frequency of electrical devices, power consumption and so on.

For resolving the above problems, FN should adapt the diversification of applications, services and user demands efficiently. FN has three optimization techniques for reducing the network power consumption, offering E2E huge bandwidth services and realizing high-efficient use of network resources.

First is ‘Device level optimization’, second is ‘System level optimization’ and third is ‘Network level optimization’.

FN self-optimization network is quite different form current networks which were designed to maximum need mainly in the following points such as device, system and network level.

- Device level optimization [1]

This can introduce drastically power reduction of networks against the previous networks which were designed to meet the maximum user need, so equipment used in networks are over-specified for most services. Operation rate optimization technique provides the minimum bandwidth which can offer services and applications by using optical layer, electrical layer and optical/electrical hybrid technique.

- System level optimization [2]

This can realize the energy saving and huge bandwidth services with performance of high security, low latency, which is target for far future E2E all optical services. System level optimization includes following two technologies.

(System performance optimization

The power consumption of each node system is almost proportional to the number of in-service ports and the clock speed of processors within the node system. Moreover, the performance of the system is designed to support peak traffic demand, which is exaggerated specification under most of the time. In this optimization, the node system shuts off underutilized ports or reduces the operational clock speed of processors on the line cards in order to improve the efficiency of the system resources.

(Function level optimization

Previous network has the problem which cannot realize both the low latency and high security level, which is one of network functions, because of using higher layer processing with lower speed. Security level optimization realizes the high secure level using lower layer processing, that is, physical layer processing technique, so coexistence of low latency and high security is possible.

- Network level optimization [3][4]

This can solve the problem such as the physical limit which includes capacity of optical fibre, operation frequency of electrical devices. Furthermore, this technique has the possibility of high efficient use of network resources such as network path, equipments and so on.

What’s new needs to be clarified.

(Path optimization

Conventional network cannot offer the E2E all optical network services with high-speed, large capacity, and low latency and previous services such as voices, texts and so on by same network from the view point of economical, technical problems and so on. Path optimization technique provides the optimized path considering services characteristics and traffic conditions of transmission route. Furthermore, path optimization has the function of synchronizing the data, can offer the information which is consist of multiple data with different characteristics by using different path.

(Network topology optimization

A set of lower-layer (e.g., optical layer) paths forms a network topology to upper layer (e.g., packet layer). Upper-layer traffic is transported over the network topology, and the optimal topology can be determined by the geographical distribution of user’s traffic demand.

(Accommodation point optimization

In previous networks, all of services are accommodated in same point of network. So the accommodation efficiency decreases because each service has different characteristics such as bandwidth, latency and different usability. This technique provides the high-efficient network architecture which realizes the flexible accommodation for adapting services using the advantage of the optical characteristics, which also leads to energy saving of networks.

9.7. Data-oriented Networking

EdNote: Clarification of term ‘data’ is needed to avoid confusion with voice/data terminology.

EdNote: We should avoid to use specific projects names as much as possible, to align this other sections.

The explosive growth of the World Wide Web in the Internet has caused a large volume of distribution of digital content such as texts, pictures, audio data, and video data. A large portion of Internet traffic is derived from this content. Therefore, several networking methods focusing on data/content distribution have been proposed. These include so-called Content Distribution Networks (CDNs) and Point-to-Point (P2P) networking for content sharing. In addition, some novel approaches specializing in data/content handling have been proposed. Content Centric Networking (CCN) is a new approach from the perspective of network usage [1][2]. It is distinguished from existing networks in the concepts of routing and security. Where the routing mechanism of current networks depends on ‘location’, routing of CCN is based on content name. CCN also proposes a network-wide caching mechanism. All CCN contents have a public-key signature and can prove their propriety by themselves (Content Based Security). Currently, CCN is evolving into Named Data Networking (NDN) that includes a wider range of networking concepts[3].

The Data Oriented Network Architecture (DONA) proposes data centric networking that emphasizes naming and name resolution of data in the network [4]. CCN assumes overlay implementation using existing IP networks. DONA assumes a new implementation base in a clean-slate manner.

The European FP7 4WORD project includes a research project for the future Internet named “Network of Information (NetInf)”[5][6]. This project takes a new approach based on an information centric paradigm that solves current Internet problems. The “PSIRP” project is another, related approach to information centric networking[7][8]. It focuses on data flow over networks and proposes a new paradigm called “publish/subscribe(pub/sub) networking”. In pub/sub networking, data senders “publish” what they want to send and receivers “subscribe” to the publications that they want to receive. The goal of these two research projects is creating new network architectures for the future based on contents/data centric paradigms.

9.8. Programmable Network supporting Economic Incentives

Ways of resolving economic tussles in cyberspace that include the economic reward for each participant’s contribution are becoming increasingly important [1]. The use of networks is considered a means to produce economic incentives in various fields as the Internet is growing and puts together diverse social functionalities. Different participants of the Internet are often pursuing interest that conflicts with others. These have led tussles over the Internet and international/domestic regulation issues are in a controversy. Future Networks should provide technology that supports ecosystem. However, as networks are ossified, economic value chain circulation is not supported technologically.

In this context, programmable network means a set of technologies that support network to be provided as users’ technical demand dynamically. It includes a variety of technologies: network virtualization, federation, programming interface, and network resource management. Each technology doesn't stand alone, but cooperates each other among different levels as a total solution, in order to program networks corresponding to diverse user demands.

Programmable network is distinguished from current networks mainly in the following points:

( Programming Interface

Conventional network devices operate with fixed specification. On the contrary, programmable network will provide programming interface so that the network can be dynamically programmed according to the user’s demand.

( Network Resource Control/Management for Dedicated Performance

Conventional network resource control/management does not fully support resource isolation when users demand specific performance. On the contrary, programmable network will provide network resource control/management for dedicated performance.

EdNote: According to the above characteristics, programmability of networks can solve the economic incentive issues, and can support ecosystem from network perspective.

Paragraph 1 and 2 does not flow.

As for the Network resource Control/management bullet point, it needs to clarify who is the user of the programmability, and what is the relationship of it with economic incentives.

10. Target Date

The estimated target date for prototyping and phased deployment of Future Networks should roughly fall between 2015 and 2020. This estimate is based on two factors: First, the status of current and evolving technologies that would be employed in the experimentation and development of FNs. Second, any novel development that might take place well beyond that estimate is too speculative and is outside the mandate of this document.

Any global multi-service infrastructure comprises a number of networks and network technologies arranged in various vertical (stacked) and horizontal (peered) combinations.

The nature of such a federated network implies a mixture of networks at different stages of evolution. Some existing components may be replaced by a new network technology, some may be enhanced by a future technique, and completely new ones may be added.  Additionally, the network components will vary dynamically from one telecommunication instance to another depending on the service under consideration, features invoked and related routing choices.

Various evolution and migration strategies may be employed to accommodate emerging and future network technologies.  Each case will be to be examined on its merits and its relation to the role played by the network technology under consideration as part of the future global infrastructure.

Appropriate usage scenarios and deployment cases will need to be considered when the research has been completed for the area(s) under consideration, and appropriate conclusions reached and agreed.

Bibliography

EdNote : The numbering of each items in this bibliography and the main body text will be corrected in the final version of this document.

[1] Recommendation ITU-T Y.2001 (2004), General overview of NGN.

[2] National Institute of Information and Communications Technology, Vision and Technology Requirements for a New-generation Network, February 2009.

[3] European Comission, Future Internet 2020: Visions of an Industry Expert Group, May 2009.

[4] Olabisi E. Falowo and H. Anthony Chan, "Effect of mobile terminal heterogeneity on call blocking/dropping probability in cooperative heterogeneous cellular networks," Telecommunication Systems, June 2010.

[1-1] Jeong, S. and H. Otsuki, "Framework of Network Virtualization", ITU-T Focus Group on Future Networks , FGFN-ODxx, December 2010.

[1-2] Oliver Bohl , Shakib Manouchehri , Udo Winand, "Mobile information systems for the private everyday life," Mobile Information Systems, December 2007

[2-1] “The NGOSS approach to Business Solutions,” Tele Management (TM) Forum, Release 1.0, 2005.

[2-2] D.C.Kilper et al.,”Optical Performance Monitoring,” J.Lightwave Technol., vol.22, pp.294-304, 2004.

[2-3] T.Kubo et al.,”In-line monitoring technique with visible light form 1.3(m-band SHG module for optical access systems,” Optics Express, vol.18,  no.3, 2010.

[3-1] International Telecommunication Union, "ICT and Climate Change", April 2008

[3-2] M. Gupta and S. Singh, "Greening of the Internet", Proc. ACM SIG-COMM '03, August 2003

[3-3] J.Baliga et al., "Photonic Switching and the Energy Bottleneck", Proc. IEEE Photonics in Switching, August 2007

[3-4] J. Chabarek et. al., "Power Awareness in Network Design and Routing", in Proc. IEEE INFOCOM '08, April 2008

[4-1] http://datatracker.ietf.org/wg/hip/

[4-2] http://datatracker.ietf.org/wg/lisp/

[4-3] Ved P. Kafle and Masugi Inoue, “HIMALIS; Heterogeneous Inclusion and Mobility Adaption through Locator ID Separation in New Generation Network,” IEICE Trans. Com., Vol. E93-B, March 2010

[4-4] Report of the Task Force on Interdisciplinary Research Activities applicable to the Future Internet, Version 4.1, July 2009

[4-5] http://www.ccnx.org/ (?)

[5-1] Olabisi E. Falowo and H. Anthony Chan, "Effect of mobile terminal heterogeneity on call blocking/dropping probability in cooperative heterogeneous cellular networks," Telecommunication Systems, June 2010

[5-2] Oliver Bohl , Shakib Manouchehri , Udo Winand, "Mobile information systems for the private everyday life," Mobile Information Systems, December 2007

[5-3] Tsunehiko Chiba and Hidetoshi Yokota, "Efficient Route Optimization Methods for Femtocellbased All IP Networks," WiMob 09', Octerber 2009

[6-1] H.Kimura et al.,”A Dynamic Clock Operation Technique for Drastic Power Reduction in WDM-based Dynamic Optical Network Architecture,” in Proc. S07-3, World Telecommunication Congress (WTC), 2010.

[6-2] C.Gunaratne et al.,”Reducing the energy consumption of Ethernet with adaptive link rate (ALR),” IEEE Trans. Computers, vol.57, no.4, pp.448-461, Apr. 2008.

[6-3] Jayant Baliga et al.,”Energy Consumption in Access Networks,” OFC’2008, OThT6, 2008.

[6-4] N.Iiyama et al.,”A Novel WDM-based Optical Access Network with High Energy Efficiency Using Elastic OLT,” in Proc. ONDM’2010, 2.2, Feb.2010.

[7-1] Project CCN http://www.ccnx.org, Sep. 2009.

[7-2] V. Jacobson, D. K. Smetters, J. D. Thornton, M. F. Plass, N. H. Briggs, and R. L. Braynard (PARC) Networking Named Content, CoNEXT 2009, Rome, December, 2009.

[7-3] http://www.named-data.net/

[7-4] T. Koponen, M. Chawla, B. Chun, et al, “A data-oriented (and beyond) network architecture,” ACM SIGCOMM Computer Communication Review, Volume 37, Issue 4, pp 181-192, October 2007.

[7-5] http://www.netinf.org/home/home/

[7-6] C. Dannewitz, "NetInf: An Information-Centric Design for the Future Internet", In Proc. 3rd GI/ITG KuVS Workshop on The Future Internet, May 2009.

[7-7] M. Särelä, T. Rinta-aho, and S. Tarkoma. RTFM: Publish/Subscribe Internetworking Architecture. In ICT-MobileSummit, 2008.

[7-8]http://www.psirp.org/home

____________