RECOMMENDATION  ITU-R  BT.1124-2

REFERENCE  SIGNALS  FOR  GHOST  CANCELLING  IN
ANALOGUE  TELEVISION  SYSTEMS

(Question ITU-R 55/11)

(1994-1995-1998)

Rec. ITU-R BT.1124-2

The ITU Radiocommunication Assembly,

considering

a)	that a ghost cancelling system using a ghost cancelling reference (GCR) signal is one of the most effective countermeasures for ghost images in individual and collective antenna reception of television signals;

b)	that the system should be effective for cancelling multiple and long delayed ghost images as well as short delayed ghost images and it should be also effective for leading ghosts and waveform equalization of video signals;

c)	that the GCR signals can be inserted into the lines in the vertical blanking intervals;

d)	that for each television system an appropriate GCR signal can be defined;

e)	that for each country the appropriate GCR signal can be used to suit the various propagation conditions and the types of transmission media;

f)	that the ghost canceller using the GCR signals can be manufactured at a reasonable cost;

g)	that the cost of ghost cancellers may be lower if there is widespread use of a common GCR signal,

recommends

1	that the GCR signal should be a dedicated reference signal optimized for ghost cancelling;

2	that the GCR signal should allow the rapid determination of the channel response even under poor signal-to-noise conditions;

3	that the GCR signal must be able to provide a flat amplitude and linear group delay response versus frequency over the entire passband of each system;

4	that the GCR signal should make efficient use of the vertical interval resources;

5	that for NTSC, PAL and SECAM television systems, a broadcaster wishing to integrate a GCR signal should use a GCR signal complying with the specifications given in Annex 1 for:

–	GCR signal A,

–	GCR signal B,

–	GCR signal C;

6	that for new GCR applications for NTSC, PAL or SECAM, GCR signal C should preferably be used;

7	that for advanced analogue television systems, a broadcaster wishing to integrate a GCR signal should use a GCR signal complying with the specifications given in Annex 2 for:

–	HD-MAC, D-MAC and D2-MAC;

–	MUSE.

ANNEX  1

GCR signal specifications for conventional TV systems

1	Introduction

GCR Signal A for use with the NTSC system, was recommended by ITU-R in 1994 and has been used extensively in Japan since 1989.

GCR Signal B was recommended by ITU-R in 1994 and has been used extensively with the NTSC system in Korea since 1993.

GCR Signal C for use with NTSC, PAL, and SECAM system is being adopted by broadcasters in many countries now introducing GCR signals.

1.1	GCR Signal A

Requirements for the GCR signal relevant to the NTSC system are specified in Tables 1 to 4 and Figs. 1 to 3.

TABLE  1

Specification of GCR waveform

|  | Value | Remarks |
| --- | --- | --- |
| Amplitude | 70 2 IRE | Difference between setup level and the centre point level of the GCR waveform. |
| Setup | 0 2 IRE |

Difference between blanking level and pedestal level of the active line.

| Difference between line A and line B should be 0.5 IRE or less. |
| --- |
| Width | 160 1.0 sc(1) (44.7 0.28 s) | Measured at 50% value of the GCR amplitude. |
| Start of GCR | 60 1.5 sc(2) (16.76 0.42 s) | GCR rising edge timing (50% point) with respect to leading edge of line sync. |
| Rising edge | Integrated sin(x)/x | See equation below. |
| Trailing edge | 0.25 0.05 s (2T bar) | Interval between 10% point and 90% point of the GCR amplitude. |

(1)	sc - Sub-carrier cycles (one colour subcarrier cycle: 1/3.579545 s).

(2) Specified at the output point of the GCR signal generator. Not specified at the output point of the GCR inserter unless necessary.

(1)

where A is a normalizing factor (A = f ()),  = 2  4.177447  106, and h (x) is a window function to give the signal spectrum as shown in Figure 4, such as raised cosine having the half amplitude width of 10.5 s.

The characteristics are applied to the differential or one-sample difference of the GCR signal.

TABLE  2

GCR Insertion line

| Insertion line numbers | 18 and 281 |
| --- | --- |

TABLE  3

Signal on the line immediately preceding the GCR line

| Field numbers |
| --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| x1 | x2 | x3 | x4 | x1 | x2 | x3 | x4 |
| x1, x2, x3 and x4 should not contain time varying information. |

TABLE  4

GCR transmission sequence

| Field number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Waveform | line A | line B | line A | line B | line B | line A | line B | line A |

1.2	GCR signal B

Requirements for the ghost cancelling reference signal relevant to the 525-line NTSC and 625-line PAL systems are specified in Tables 5 to 8 and Figures 4 and 5.

TABLE  5

Ternary sequence of length 366

| 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | –1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | –1 | 0 | 1 | 0 | 0 | 0 | –1 | 0 | –1 | 0 | 1 | 0 | 1 | 0 |
| –1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | –1 | 0 | –1 | 0 | –1 | 0 | –1 |
| 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | –1 | 0 | 1 | 0 | –1 | 0 |
| 1 | 0 | –1 | 0 | –1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | –1 | 0 | –1 |
| 0 | 1 | 0 | 1 | 0 | –1 | 0 | –1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| –1 | 0 | 1 | 0 | –1 | 0 | –1 | 0 | 1 | 0 | –1 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 |
| -1 | 0 | 0 | 0 | -1 | 0 | 0 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 |
| 0 | -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 |
| -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 |
| -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | 1 |
| 0 | -1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 |
| -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | 0 | 0 | -1 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 |
| 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | -1 | 0 | 1 |
| 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 |
| 1 | 0 | 0 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 |
| 0 | -1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 |
| 1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 |
| 0 | -1 | 0 | -1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |
| -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | -1 |
| 0 | 1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 | 0 |

TABLE  6

Specifications of GCR waveform

|  | Television system | 525-line | 625-line |
| --- | --- | --- | --- |
|  | B, G | D, K |
| 1 | GCR signal frequency limit | 4.18 MHz | 5.0 MHz | 6.0 MHz* |
| 2 | Pedestal height | 30 IRE | 300 mV |
| 3 | Start of pedestal** | 8.75 (s | 10.5 (s |
| 4 | Finish of pedestal** | 61.9 (s | 62.5 (s |
| 5 | Start of GCR** | 11.5 (s | 12.2 (s |
| 6 | Duration of GCR | 25.6 (s | 20.6 (s |
| 7 | Lowest level of GCR | -10 IRE | 0 mV |
| 8 | Highest level of GCR | +70 IRE | 600 mV |
| 9 | Clock frequency*** | 4 x 3.58 MHz | 4 x 4.43 MHz |

*	The 6 MHz option is not compatible with transmission of NICAM digital sound using a 5.85 MHz carrier.

**	The start and finish times are defined at the half-amplitude points.

*** This refers to the use of a clock at four times the colour subcarrier frequency of NTSC or PAL, as appropriate.

TABLE  7A

Transmission sequence of NTSC GCR signal

| Field number | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| GCR signal polarity | + | - | + | - |

TABLE  7B

Transmission sequence of PAL GCR signal*

| Field number | 2 | 4 | 6 | 8 |
| --- | --- | --- | --- | --- |
| GCR signal polarity | + | - | + | - |
| * There is no absolute relationship between the polarity of the GCR transmission sequence and the eight-field sequence of PAL. |

TABLE  8

The frequency values in Figure 4

| TV system | 525-line | 625-line |
| --- | --- | --- |
| Frequency |
| B, G | D, K |
| f1 (MHz) | 1.00 | 1.00 | 1.00 |
| f2 (MHz) | 3.58 | 4.43 | 4.43 |
| f3 (MHz) | 4.09 | 4.80 | 5.80 |
| f4 (MHz) | 4.18 | 5.00 | 6.00 |
| f5 (MHz) | 4.25 | 5.20 | 6.20 |

FIGURE  4

Frequency characteristic of the lowpass filter

FIGURE  5A

Positive GCR signal for 525-line systems

FIGURE  5B

Negative GCR signal for 525-line systems

FIGURE  5C

Positive GCR signal for 625-line systems (5 MHz)

FIGURE  5D

Negative GCR signal for 625-line systems (5 MHz)

FIGURE  5E

Positive GCR signal for 625-line systems (6 MHz)

FIGURE  5F

Negative GCR signal for 625-line systems (6 MHz)

1.3	GCR signal C

Requirements for the ghost cancelling reference (GCR) signal are described below. Specific parameters for 525- and 625-line NTSC, PAL and SECAM television systems (see Note 1) are set out in Table 9.

TABLE  9

| Television system |
| --- |
| 525-line | 625-line |
| f1 | GCR signal frequency limit | 4.1 MHz | 5.0 MHz(1) |
| f2 | GCR signal frequency stop limit | 4.3 MHz | 5.2 MHz |
| V1 | Pedestal height | 30 IRE | 350 mV |
| T1 | Start of pedestal | 9.5 ms | 10.5 ms |
| T2 | Finish of pedestal | 58.5 ms | 62.5 ms |
| T3 | Duration of GCR | 35.5 ms | 23.2 ms |
| T4 | Start of GCR | 12.0 ms | 12.2 ms |
| T5 | First peak of GCR | 16.7 ms | 15.8 ms |
| V2 | Lowest level of GCR | -10 IRE | 0 mV |
| V3 | Highest level of GCR | +70 IRE | 700 mV |
| GCR polarity: |
| Line A | Normal | Normal |
|  | Line B | Inverted | Inverted |
| GCR transmission sequence(2): |
| Field 1 | Line A | –(3) |
|  | Field 2 | Line B | Line A |
|  | Field 3 | Line A | –(3) |
|  | Field 4 | Line B | Line B |
|  | Field 5 | Line B | –(3) |
|  | Field 6 | Line A | Line A |
|  | Field 7 | Line B | –(3) |
|  | Field 8 | Line A | Line B |

(1)	GCR signal for Recommendation ITU-R BT.470 system N.

For 625-line television system N, described in Recommendation ITU-R BT.470, the available vision bandwidth (4.2 MHz), is less than the bandwidth of the 625-line GCR (5.0 MHz). It is suggested that for television system N, the GCR signal described in this Recommendation for 625 line signals be used, but be band limited to the available vision bandwidth.

(2)	There is no absolute relationship between the polarity of the GCR transmission sequence and the eight-field sequence of PAL.

(3) The use of a field mode GCR signal for 625-line systems, in conjunction with appropriate receiving equipment might offer improved performance in the case of moving ghost signals. Further studies need to be conducted to investigate this possibility.

NOTE 1 – Correct operation of the motion adaptive Colour Plus (MACP) process used by the PALplus system relies on the fact that points separated by 312 lines within a frame have a precise phase relationship. In order to avoid disturbing this relationship, any changes to the equalization of the signal applied by a ghost canceller located in either the transmission or reception chain should preferably be made during the period of lines 624 to 22.

The GCR signal is placed on a single line in the vertical blanking interval, on one line per field in 525-line systems, and on one line per frame (two fields) in 625-line systems.

The GCR signal has a flat spectrum and high energy up to the frequency f1 and has low energy beyond the frequency f2. The values of f1 and f2 are shown in Table 9. Figure 6 shows the spectrum of the GCR signal. The normalized GCR signal as a function of time is shown in Fig. 7.

In 525-line systems, the GCR signal is placed on line 19 (and the corresponding line in the following field). In 625-line systems, the GCR signal is preferably placed on line 318, with the preceding line 317 containing no time-varying information. For both 625- and 525-line systems the line immediately preceding the GCR line should preferably not contain time varying information to avoid constraining the performance of ghost cancellers.

| To provide efficient cancellation of 625-(525)-line systems requiring post ghost cancellation ranges greater than approximately 38 (31) m |  |  |  |  |
| --- | --- | --- | --- | --- |