RECOMMENDATION  630*

MAIN  CHARACTERISTICS  OF  TWO  FREQUENCY
SHIPBORNE  INTERROGATOR  TRANSPONDERS  (SIT)

(Question 28/8)

(1986)

Rec. 630

The CCIR,

CONSIDERING

(a)	that the use of a secondary radar system would increase the ship's radar range and improve radar discrimination of vessels in the presence of interference;

(b)	that the use of a secondary radar system would make it possible to identify individual ships and to obtain navigational and other data from an interrogated vessel;

(c)	that the combined use of a secondary radar system and of an automatic radar plotting aid (ARPA) would enhance the efficiency of the latter by increasing the range, the noise immunity of the reply co-ordinate signal and absence of fluctuation in its amplitude;

(d)	that in view of CONSIDERINGs (a), (b), and (c), the use of a secondary radar system would help to improve the safety of shipping and the economics and efficiency of shipping operations;

(e)	that in the design, preference should be given to a system using two-frequency interrogation consisting of a SIT interrogating signal and a shipborne navigation radar sounding pulse in the 3 cm band;

(f)	that the operation mode and the main operating characteristics of the system, as well as the main technical characteristics of the SIT, should be co-ordinated internationally by the users to ensure the compatibility of equipment manufactured in different countries,

UNANIMOUSLY  RECOMMENDS

that for the two-frequency SIT system operating in the 10 cm band and the 3 cm band, designed to ensure safe passage of ships and regulation of the movement of ships from a central point:

–	the operating modes should conform to Annex I,

–	the operating characteristics should conform to Annex II,

–	the technical characteristics should conform to Annex III.

ANNEX  I

OPERATING  MODES

| Interrogation |
| --- |
| Response |
| Type of | Address | Content | Capacity | Data input | Reflection |
|  | working |
|  | Type | Location |
| All ships | All ships | Polar ship co-ordinates | – | – | Screen blip | PPI radar screen |
| Selective I | Ship selected by operator | Ship station identity | 9 digit number | From continuous storage unit | Figures | Panel display |
| Selective II | Ship selected by operator | Heading Speed Manoeuvre | 3 decimal digits 2 decimal digits 1 decimal digit | From ship direction and speed sensors or manually | Figures | Panel display |
| Selective III-VI | Ship selected by operator | Determined in development of system | 6 digit number | From continuous storage unit or manually | Figures | Panel display |
| Note. – Blip on PPI radar screen is shown with all types of operation. |

ANNEX  II

MAIN  OPERATING  CHARACTERISTICS  OF
SECONDARY  MARINE  RADAR  SYSTEM

| Parameter | Value |
| --- | --- |

Range:

Minimum (m)

Maximum (raised antenna, height 15 m)
(nautical miles)

Resolution:

In direction (at a radar antenna radiation pattern of width 1°) (degrees)

In distance (m):

–	all ships operation
	–	selective operation

Distance of response signal from echo signal (m)

Error in determination of ship co-ordinates

£ 300


³ 010

£ 003

£ 200
£ 500

£ 200

Not worse than radar error

ANNEX  III

MAIN  TECHNICAL  CHARACTERISTICS  OF  SIT

| Parameter | Value |
| --- | --- |
| 10-cm band | 3-cm band |

Antenna:

Polarization

Radiation pattern (degrees):

In horizontal plane

In vertical plane

Transmitter:

Carrier frequency (MHz)

Impulsive power (W)

Length of pulse (ns)

Receiver:

Sensitivity (dBW)

Frequency band (MHz)

Vertical

360°

40°-60°

2940 ± 2

100-200

100 ± 20

Better than –115

2930-2950

Horizontal

360°

40°-60°

–

Better than –72

9320-9500

Bit rate (Mbit/s):

Of interrogating signal

Of response signal

Interrogating signal lead time relative to associated radar sounding pulse (ms)

2

3.3

14 ± 0.2

# Footnotes

*	The Director, CCIR, is requested to bring this Recommendation to the attention of the International Maritime Organization (IMO) and the International Association of Lighthouse Authorities (IALA).