Manufacturer: ABC Device name: XYZ Designation: 01-WB IMEI: 12345678910 SW version: 1.2.3.4 Audio Mode: Wideband Testing Date MM/DD/YY *informative

ITU-T P.505 “Quality Pie” chart for the wideband Bluetooth® test results of the ABC XYZ

Result summary based on P.1110 chapter 12 test cases (clockwise)

- As expected the AT+NREC=0 command is confirmed with “OK”.

- The roundtrip delay is within the required range.

- The setting of the phone’s volume control does not influence the measured JLR in receiving direction.

- The noise reduction is active although the AT+NREC=0 command was answered with “OK”.

- The echo canceller is switched off as required.

- The double talk test (“DT”) shows a transparent transmission in sending direction.

Note that this test is informative only but confirms that echo control has been deactivated as expected.

- The JLR of 0.3 dB measured in sending direction (“JLR (SND)”) indicates transparency and is within the recommended range of 0 ± 2 dB.

- The frequency response tolerance in sending direction (“SFR”) is violated.

- The linearity test in uplink indicates the presence of an active gain control.

- The listening quality in sending direction is slightly too low (“MOS-LQO SND”).

- The JLR of -0.1 dB measured in receiving direction (“JLR (RCV)”) indicates transparency and is within the recommended range of 0 ± 2 dB.

- The tolerance scheme for the receiving frequency response (“RFR”) is met.

- The linearity test in downlink indicates a level-transparent transmission.

- The listening quality in receiving direction is sufficiently high (“MOS-LQO RCV”).

Wideband results annex:

Roundtrip Delay:	153.4 ms (limit ≤ 190 ms)

| Sending Frequency Response (SFR) | Receiving Frequency Response (RFR) |
| --- | --- |
| Minimum distance -5.5 dB at 200 Hz | Minimum distance 1.0 dB at 6300 Hz |
| JLR SND: 0.3 dB | MOS-LQOw SND: 3.6 | JLR RCV: -0.1 dB | MOS-LQOw RCV: 3.9 |
| Noise Reduction Test | Echo Canceller Test (-16 dBm0, 20 dB simulated echo path) |
| *Instead of 5 ms |  |
| NR is enabled | EC is deactivated (20.3 dB) |

Additional informative test results:

Results measured without sending the “AT+NREC=0” command

| SFR |  | RFR |  |
| --- | --- | --- | --- |
| JLR (SND): | -7.5 dB | JLR (RCV): | 1.7 dB |
| Noise reduction: | enabled | Echo canceller: | disabled |

Cross connection tests (WB Bluetooth® to WB vs. NB network connection)

(wideband analyses applied)

| SFR |  | RFR |  |
| --- | --- | --- | --- |
| JLR (SND, WB network): | 0.3 dB | JLR (RCV, WB network): | -0.1 dB |
| JLR (SND, NB network): | -0.6 dB | JLR (RCV, NB network): | -0.8 dB |

# Text boxes

Contact person:    Mr. Denis Andreev,  denis.andreev@ITU.int,                  phone +41 227305780

Mr. Marc Lepage,    marc.lepage@head-acoustics.de,   phone +49 2407 577-105

Mr. Frank Kettler,    frank.kettler@head-acoustics.de,    phone +49 2407 577-68