## Slide 1: ITU Workshop on “Voice and Video over LTE” Geneva, Switzerland, 1 December 2015
Considerations for end to end video quality QoE assessment as a means of verifying interoperability
Paul Coverdale
Consultant, Huawei Technologies Co. Ltd.
coverdale@sympatico.ca

## Slide 2: Outline
Background
Methodologies for assessing video QoE
Key requirements for an objective video QoE assessment tool
Current ITU-T Standards
Summary

## Slide 3: Background
Today LTE is deployed by 360 operators in 124 countries. Out of them, 80 operators are investing in Voice over LTE (VoLTE) and 14 have already launched VoLTE services.
But VoLTE also allows for video over LTE (ViLTE) with managed quality of service, since the network is managed by the operator allowing them to prioritize real-time communication over data and reserve resources for specific services.
But how to ensure interoperability of ViLTE among different service providers?

## Slide 4: Interoperability as perceived by the end-user
Important to consider interoperability from the viewpoint of the end-user
  They are the one who pays the bill
The need to reliably establish and close a video session is clearly important, but so also is the video quality (QoE) during the session

## Slide 5: Methodologies for assessing video QoE
In principle, assessment of Quality of Experience (QoE) for video (as for audio) must be performed using subjective tests, with metrics such as the mean opinion score (MOS)
However, it is also possible to estimate QoE based on objective measurements and associated quality estimation models
Subjective testing needs more resources and effort, because it requires human subjects, and is not so convenient in a live-service setting
Objective measurement and QoE calculation is generally much faster and more convenient, but the accuracy of the final evaluation depends on the accuracy of these models, and an understanding of the important human factors

## Slide 6: Evolution of Video Quality Experience: Different Screens, Services, and Networks
Interactive and immersed experience
Meeting basic requirements
Static 3DDynamic 3D (holographic)
1970s–1980s
1990s-2010s
2020s
Black&whiteColorful
VCR  8K
AnalogDigital
Plane  Stereoscopic
Multi-Screen Experience to Eye’s Extreme
(Scope of the current experience standards)
Live
TV call
surveillance
VoD

## Slide 7: Requirements for objective video QoE assessment
Research method
Subscriber survey
Determine top factors and their weights.
Human factor engineering experiments
Measure subjective perception.
ITU-T Recommendations
Determine the calculation method and formulae
Performance Metrics
Experience modeling
Measurement indicators
Network requirements
Network architecture
1
2
3
4
Network assessment
Planning guidance
Experience assessment
Continuous evolution
Application scenario
  Mobile network
  Fixed network
  Phone
  Pad
  TV
  BTV
  VoD
  Security surveillance
  Camera
  Video communication
Quantified collection

## Slide 8: Subscriber Survey, Highlighting Top 3 Factors That Affect User Experience
Subscriber survey
Determine top factors and their weights.
Focus group interview
Questionnaire
3000+ survey samples
Top 3 factors that affect user experience: video source quality, video loading speed, and video view experience
Video quality = Content quality (ultra HD, HD, and SD)
Initial loading = Content loading duration (initial channel zapping or VOD loading response time)
View experience = Broadcasted video quality (frame freezing or blocking)
Source: Huawei, UCD center, 2015
Weight importance
Note: A larger weight value indicates greater importance.
Interaction
Contents
Performance

## Slide 9: Video QoE Modelling
Interactive experience
0 damage
0 waiting
View experience
Top Three Factors for Video Experience
Viewing process
0 distortion
Video quality
High definition
High Frame rate
Video source
Color Gamut
Playback process
Zapping time
0 Blocking
0 Stalling
Initial Loading time
Experience
targets
Experience
factors

## Slide 10: Video QoE Assessment Panorama
  Interactive experience
Viewing experience
  Video quality
sQuality*
sInteraction
sView
Video MOS = f (sQuality, sInteraction, sView)
Video MOS modeling factors
Application scenario
  Mobile network
  Fixed network
Objective multi-screen, multi-network, and multi-service(BTV,VOD Video communication Video surveillance etc) video experience standard
  Phone
  Pad
  TV
  BTV
  VoD
  Security surveillance
  Camera
  Video communication
* s=score
Notes: IV : changes in GREEN

## Slide 11: Video Quality Factors: Definition, Motion, and Fidelity
Video quality
Interaction experience
Viewing experience
The frame rate affects video motion.
High fidelity means true colors, delicate pictures, and complete details.
Delicate
pictures
True
colors
Complete details
SDR
8 bits
HDR
10 bits
HDR
12 bits
8 bits
10 bits
12 bits
Rec. BT.709
8 bits
Rec. BT.2020 10 bits
Rec. BT.2020
12 bits
Maximum frame rates for screen sizes
Chart: 
屏幕最小分辨率 | 3557.8959 | 4489.3125 | 3187.8747 | 4554.1067 | 7590.1778
100"
41 cm
Typical viewing distance of a mobile phone with a 6" screen:
30 cm
Typical viewing distance of an iPad with a 9.7" screen:
60"
The definition depends on viewing angle and resolution.
2.5 m
42"
9.7"
6"
Typical viewing distance of a TV screen:
（Drama）
(Sports)

## Slide 12: Interactive Response Factors: Video Loading and Switching Duration
Video quality
Interaction experience
Viewing experience
100 ms = immediate response
1s channel switching
0.5s fast forwarding/rewinding
Interactive Operations and Acceptable User Experience
Ultimate Experience Objective: 0 Wait Time
2s video loading
Notes: IV : changes in GREEN

## Slide 13: Viewing Experience Factors: Erratic Display/Video Freeze
Video quality
Interaction experience
Viewing experience
Ultimate user experience: 0 occurrence of video freeze and erratic display
Source: DSL Forum TR-126
Current criteria (VOD freeze):
  VOD freeze duration on mobile phone/pad screens <= 10%
  VOD freeze duration on TV screens <= 1%
Current criteria (erratic display during live broadcast):
  Resolution higher than 720p: 1 erratic display/4 hours;
  Resolution lower than 720p: 1 erratic display/2 hours;
Ultimate experience: 0 erratic display/video freeze
  Same requirement for TV, mobile phone, and pad screens
Notes: IV: changes in GREEN

## Slide 14: Anticipated Video Service Experience Evolution
  Interaction experience
Viewing experience
  Video quality
2020+
2018
Now
  Number of erratic displays during a live video stream<= 2
  VOD freeze duration on mobile phone/pad screens <= 10% (within the 1-minute statistical period)
  VOD freeze duration on TV screens <= 1% (within the 45-minute statistical period)
  TV: 8k @ 240 fps, HDR, 12 bit, ITU-R Rec. 2020
  Mobile phone: 4k @ 120 fps, HDR, 12 bit, ITU-R Rec. BT.2020
  TV:
    channel switching time < 100 ms
    Initial VOD wait time: < 100 ms
  Mobile phone:
    initial VOD wait time < 100 ms
  TV: 4k @ 120 fps, HDR, 12 bit, ITU-R Rec. BT.2020
  Mobile phone: 2k @ 120 fps, HDR, 12 bit, ITU-R Rec. BT.2020
  Number of erratic displays during live broadcast <= 1
  VOD freeze duration on mobile phone/pad screens <= 5% (within the 1-minute statistical period)
  VOD freeze duration on TV screens <= 0.1% (within the 45-minute statistical period)
  TV:
    channel switching time < 500 ms
    Initial VOD wait time: < 1s
  Mobile phone:
    Initial VOD wait time: < 1s
  TV: 1080p @ 60 fps, 8 bit, ITU-R Rec. BT.709
  Mobile phone: 720p @ 30 fps, 8 bit, ITU-R Rec. BT.709
  TV:
    channel switching time < 1s
    Initial VOD wait time: < 2s
  Mobile phone:
    initial VOD wait time < 3s
  Number of erratic displays during live broadcast <= 0
  VOD freeze duration on mobile phone/pad screens <= 0% (within the 1-minute statistical period)
  VOD freeze duration on TV screens <= 0% (within the 45-minute statistical period)
The video industry technical can help the 3 top factors reach the following requirements.
Notes: The research about the experience of video communication is in progress

## Slide 15: Current ITU-T Video QoE Models
user interactions (such as pausing, seeking, user initiated quality change, user initiated play or user initiated end) are NOT considered at all
Measures the quality degradation
    due to compression
    due to packet-loss
    due to rebuffering
Provides packet-level (P.1201)/bit stream-level (P.1202) assessment algorithm
(Rec. P.1201 Appendix III)
HTTP Progressive Download
IPTV/Mobile TV Services
Formulated by adding the initial buffering time and video freeze impact to the P.1201 standard
Without consideration of user interactions
(Rec. P.1201/P.1202)
Notes: Difference between the P.1201 and P.1202 standards
Complementary to the ITU-T P.1202 models, there are two further models described in ITU-T P.1201.1 and ITU-T P.1201.2. The respective entry-document for these models is ITU-T P.1201. It describes packet header only-based video, audio and audiovisual quality models. The main differences with ITU-T P.1202 can be summarized as follows:
The ITU-T P.1201 models provide audio, video and audiovisual quality estimates, while the ITU-T P.1202 only models provides video quality estimates
The ITU-T P.1201 models use packet header information, while the ITU-T P.1202 models exploit further bitstream information, such as coding-related information. As a consequence, the ITU-T P.1202-models can be more accurate in their quality predictions. In turn, they require non-encrypted streams, to enable the access to payload information. Since the ITU-T P.1202 models are more complex, they also require more computational power to estimate the video quality

## Slide 16: Summary
Successful interoperability of ViLTE depends on ensuring end-user satisfaction with the resulting video quality (high QoE)
Standardized objective models for predicting video QoE are becoming available in ITU-T, and will play an important rule in ensuring ViLTE interoperability
Will complement audio QoE assessment models for ensuring VoLTE interoperability