## Slide 1: ITU Workshop on “Quality of Service and Quality of Experience of Multimedia Services in Emerging Networks” (Istanbul, Turkey, 9-11 February 2015)
QUALITY PARAMETERS of FIXED TELEPHONE SERVICES in TURKEY and BENCHMARK STUDIES
Mustafa ALANOĞLU,
Senior Expert, Türk Telekom
mustafa.alanoglu@turktelekom.com.tr

## Slide 2: QUALITY PARAMETERS OF FIXED TELEPHONE SERVICES
Service Quality Criterion | Related Measure | Measured Value | Target Value
Supply Time for the initial connection | The times by which the fastest 95% requests are completed | Day/s | ≤ 6
Faults Rate Per Access Line | Ratio of valid fault reports over total number of subscriber lines | % | ≤ 2,2
Faults Repair Time | The time by which the fastest 95% of valid faults on access lines are repaired | Hour/s | ≤ 90
Faults Repair Time for persons with disabilities | The time by which the fastest 95% of valid faults on access lines are repaired | Hour/s | ≤ 48
Unsuccessful Call Ratio | Unsuccessful call ratio in national calls | % | ≤ 1,5
 | Unsuccessful call ratio in international calls | % | ≤ 2,5
Call Set Up Time | The mean value in seconds for national call | Sec/s | ≤ 3
 | The mean value in seconds for international calls | Sec/s | ≤ 7
Proportion of Available Public Pay phones | Proportion of available public pay phones to all public pay phones | % | ≥ 95
Bill Complaints Ratio | Ratio of the bill complaints over the total number of bills | % | ≤ 1

## Slide 3: SUPPLY TIME FOR THE INITIAL CONNECTION ≤ 6 Days
A new access line
Taken over by another customer
An additional access line
The renewal of the technology
Includes official holidays
Starts with beginning of sign of a contract
Each requested service separately
Cancelled requests
The number of transfer requests
Agreement for some time in the future
Inadequate infrastructure
Transfer of subscription requests
The instant of a valid service order being received by a service provider
The instant a working service is made available to use
(Included)
(Excluded)

## Slide 4: Supply Time for the initial connection – Benchmark of Target Values*
5 Days, %95
21 Days, %95
43 Days, %99
30 Days, %95
70 Days, %99
14 Days, %95
32 Days, %99
1 week, %80
4 weeks, %95
12 weeks, %99
60 Days, %99
6 Days, %95
* Study of ETNO NANI (Naming, Addressing and Numbering Issues) Working Group, 2013 May

## Slide 5: FAULTS RATE PER ACCESS LINE ≤ %2,2
Calculated faults must be in the responsibility of the operator
Received Fault reports should be counted rather than the number of lines affected
Total used subscriber lines at the end of the measuring period
Faults due to customer responsibilities are excluded
Reported Valid Faults
Total number of subscriber lines

## Slide 6: Faults Rate Per Access Line– Benchmark of Target Values*
% 7,5
% 10
% 20
% 12,9
% 13,5
% 4
% 2,2
* Study of ETNO NANI Working Group, 2013 May

## Slide 7
The instant when a fault has been notified by the customer
The instant when the service has been restored and is ready to use
FAULTS REPAIR TIME ≤ 90 Hours
The cases that have an appointment in a future date
When the subscriber is absent in the agreed time
Special agreement including a specific fault repair time
Faults in responsibility of subscribers
(Excluded)

## Slide 8: Faults Repair Time – Benchmark of Target Values*
Acc. Net.
30 h, %80
96 h,%95
Others
24 h, %99
36 h, %95
35 hours, %80
40 hours, %95
60 hours, %99
Acc. Net.
72 h, %80
165 h,%95
Others
47 h, %99
108 h, %95
47 hours, %80
125 hours, %95
36 hours, %70
72 hours, %85
144 hours, %95
48 hours, %95
90 hours, %95
* Study of ETNO NANI Working Group, 2013 May

## Slide 9: UNSUCCESSFUL CALL RATIO ≤ %1,5 / %2,5
Unsuccessful calls
Total number of call attempts
Unsuccessful Call
Is a call attempt to a valid number, which calling party can’t take
Neither busy tone
Nor ringing tone
Nor answer signal
within 30 seconds
The scarcity of resources of radio link, transmission, switching etc.

## Slide 10: Unsuccessful Call Ratio – Benchmark of Target Values*
N/A
N/A
Int’l; %6
Nat’l ; %4
N/A
N/A
Int’l; %2
Nat’l ; %1
Int’l; %2,5
Nat’l ; %1,5
* Study of ETNO NANI Working Group, 2013 May

## Slide 11: CALL SET UP TIME ≤ 3 / 7 Second
Starts when the address information required for setting up a call is received by calling network
Finishes when
busy tone or
ringing tone or
answer signal
is received by the calling party

## Slide 12: Call Set Up Time – Benchmark of Target Values*
N/A
N/A
Int’l; 5 sec
Nat’l ; 3 sec
N/A
N/A
Int’l; 9 sec
Nat’l ; 2 sec
Int’l; 7 sec
Nat’l; 3 sec
* Study of ETNO NANI Working Group, 2013 May

## Slide 13: PROPORTION OF AVAILABLE PUBLIC PAY PHONES ≥ %95
Available Public Pay Phones
Total number of pay phones
Available means that;
Public pay phones can be used at any time (from 00:00 to 23:59)
Example; If a public pay phone
has a failure at 23:59
then it is repaired at 00:01 (just 2 minutes later)
this public pay phone should be accepted as not working for 2 days

## Slide 14: Proportion Of Available Public Pay Phones– Benchmark of Target Values*
N/A
% 96
% 92
% 96
% 93
N/A
% 95
* Study of ETNO NANI Working Group, 2013 May

## Slide 15: BILL COMPLAINTS RATIO ≤ %1
All bill complaints
Total number bills
Regardless of the validity of the complaint (all billing complaints )
Regardless of the dates of calls or any other occurrences
Bill inquiries and failure notifications are excluded

## Slide 16: Bill Complaints Ratio– Benchmark of Target Values*
% 1
For just billing mistakes,
% 0,04
% 1
Disputable bills; %2,7
Billing Faults, %0,5
% 0,2
% 0,5
% 1
* Study of ETNO NANI Working Group, 2013 May

## Slide 17: DO WE NEED ANY ADDITIONAL PARAMETER?
Is it enough to only discount the prices of tariffs for persons with disabilities (pwd)?
Around 15 per cent of the world's population, or estimated 1 billion people, live with disabilities.
They are the world's largest minority
What about Quality of Service?
Chart: * PERCENTAGE OF PWD
| High-Income Countries | Middle-Income Countries | Low-Income Countries | WORLD
Prevalence | 0.12 | 0.17 | 0.15 | 0.16
*http://whqlibdoc.who.int/publications/2011/9789240685215_eng.pdf?ua=1

## Slide 18: FAULT REPAIR TIME FOR PERSONS WITH DISABILITES
Target value of Fault repair time for other people ≤90 hours
BUT
48 hours for the persons with disabilities.
Telecommunication services are much more important for the people with disabilities since it may be the only way of communication for them
Thus, we may accept that solving
the problems of the persons with disabilities = emergency calls
THAT MUST BE A RECOMMENDATION / STANDARD, OR NOT ?
The persons with disabilities at least the ratio of %40 (it is needed to be certified)

## Slide 19: Thanks
COMMENTS & Questions?