## Slide 1: Situation Analysis on Standards for Safe Listening
Simão Campos ITU-T Study Group 16 "Multimedia" ITU-T Workshop on Standards for Safe Listening Geneva, Switzerland, 6 June 2016

## Slide 2: Background
Joint WHO-ITU Joint Stakeholders’ Consultation and Expert Meeting on Safe Listening Devices (Geneva, 1-2 October 2015)
Identified need for a gap analysis on standards for safe listening
  Desk review of existing standards and related info done Nov 2015–Jan 2016 http://itu.int/en/ITU-T/Workshops-and-Seminars/safelistening/Documents/ Standards_for_safe_listening_devices_situation_analysis_report.pdf
  Focus mainly on personal music players as sources of recreational sound
    Excludes sources such as concerts, sporting venues and personal sound amplifiers

## Slide 3: Definitions
Personal audio system: a personal audio system refers to the complete listening system which consists of two parts: 1) the personal music player and 2) the headphones/earphones used with it.
Personal music player: a personal music player refers to portable equipment intended for use by an ordinary person, that:
  Is designed to allow the user to listen to audio or audiovisual content/material; and
  Uses a listening device, such as headphones or earphones that can be worn in or on or around the ears; and
  Has a player that can be body worn (of a size suitable to be carried in a clothing pocket) and is intended for the user to walk around while in continuous use (for example, on a street, in a subway, at an airport, etc.).
  Examples include portable CD players, MP3 audio players, mobile phones with MP3 type features, personal digital assistants (PDAs) or similar equipment. (Excluded from the definition are rehabilitative and medical devices (Hearing aids, FM loops) as well as personal sound amplification devices.)
Transducer: in the context of this document, a transducer refers to a earphone/headphone used along with a personal music player for purpose of listening.

## Slide 4: Method
Report from the October 2015 consultation meeting
Literature and website research
  Access to documentation is limited as they are paying publications

## Slide 5: Standards

## Slide 6: SDOs
ANSI, ASA
CENELEC, IEC
ITU-T, ITU-R

## Slide 7: Identified standards
Many standards exist for occupational settings
Several standards address open field
But only a handful of standards are specific to personal media devices/systems

## Slide 8: CENELEC
EN 50332 – Sound system equipment: Headphones and earphones associated with personal music players (PMPs) – Maximum sound pressure level measurement methodology
  EN 50332-1:2013 (“one package equipment”, where the headphones and the music player are supplied together as a unit)
  EN 50332-2:2013 (headphones and the music player supplied separately)
  EN 50332-3: ongoing work on dosimetry
    Reduce false warnings (given by part 1 and 2)
    help protect music integrity by not requiring absolute reduction of music levels of recorded content, but rather managing exposure over time.

## Slide 9: IEC
IEC/EN 60065:2014: Audio, video and similar electronic apparatus - Safety requirements
  IEC international standard safety requirements at large
  Includes specification for sound level limits, to be tested with either EN 50332-1 or EN 50332-2
IEC/EN 62368-1:2014 – Audio/video, information and communication equipment – Part 1: Safety requirements
  replaces EN 60065 (A/V equipment), EN 60950-1 (IT & comms eq.)
  EN 50332 parts 1 and 2 implemented in its clause 10.6
  Transposed in US and Canada as CSA/UL 62368-1

## Slide 10: ISO
ISO 11904 Acoustics – Determination of sound immission from sound sources placed close to the ear
  http://www.iso.org/iso/iso_catalogue/catalogue_tc/catalogue_detail.htm?csnumber=33944
  Part 1: Real person
  Part 2: Manikin

## Slide 11: ITU (1)
ITU-T P.311 (03/2011) Transmission characteristics for wideband digital handset and headset telephones http://www.itu.int/rec/T-REC-P.311
  audio performance requirements and test methods for wideband (8000 Hz) handset and headset telephones
ITU-T P.380 (11/2003)– Electroacoustic measurements on headsets http://www.itu.int/rec/T-REC-P.380

## Slide 12: ITU (2)
ITU-T P.381 (02/2014) – Technical requirements and test methods for the universal wired headset or headphone interface of digital mobile terminals
  http://www.itu.int/rec/T-REC-P.381
ITU-R BS.1770-4 (10/2015) - Algorithms to measure audio programme loudness and true-peak audio level
  http://www.itu.int/rec/R-REC-BS.1770
  objective multichannel loudness measurement algorithm for programme delivery and exchange
  Not compatible with EN 50332 test methods

## Slide 13: Implementation

## Slide 14: Standards adoption is voluntary
The adoption of standards is by nature voluntary.
However, adoption can be mandated:
  Country or regional level: inclusion in legislation or regulations
  Private sphere: inclusion in contracts or procurement requirements

## Slide 15: European Union and Switzerland
Europe
  Application of EN 50332 (-1, -2) mandated since January 2013
Switzerland:
  SNEN 60065:2014 (transposition of EN 60065:2014)
  SNEN 50332:2013 (transposition of EN 50332:2013)

## Slide 16: Rest of the world
No specific regulations related to recreational use of personal audio systems were found in this study

## Slide 17: Implementation by vendors
No reference in user messages or documentation on implementation of particular standards
Devices
  Varied warnings about levels
  Warning seems to be triggered by output level settings, not actual measurements on signal being played
Other type of information to users
  Smartphone vendors seem to be more consistent than MP3 players manufacturers in providing information to users
Notes: Warning image from a Samsung S5 phone, when an external device is connected to the audio-out exit.

## Slide 18: Gap analysis

## Slide 19: Current situation (1)
At present there are standards developed by the CENELEC which measure sound pressure levels in PMPs.
  As per these standards, all devices should have a default output limit of 85 dB.
  The user can choose to override the limit (set by the device), so that the sound level can be increased up to maximum 100 dB.
  If the user overrides the limit, warnings about the risks must be repeated every 20 hours of listening time.
  IEC transposed the related CENELEC standards as a global standard
Personal music players sold in Europe after February 2013 are expected to comply with these standards.
  No indication of adherence was found in other parts of the world

## Slide 20: Current situation (2)
There is a lack of performance/quality certification of some devices in low- and middle-income countries. This makes it easier for counterfeit and low quality devices to inundate the market.
The above-mentioned standards do not take into consideration the duration of sound exposure, which is as important as the volume level.
Evidence suggests that users often consider the limit set as annoying and frequently override it, ignoring the warning message.

## Slide 21: Looking ahead
Identify effective hearing protection approach that is acceptable to users
  Parameters should be identified that assist users to make listening safe whilst maintaining the quality of their listening experience.
Dosimetry is an essential part

## Slide 22: Points to consider for global standards on safe listening devices (1)
Uniform and reliable methods to measure sound output must be applied.
  Harmonization needed for measurement methods (e.g. ISO 11904-1/2 or EN 50332-1/2) and reference signals
Performance standards need to take into account the sound pressure at the level of the user’s ear, not electric levels
Players should recognize the transducer used and configure the output volume level and estimate dose, based on the transducer used.

## Slide 23: Points to consider for global standards on safe listening devices (2)
Profiles could identify from basic devices ("low end") to high-end ones.
  All devices should provide adequate protection;
  High-end devices can have more plug-and-play functions and customization options, for example.
  Profiling could also distinguish level-only and dosimetry enabled devices
Apps could be provided for hearing tests by users and use results to set the threshold at which warnings would appear
  Warning customization to make it more relevant to an individual

## Slide 24: Points to consider for global standards … (2)
Devices display messages suitable to promote safe listening practices.
  Provide information on the impact of users' decision (to raise or reduce the volume)
Warning information should be easy to reach (e.g. a common WHO portal) and to understand
Encourage technics for noise reduction, isolation or cancellation
  Reducing background noise: less need to turn up the music volume

## Slide 25: And finally:
Standards should be developed and implemented globally
  collaborative effort of all stakeholders, including all relevant SDOs
  Implemented by manufacturers of personal music players and of earphones/headphones

## Slide 26: Let's make listening … … both safe and enjoyable Thank you!

## Slide 27: Some feedback received

## Slide 28: ISO TC 43
Harmonize the use of SPL and Lp;
Verify applicability of:
  EN 352-6 “Hearing protectors - Safety requirements and testing - Part 6: Ear-muffs with electrical audio input”
  EN 352-8 “Hearing protectors - Safety requirements and testing - Part 8: Entertainment audio ear-muffs”
Comments on dosimetry from Prof Dorte Hammershoi (Aalborg Univ.)
Notes: Dorte Hammershoi:
“I'm familiar with the efforts in CENELEC TC 108X (the EN 50332 series), and have given comments to the convenor on alternative directions. Last summer I presented a paper at an Audio Engineering Society conference (attached), which shows the significance of the earphone sensitivity. This variation is not considered in the current EN 50332 approach. I'm not familiar with the efforts of the other working groups, and can only comment on a general level for the EN 50332, which I think need some revision to meet an international interests. The following seems necessary to discuss and relate to:
1) The earphone sensitivity. The producers of the music players may assume a certain earphone at delivery, but very few use these throughout the use time of the player. The sensitivity of the earphones vary so much that a best guess based on player output voltage alone can be 10-20 dB wrong, suggesting dose estimates varying from minutes to hours. It is not in anyone's interest to limit the variation in earphone products further, thus our standardization efforts should embrace the variation, not ignore it. The risk of using e.g. high quality circumaural earphones from e.g. Sennheiser will e.g. be severely overestimated by any Apple product assuming their own earphone. I'm including one graphic from my presentation, which shows the variation on a dose scale.
2) The dose estimate proposed by EN 50332-3 can only be realized by sample-by-sample signal processing, or by adding analog electronic circuitry. This is an extremely expensive solution, taking either power from the player during run-time, or space from the compact design of players. Only future generations of players may meet this requirement, and it will take years of development before the first product includes a satisfying solution.
3) The 50332 is not well aligned with international efforts. EN 50332-1 lay down the measurement procedure, which was the starting point for the ISO 11904 work, and which was shown to include an unnecessary bias (from the mismatch between the weighting curve and the equivalent for humans), and a sub-optimal accuracy in the final noise immission estimate, because the sound exposure is not analyzed in frequency bands. This size of this bias will depend on the earphone, and thus not be a simple constant, one can account for.
4) A revision of 50332-1 to align with ISO 11904 will enable the EN 50332-3 (dose estimates) to be based on third octave band values, that may either be provided by an online service for each music track (e.g. as side information from the music provider, spotify etc.), or possibly from readilly available MP3 gain factors (I don't know the standard well enough to know for sure). This way, one can avoid sample-by-sample signal processing entirely, and at the same time get better dose estimate. Only very few third octave values (19 or 17 or even less) are required to adequately describe the essential bandwidth, and these can be subsequently weighted by the volume and play time settings used during playback, and earphone sensitivity as programmed by producer, user or music provider, or serviced by on-line catalogues. This will not give exactly the same result, but surely a more reliable one than the alternative (ignoring earphone sensitivity).
5) The EN 50332-3 dose estimate ignores both the ear-to-free-air weighting (inverse head-related transfer function) which is required to make dose estimates comparable to free air reference material (current legislation etc.), and the earphone sensitivity. One can argue that if earphones were designed to mimic either free or diffuse field, these two omissions would cancel each other, but measurements over time reveals that this assumption doesn't hold. Again, it is probably not in anyone's interest to enforce a development that limits this variation.
6) The CENELEC efforts are the result of a decision from the European commission in 2009, which specified that "the music players must not put their users at risk". This is extremely difficult, since a single track of music played at the highest level may already exceed a day dose, and we don't want to compromise dynamics further by reducing the maximum output voltage, nor to force the music player to turn off. The 8 hour average of 80 dB with 3 dB trading for each doubling of time, is by most considered a safety limit. This philosophy may not be well aligned with international strategies, e.g. WHO leans on the American NIOHS recommendations (85 dB over 8 hours), where one can listen at 100 dB for 15 minutes rather than 3 min. An aligned strategy for dose estimation and user display should allow both the display of the safety limit (80 dB over 8 hours), and a recommended (reduced risk) limit based on 85 over 8 hours. A "likely damage" limit based on 90 dB over 8 hours could also be considered to allow for information of the risk level, and not just "you are at risk" (which the 80 dB over 8 hours represent).”