INTERNATIONAL TELECOMMUNICATION UNION

TELECOMMUNICATION
STANDARDIZATION SECTOR

STUDY PERIOD 1997 - 2000

COM 11-R 8-E

April 1997

Original: English

Question: 15/11

STUDY GROUP 11 – REPORT R 8

SOURCE*:	STUDY GROUP 11

TITLE:	REPORT OF THE MEETING HELD IN GENEVA FROM 13-31 JANUARY 1997: PART I - IMPLEMENTORS' GUIDE FOR Q.2140 (02/1995)

________

The reports of the meeting of Study Group 11 and its Working Parties are published in the documents listed in COM 11-R 1.

STATUS - This text was approved by Study Group 11, January 1997.

NOTE - This text is also available from the ITUDOC.

1	Introduction

1.1	References

[1]	ITU-T Recommendation Q.2140 - 02/95 - B-ISDN ATM Adaptation Layer - Service Specific Coordination Function for Support of Signalling at the Network Node Interface (SSCF at NNI).

[2]	Implementors' Guide for Q.2110, COM 11-R 7.

1.2	Background

This guide is a compilation of reported defects, their resolutions and minor upgrades to the 1994 edition of the ITU-T Recommendation Q.2140. It includes all approved corrigenda and is intended to be an additional authoritative source of information for implementors to be read in conjunction with the Recommendation itself.

1.3	Scope of the guide

This guide records the resolutions of defects in the following categories:

•	editorial errors;

•	technical errors, such as omissions, inconsistencies etc.; and

•	ambiguities.

In addition, this guide records minor enhancements to the Recommendation in the following categories:

•	increased interoperability; and

•	deployment possibility in new environments.

1.4	Contacts

| Rapporteur (Q.15/11): | Dr. Pietro Schicker Swiss Telecom PTT/ Scientific Consulting | Tel: +41 1 938 1555 Fax: +41 1 938 1557 email: schicker@scicon.ch |
| --- | --- | --- |

| Former Rapporteur: | G. Ratta Bellcore | Tel: +1 908 758 5696 Fax: +1 908 758 4131 email: gratta@notes.cc.bellcore.com |
| --- | --- | --- |

2	Editorial errors

2.1	Organization of Table 6/Q.2140

Synopsis

Table 6/Q.2140 "State transition table for SSCF at NNI" is organized wrongly.

Mod. a)		At the second occurrence of the term "AAL-START-request" in the first column (bottom of page 25), the complete row must be transferred to the start of the table on the following page (top of page 26 after table heading).

| AAL-START-request | Illegal | Illegal | Illegal | Illegal |
| --- | --- | --- | --- | --- |

Mod. b)		The table header on pages 26 to 30 should be replaced with the following template header:

| State | Alignment/Outgoing Disconnection Pending 2/4/2 | In service/Data transfer ready 3/10/5 | Proving/Data transfer ready 2/10/3 | Aligned ready/ Data transfer ready 2/10/4 |
| --- | --- | --- | --- | --- |
| SSCF timers running | T2 |
| T2, T3 | T2 |
| Event |

2.2	Optional status in PICS proforma (A.5.1 protocol capabilities (PC) - SSCOP)

Synopsis

The entry "PC9" in the PICS proforma (§ A.5.1) should have a status "O".

Mod. a)		Replace the row with "PC9" in the first column with:

| PC9 | Does the ITU support polling after retransmission? | O | Q.2110 SDL Figure 20 (sheet 38 of 51) | Yes:_No:_X:_ |
| --- | --- | --- | --- | --- |

2.3	Typographical errors

Mod. a)		In the third paragraph of § 6.2.1 the term "AAL-OUT_OF_SERVICE.indication" should be spelled with a hyphen before "indication" as in the rest of the Recommendation, i.e., "AAL-OUT_OF_SERVICE-indication".

3	Technical errors

None.

4	Ambiguities

None.

5	Increased interoperability

5.1	Increased robustness during power-up connection establishment

Synopsis

An option is introduced to allow the SSCOP entity to accept a BGN PDU in state IDLE irrespective of the values of N(SQ) in the BGN PDU and the state variable VR(SQ) (see [2] § 5.1).

Mod. a)		In § A.5.3, add a further row to the table as follows:

| Item # | Protocol feature | Status | References | Support |
| --- | --- | --- | --- | --- |
| SP12 | Is power-up robustness implemented? | O | SDL | Yes:_No:_X:_ |

6	Deployment possibility in new environments

None.