INTERNATIONAL TELECOMMUNICATION UNION

TELECOMMUNICATION
STANDARDIZATION SECTOR

STUDY PERIOD 1997 - 2000

COM 11-R 138-E

April 1999

Original: English

Question: 16/11

E

STUDY GROUP 11 – REPORT R 138

SOURCE*:	STUDY GROUP 11

TITLE:	IMPLEMENTORS' GUIDE (03/99) FOR RECOMMENDATION Q.714 (07/96)

________

1	Introduction

This document contains clarification on the use of centralized database during the Global Title Translation process.

1.1	References

[1]	ITU-T Recommendation Q.714 - 07/96 - Signalling System No. 7 - Signalling Connection Control Part Procedures.

Change marks (new text; deleted text) in this Implementors' Guide refer to this version of Q.714.

1.2	Background

This guide is a clarification to the 1996 edition of ITU-T Recommendation Q.714. The guide is intended to be an additional authoritative source of information for implementors to be read in conjunction with the Recommendation itself.

1.3	Scope of the guide

This guide records enhancements to the Recommendation in the following category:

•	ambiguities.

Attention: This is not an ITU publication made available to the public, but an internal ITU Document intended only for use by the Member States of the ITU and by its Sector Members and their respective staff and collaborators in their ITU related work. It shall not be made available to, and used by, any other persons or entities without the prior written consent of the ITU.

1.4	Contact

| Rapporteur Q.16/11: | Brian Skinner, BT PP2.27 Angel centre, London EC1 United Kingdom | Tel: +44 171 843 7510 Fax: +44 171 490 8375 email: brian.skinner@bt.com |
| --- | --- | --- |

1.5	Document history

| Version | Summary |
| --- | --- |
| (03/99) | New Implementors' Guide - draft |

2	Change to Q.714

The first bullet item of § 2.1 (SCCP addressing) is modified as such:

1)	Global Title – A global title is an address, such as dialled-digits, which does not explicitly contain information that would allow routing in the signalling network, that is the translation function of the SCCP is required. This translation function could be performed on a distributed basis or on a centralized basis. The last case, where a request for translation is sent to a centralized data base, may be accomplished, for example, with transaction capabilities (TC). This matter is for further studyand its associated data are assumed to be part of the SCCP node. Access to an external database during invocation of this function is not specified and is for further study.