INTERNATIONAL TELECOMMUNICATION UNION

TELECOMMUNICATION
STANDARDIZATION SECTOR

STUDY PERIOD 1997 - 2000

COM 11-R 104-E

June 1998

Original: English

Questions: 12/11

E

STUDY GROUP 11 – REPORT R 104

SOURCE*:	STUDY GROUP 11

TITLE:	IMPLEMENTORS' GUIDE (05/98) FOR RECOMMENDATION Q.734.1 (03/93)

________

1	Introduction

1.1	References

[1]	ITU-T Recommendation Q.734.1 (03/93)

[2]	ITU-T Recommendation Q.115 (01/97)

[3]	ITU-T Recommendation Q.764 (09/97)

1.2	Background

This guide is a compilation of amendments to the 1993 edition of the ITU-T Recommendation Q.734.1 [1]. It includes all approved corrigenda and is intended to be an additional authoritative source of information for implementors to be read in conjunction with the Recommendation itself.

1.3	Scope of the guide

This guide records the resolutions of defects in the following categories:

•	editorial errors;

•	technical errors, such as omissions, inconsistencies, etc.; and

•	ambiguities.

1.4	Contacts

| Editor: | Pieter Veenstra KPN Telecom B.V. P.O. Box 30150 2500 GD The Hague The Netherlands | Tel: +31 70 3439121 Fax: +31 70 3437303 Email: p.k.veenstra@kpn-telecom.nl |
| --- | --- | --- |

1.5	Document history

| Version | Summary |
| --- | --- |
| 05/98 | New Implementors' Guide |

2	Editorial errors

None.

3	Technical errors

3.1	Echo control related procedures

Synopsis

New echo control logic procedures have been specified in ITU-T Recommendation Q.115 [2] in conjunction with new echo control signalling procedures in ITU-T Recommendation Q.764 [3]. As result the echo control related statements in the procedures for Conference Calling have become outdated. As a consequence, the echo control related text phrases in § 1.5.2.1.1.1 a) and § 1.5.2.1.1.1 b) have to be replaced by new text.

Please replace the following text phrases in ITU-T Recommendation Q.734.1 [1]:

1.5.2.1.1.1	Requirements related to echo control

a)	General

The originating local exchange where the conference bridge is located should have the capability to invoke echo control procedures. This is necessary in the case the total propagation delay for the two legs in the conference is above the value where echo control is necessary (ref. 2.6/Q.764).

The exchange must also have the capability of storing propagation delay information received either in a received IAM (for incoming calls) or in ANM/CON (for outgoing calls) until call release. This must be done for all legs included in the conference.

b)	Criteria to initiate echo control procedures

Upon adding a new call to the conference, the received propagation delay value related to this leg shall be added to each of the other legs to decide whether echo control apply for the legs concerned.

If echo control is necessary, the exchange will initiate echo control procedures for each of the legs concerned. (2.7/Q.764).

by:

1.5.2.1.1.1	Requirements related to echo control

The echo control logic as defined in ITU-T Recommendation Q.115 (01/97) shall apply. The exchange shall also have the capability of storing propagation delay information received either in the Initial Address message (for incoming calls) or in the Answer/Connect message (for outgoing calls) until call release. This shall be done for all legs included in the conference.

4	Ambiguities

None.

_____________________