INTERNATIONAL TELECOMMUNICATION UNION

TELECOMMUNICATION
STANDARDIZATION SECTOR

STUDY PERIOD 1997 - 2000

COM 11-R 109-E

June 1998

Original: English

Question: 2/11

E

STUDY GROUP 11 – REPORT R 109

SOURCE*:	STUDY GROUP 11

TITLE:	IMPLEMENTORS' GUIDE (05/98) FOR RECOMMENDATION Q.751.3 (07/97)

________

1	Introduction

1.1	References

[1]	ITU-T Recommendation Q.751.3 - (07/97) - Network Element Information Model for MTP Accounting

Change marks in this Implementors' Guide refer to this version of Q.751.3.

1.2	Background

This guide is a compilation of reported defects, their resolutions and minor upgrades to the 1997 edition of the ITU-T Recommendation Q.751.3. It includes all approved corrigenda and is intended to be an additional authoritative source of information for implementors to be read in conjunction with the Recommendation itself.

1.3	Scope of the guide

This guide records the resolutions of defects in the following categories:

•	editorial errors;

•	technical errors, such as omissions, inconsistencies, etc.; and

•	ambiguities.

1.4	Contact

Rapporteur Q.2/11:	Clemens Suerbaum 	Tel.	+ 49 89 722 - 42418
	Siemens AG	Fax:	+ 49 89 722 - 24159
	OEN SN ESC 12 	Email:	clemens.suerbaum@oen.siemens.de
	Machtlfingerstr. 1
	D-81359 Munich
	Germany

1.5	Document history

| Version | Summary |
| --- | --- |
| 05/98 | New Implementors' Guide |

2	Editorial errors

2.1	Missing objectManagementNotificationsPackage in Table 4 and 5/Q.751.3

Synopsis: The objectManagementNotificationsPackage is defined to be part of the managed object classes mtpAccount and siGroup, but is missing in the corresponding tables in the informal section:

Mod. a): Add the following lines to Table 4/Q.751.3 (object class mtpAccount) and Table 5/Q.751.3 (object class siGroup):

| attributes | notifications | actions |
| --- | --- | --- |
| "ITU-T Rec. M.3100 (1995)":objectManagementNotificationsPackage (M) |
|  | "ITU-T Rec. X.721 (1992)":attributeValueChange |
| "ITU-T Rec. X.721 (1992)":objectCreation |
| "ITU-T Rec. X.721 (1992)":objectDeletion |

2.2	Wrong object class referenced in Table 6/Q.751.3 for dpcGroup

Synopsis: In this table the specific errors for the different object classes are listed. In the lines relating to object class dpcGroup object class mtpAccount is referenced erroneously.

Mod. a): Change Table 6/Q.751.3 as follows:

| Operation | Error | Description |
| --- | --- | --- |

|  | object class dpcGroup |
| --- | --- |
|  | REPLACE ADD-REMOVE pointCodeSet + CREATE | pointCodeNotExistingInSameMtp SignPointError | At least one of the point codes is not used by any signRouteSetNePart instance contained in the same mtpSignPoint as the dpcGroup. |
|  | pointCodeUsedByMtpSignPointError | At least one of the point codes is used as point code by the mtpSignPoint containing the dpcGroup. |

3	Technical errors

Although some of these errors have their origin in an editorial error, they were categorized as technical errors, if the formal definitions are affected.

3.1	Duplication of attribute controlPointer in object class mtpAccount

Synopsis: The attribute controlPointer was moved in a separate conditional package. It was missed to delete it in the mtpAccountPackage.

Mod. a): Delete the attribute controlPointer from the mtpAccountPackage. This results in the following:

mtpAccountPackage PACKAGE

BEHAVIOUR mtpAccountPackageBehaviour BEHAVIOUR DEFINED AS

".....";;

ATTRIBUTES

mtpAccountId  GET SET-BY-CREATE,

signLinkSetTpSet  GET SET-BY-CREATE ADD-REMOVE,

operatorName  GET SET-BY-CREATE,

selectionGroupSetForAccounting  GET REPLACE ADD-REMOVE;

selectionGroupSetForVerification  GET REPLACE ADD-REMOVE;

NOTIFICATIONS

mtpAccounting,

mtpAccountingVerification;

REGISTERED AS {mtpAccountPackage-POi};

3.2	Duplication of OBJECT IDENTIFIERS

Synopsis: Some of the OBJECT IDENTIFIERS defined in the ASN.1 module are used twice, but must be unique.

Mod. a): Change the OBJECT IDENTIFIERS as follows:

-- ASN.1 OBJECT IDENTIFIER definitions

dpcGroupId-AOi OBJECT IDENTIFIER ::= {accountingAttribute dpcGroupId(13)}

mtpAccountId-AOi OBJECT IDENTIFIER ::= {accountingAttribute mtpAccountId(14)}

_____________