INTERNATIONAL TELECOMMUNICATION UNION

TELECOMMUNICATION
STANDARDIZATION SECTOR

STUDY PERIOD 1997 - 2000

COM 11-R 131-E

April 1999

Original: English

Question: 11/11

E

STUDY GROUP 11 – REPORT R 131

SOURCE*:	STUDY GROUP 11

TITLE:	IMPLEMENTORS' GUIDE (03/99) FOR RECOMMENDATION Q.931 (05/98)

________

1	Introduction

1.1	References

[1]	ITU-T Recommendation Q.931 - (05/98) - Digital Subscriber Signalling System No. 1 - ISDN User-Network Interface Layer 3 Specification for Basic Call Control

1.2	Background

This guide is a compilation of reported defects, their resolution and minor upgrades to the 1998 edition of ITU-T Recommendation Q.931 [1]. It includes all approved corrigenda and is intended to be an additional authoritative source of information for implementors to be read in conjunction with the Recommendation itself.

1.3	Scope of the guide

This guide records the resolution of defects in the following categories:

•	editorial errors;

•	technical errors, such as omissions, inconsistencies, etc.; and

•	ambiguities.

Attention: This is not an ITU publication made available to the public, but an internal ITU Document intended only for use by the Member States of the ITU and by its Sector Members and their respective staff and collaborators in their ITU related work. It shall not be made available to, and used by, any other persons or entities without the prior written consent of the ITU.

In addition, this guide records minor enhancements to the Recommendation in the following categories:

•	increased interoperability; and

•	deployment possibility in new environments.

1.4	Contacts

Rapporteur Q.11/11: (See information in the list of Rapporteurs for Study Group 11 on the Web.).

1.5	Document history

| Version | Summary |
| --- | --- |
| 03/99 | New implementors' guide |

2	Editorial errors

None.

3	Technical errors

None.

4	Ambiguities

Subclause 4.5.15 of ITU-T Recommendation Q.931 [1], Date/time information element:

If the date is represented using the gregorian calendar, the field "year" shall contain the binary representation of the last two digits of the decimal representation of the year, i.e. the binary representation of a number in the range from 0 to 99. Example: The year 1998 shall be coded as "01100010", which is the binary equivalent of the decimal number "98". The year 2001 shall be coded as "00000001", which is the binary equivalent of the decimal number "01".

5	Increased interoperability

None.

6	Deployment possibility in new environments

None.