|  | INTERNATIONAL TELECOMMUNICATION UNION |
| --- | --- |
| ITU-T | G.729 Implementers Guide |
| TELECOMMUNICATION STANDARDIZATION SECTOR OF ITU | (25 October 2002) |
|  | SERIES G: TRANSMISSION SYSTEMS AND MEDIA, DIGITAL SYSTEMS AND NETWORKS Digital terminal equipments – Coding of analogue signals by methods other than PCM |
|  | Implementers' Guide for G.729 Annexes B, F, G, I and C+ (Coding of speech at 8 kbit/s using CS-ACELP) |

Implementers Guide for Recommendation G.729

___________________

Contact Information

| Rapporteur, ITU-T Study Group 16 / Question 10 | Claude Lamblin France Telecom R&D /DIH Technopole Anticipa 2 avenue Pierre Marzin 22307 LANNION Cedex France | Tel: +33 2 96 05 13 03 Fax: +33 2 96 05 35 30 Email: claude.lamblin@rd.francetelecom.com |
| --- | --- | --- |

SUMMARY

# Implementors' Guide for Recommendation G.729

This document contains the Implementers' Guide for ITU-T Recommendation G.729 and its Annexes B, F, G, I and C+ that corrects defects reported at SG 16’s meeting 15-25 October 2002.

Table of Contents

Implementors' Guide for Recommendation G.729	ii

Implementers' Guide for G.729 Annexes B, F, G, I and C+	1

Description of the needed changes	1

Modifications to fixed-point C source codes in G.729 Annexes B, F, G, I and C+	1

# Implementers' Guide for G.729 Annexes B, F, G, I and C+

# Description of the needed changes

As described in COM16-D244, the problem is caused by the lack of safe initialization of LSFs indices, and the search for the SID optimal indices may terminate abnormally, resulting in a possible crash of the simulation program. The problem was identified on G.729 Annex I, but it is applicable also for Annexes B, F, G, and C+.

# Modifications to fixed-point C source codes in G.729 Annexes B, F, G, I and C+

In the file qsidlsf.c, in the routine New_ML_Search_1 at line 195, and in the routine New_ML_Search_2 at line 264, add two lines, changing both blocks of identical code from:

for (q=0; q<K; q++){

for (p=0; p<J; p++)

for (m=0; m<MQ; m++)

if (sub(sum[p*MQ+m], min[q]) < 0){

min[q] = sum[p*MQ+m];

min_indx_p[q] = p;

min_indx_m[q] = m;

}

sum[min_indx_p[q]*MQ+min_indx_m[q]] = MAX_16;

}

to the new code:

for (q=0; q<K; q++){

min_indx_p[q] = 0;

min_indx_p[q] = 0;

for (p=0; p<J; p++)

for (m=0; m<MQ; m++)

if (sub(sum[p*MQ+m], min[q]) < 0){

min[q] = sum[p*MQ+m];

min_indx_p[q] = p;

min_indx_m[q] = m;

}

sum[min_indx_p[q]*MQ+min_indx_m[q]] = MAX_16;

}

Note: for Annex C+, the constant FLT_MAX_G729 should be used, instead of the constant MAX_16.

-- END --