## Slide 1: Internet services pricing under usage-based cost allocation: Congestion dependence
Havana (CUBA), 22 October, 2001
Most of the slides in this presentation come from Mark Scanlan (EU researcher) who submitted them during the Brastislava seminar on New Trends in Tariff Policies (September 2001)
pape-gorgui.toure@itu.int

## Slide 2: Issues addressed in this presentation
QoS and congestion management
Real-time services
Matching price structures with cost causation
Technical mechanisms to improve QoS
Future fragmentation in standards, and industry structure ?
Network externalities

## Slide 3: QoS and congestion management
QoS on the internet is essentially statistical:
All packets treated the same, but ‘real-time’ service packets require different QoS.
Notes:   QoS on the Internet is essentially statistical: Latency, jitter, bandwidth availability, packet loss, network resources availability
  The ‘best effort’ principle on the basis of which the information are routed through the network has not alowed yet real time service to be viable on the public internet.
  As well as for technology reasons, one of the main causes of this is that economically efficient pricing structures are not used.

## Slide 4: Existing congestion management
Over-provisioning has been the principle means ISPs have used in meeting peaks in demand.
ISPs accept traffic on a ‘best-effort’ basis, although increasingly QoS statistics are contracted.
Congestion management / resource optimisation is treated as a technical issue
Notes: In order to anticipate the growing need of resources, in particular during peak hours, ISPs have been over-provisioning for years.
One can, nevertheless, notice that the issue of QoS is getting more and more important with real time services (especially VoIP) being increasingly demanded through the Internet.
Until now, the network resource optimization and/or congestion management has been treated as a technical issue: network dimensioning in order to provide given technical performances at peak time.

## Slide 5: Congestion management
Presently backbone congestion is hidden within:
  Overall round trip times and system start-up latency, and
  Delays between the backbone and end-user.
Broadband access will help bring backbone congestion into focus.
Notes:   TCP
    Little account of order and timing
    queuing results in overflow indicating congestion to sending TCPs and a slow down in packet sending.
  ATM – traffic shapping: ITU recommendations have created for ATM the necessary framework.
  The backbone are congested but the effect of that is hidden by both the lenghth of the transport process in TCP, the technical limitations inherent to network access procedures (start-up latency, and the delay between backbone and end-user).
  One can expect that when the ‘broadband access’ is more widely used, the focus will be back on the backbone congestions.

## Slide 6: Congestion management
Prices provide the efficient means for managing congestion.
Presently, dial-up users are charged:
  by their access provider
    per minute (EU); Zero - DLS, USA, NZ; 25 cents (Aust)
  per month by their ISP
Price signals are passed from the parameter up through the loose hierarchy
  No congestion pricing with ISP interconnection
Notes: Researchers in big universities have been significantly sponsored by both the public and the private sector in order to evaluate the extent to which pricing policies might provide means for managing congestion.
Valuable findings have been made but until now the methods used to charge dial-up users exclude the congestion criteria:
  Access charge
  Per month charge
Interconnection between ISPs also exclude the congestion criteria

## Slide 7: Congestion management
Increasingly flat-rate pricing is the end-user ISP model - extra packets are not priced.
To be economically efficient the structure of prices should match the structure of costs.
There are 3 types of cost involved that should ideally be mirrored in the prices charged to users.
  1. fixed costs (these don’t vary with usage).
  2. initial cost of connecting a customer to the internet
  3. congestion cost
Notes: Flat-rate pricing applied to end-users is almost synonymous of Internet business model;
But it is obvious that flat-rate pricing doesn’t match the cost structure of internet based service provision, and therefore are not economically efficient;
In an ideal situation, the pricing mechanism should mirror the types of cost involved:
  1. fixed costs (these don’t vary with usage).
  2. initial cost of connecting a customer to the internet
  3. congestion cost

## Slide 8: Congestion management (cont)
For economic efficiency the price structure should have all 3 components:
  1. A subscription charge
    These costs cannot be said to be incremental to any single customer.
    No person should be charged a subscription more than their willingness to pay.
  2. A one-off charge, and
  3. A congestion charge.
Notes: (comment the slide first)
A few researchers are of the view that the congestion charge should not be intended to recover costs (already recovered by subscription and one-off) but influence consumers priorities for a more adequate use of the network resources

## Slide 9: Congestion management (cont)
Web-sites are the main senders of traffic - not end-users.
Fixed costs (1) should be shared between W-S and end-users, given network effects.
Does not alter the need for congestion pricing, but does complicate it.
Notes: To whom will the traffic coming from a Web-site be charged?
The asymmetric nature of data traffic is such that the volume of traffic received after a request is usually far more important than the one of the request itself;
But the answer is induced by the request!
Some think that the Web-site should bear part of the associated costs;
Experiments based on asymmetric bandwidth reservation proved that the end-user is ready to pay for adequate inbound bandwidth if it improves the transfer rate of incoming data;
This doesn’t alter the need for congestion pricing but makes it more complicated

## Slide 10: Congestion management (cont)
The congestion charge
    should not apply when the network is uncongested
    should equal the marginal cost of delay if existing capacity is optimal.
    If a price higher than this can be charged, and the network still becomes congested, it indicates a profitable opportunity to increase capacity.
On the PSTN congestion pricing is charged during a time-of-day.
Not practical for the internet due to congestion periods being unpredictable. Alternative is some form of spot market.
Notes: The congestion charge is an ‘additional’ charge applicable only when the network is congested; in principle, it is seen like a penalty put on a new call whose treatment is susceptible to degrade the QoS provided to the consumers already using the network at a given time.
This means that, in economic terms, a consumer will take the decision to place a call at a given time if he deems the utility of the service at that time higher than the sum of the one-off price and the congestion penalty.
The principle of congestion pricing has been used for a long time on the PSTN by mean of “time-of-day” bands. But the time bands known on PSTNs are static.
The situation for the Internet seems to be more complex because the congestion periods are less likely to be predictable.Many researchers have been working on dynamic pricing mechanisms having the form of spot market.

## Slide 11: Congestion management (cont)
real-time Vickrey auction has been proposed
  All users admitted to the internet during this period would pay the bid price of the marginal user.
  This would be zero at uncongested periods
  Where there is insufficient capacity, it will provide a price that will signal that an increase in capacity is profitable (required).
Not practical as packets cannot be accounted for presently.
Notes: Much has been said on how to practically implement dynamic pricing; the most recurring idea is the “auctioning”
  All users admitted to the internet during this period would pay the bid price of the marginal user.
  This would be zero at uncongested periods
  Where there is insufficient capacity, it will provide a price that will signal that an increase in capacity is profitable (required).
But that is still theoretical. First of all the packets can not be accounted for presently, second, in order to garantee end-to-end QoS all the backbone providers should adopt the same pricing principles and have settlement agreements which might need a common regulatory framework. That is not the case yet.

## Slide 12: Future congestion management (cont)
Problems:
    RSVP has poor scalability
    IntServ requires a basic feedback mechanism to prevent network resources being cornered - not addressed by designers.
    Complexity of the IntServ RSVP model means it is not considered the way forward for the public internet.
DiffServ requires users wanting higher QoS to define their service profile, with tagged packets needing to fit this profile
Notes: New protocoles are designed to allow control of end-to-end QoS per data flow. They tend to enable QoS statistics to be raised to several levels, thus making it possible for real-time applications to run on the internet.
Option that appears more suitable for real-time service requires estimates of the demands to be generated by users so that resources are available.
The basic RSVP protocoles have drawbacks that makes their use in the public Internet rather difficult;
The two main protocoles that seem to raise more hope are DiffServ (Differentiated Services) and MPLS (MultiProtocole lebeled Switching): the first sets a way to differentiate the routing methods applied to different classes of packets; the second creates a chanel end-to-end after call set-up.

## Slide 13: Future congestion management
Traffic controls :
    Occur at admission
    traffic is scheduled according to customer profile
    traffic is sorted for different treatment
    network resources need to be allocated
Sorting, profiling, metering, happen at the boundaries between networks, where packet tags are addressed in aggregate - scalable 
Needs IPv6 to operate
No guarantees - requires QoS contracting and verification between ISPs.
Notes: In short, additional technical means are needed in order to better handle the traffic flows through over the network and allocate the necessary resources according to different classes;
What happens at the boundary of two networks will be more complexe. It is obvious that the implementation of IPv6 will facilitate the application of resource reservation protocoles, but will the ISPs accept to have QoS commitments between all of them?

## Slide 14: QoS and standards co-ordination
Strategic interests of 1 (or more) leading IBPs may be to differentiate itself by offering new services on-net only.
If this is likely to occur, vertical and some horizontal integration may well occur.
In a growing market where indirect network effects are strong, the incentive to co-operate with standards may counter incentive of IBPs to differentiate themselves.
Notes: One can fear that a Top-tiers high class Internet Bandwidth Provider be tempted to offer new real-time services on-net only, managing from inside his network, and limiting or forbidding any access to those services by other ISPs
But the risk of having such service islands, although real, will, on the long run, be mitigated by the economically rewarding effect of externality which increases the utility of those services as the number of their users grows.

## Slide 15: Conclusions
The internet is edging toward becoming an integrated services network
  e-mail; File Transfer Protocol (FTP); WWW; VoIP; Video.
Lack of efficient pricing structure running through the internet is delaying the development of ‘real-time’ services.
Ongoing technology developments are occurring, but economic issues need to be addressed.
Notes: The future generations of the Internet will make IP the basic protocol for integrated service network.
The technical limitations are under consideration now and no doubt that solutions exist and will be available soon;
Nevertheless, the transition time might be very long because of the actual commercial situation which is, to a large extent, at the advantage of a few big providers who will keep the status quo as long as possible.
The lack of an efficient end-to-end pricing structure, linking Qos and off-net agreements between ISPs, will be the most critical issue for the development of real-time services.
---oOo---

## Slide 16: Conclusions (cont)
Arguably the main problem will be in securing similar QoS for traffic going off-net.
  Accounting systems that provide ISPs with transparency will need to be developed.
Strategic interests of 1 or more IBPs may result in (vertical) agreements, vertical mergers, and real-time services only being provided on-net .
Email, WWW, FTP would still be universally provided. But new products might be on-net only.