## Slide 1: COSITU
The ITU model for the calculation of telephone service costs, tariffs and interconnection charges

## Slide 2
Note: The views expressed in this paper are those of the author and do not necessarily represent the opinions of ITU or its membership.
The terms and definitions used are the author’s own and can on no account be regarded as replacing the official ITU definitions.
pape-gorgui.toure@itu.int

## Slide 3: Definition of services for which COSITU calculates costs
Local(urban): Traffic carried solely within the network of the operator for which the calculations are made, between users located in the same local charging area,
Trunk(interurban): Traffic carried solely within the network of the operator for which the calculations are made, between users located in different local charging areas,
International outgoing: A call from an end-user connected to the network of the operator running the international gateway to a correspondent located outside the national boundaries,

## Slide 4: Definition of services for which COSITU calculates costs
Incoming international: A call from a user located outside the national boundaries to an end-user connected to the network of the operator running the international gateway,
Outgoing subregional: A call from an end-user connected to the network of the operator running the international gateway to a correspondent located outside the national boundaries, in a country which can be accessed by terrestrial media that are also used for trunk calls,

## Slide 5: Definition of services for which COSITU calculates costs
Subregional incoming: A call from a user located outside the national boundaries, in a country which can be accessed by terrestrial media also used for trunk traffic, to an end-user connected to the network of the operator running the international gateway,

## Slide 6: Definition of services for which COSITU calculates costs
International to international: A call between two non-subregional international correspondents via the international gateway of the operator for which the calculations are made,
International to subregional: A call from a non-subregional international correspondent to a subregional correspondent via the international gateway of the operator for which the calculations are made,

## Slide 7: Definition of services for which COSITU calculates costs
Subregional to international: A call from a subregional correspondent to a non-subregional international correspondent via the international gateway of the operator for which the calculations are made,
Subregional to subregional: A call between two subregional correspondents via the international gateway of the operator for which the calculations are made,

## Slide 8: Definition of services for which COSITU calculates costs
International to national: A call from an international correspondent to an operator without an international gateway located within the same political borders as the operator running the international gateway for which the calculations are made,
National to international: A call from an operator without an international gateway located within the same political borders as the operator running the international gateway for which the calculations are made, to an international correspondent,

## Slide 9: Definition of services for which COSITU calculates costs
Outgoing national: A call from an end-user of the network of the operator for which the calculations are made to another operator located within the same political borders as the first operator,
Incoming national, single transit: A call coming from the network of another national operator to an end-user located in the charging area of the interconnection point and connected to the network of the operator for which the calculations are made,

## Slide 10: Definition of services for which COSITU calculates costs
Incoming national, double transit: A call coming from the network of another national operator to an end-user located outside the charging area of the interconnection point and connected to the network of the operator for which the calculations are made,
National to national: A transit call between two national operators via the network of the operator for which the calculations are made,

## Slide 11: International boundaries of networks
Political boundaries do not always correspond to the international boundaries of networks: an imaginary point in the middle of the international area delimits the international “half-circuit” which completes the national network
COUNTRY A

## Slide 12: National boundaries of networks and the bases for interconnection
Within a given jurisdiction, the interconnection points set the network boundaries.
Costs incurred within the boundaries of a network are endogenous costs, which the operator is at liberty to improve itself.
Except for transit charges identified at transmission, payments to other correspondents for terminal traffic are exogenous costs which are not counted in determining costs at boundaries.

## Slide 13: Endogenous costs and exogenous costs
COUNTRY A
COUNTRY B
Endogenous costs
Exogenous costs

## Slide 14: Change management
Historical costs: Based on the cost price of equipment and services,
Current costs: Take account of the changing environment: falling prices of telecommunication equipment, currency depreciation. COSITU utilizes current costs as confirmed on the relevant market.

## Slide 15: Actual costs versus optimum costs
The costs (even current costs) incurred in offering the service are not necessarily optimum.
Efficiency of service provision can be an important factor.
The structural realities of the different kinds of markets should nonetheless be considered in making any judgements.

## Slide 16: Basic principles for cost models
Transparency:
  The open availability of information used in the cost derivation process in order to allow comprehension of the final rate from the vantage point of an external analyst.
Practicability:
  The ability to implement a costing methodology with reasonable demands being placed on data availability and data processing in order to keep the costing exercise economical yet still useful.

## Slide 17
Causality:
  The demonstration of a clear cause-and-effect relationship between service delivery, on the one hand, and the network elements and other resources used to provide it, on the other hand, taking account of relevant cost determinants (cost inducers).

## Slide 18
Contribution to common costs:
  Costing methodologies should provide for a reasonable contribution to common costs.
Efficiency:
  The provision of a forecast of cost reductions that result from a more efficient combination of resources.

## Slide 19: Stages of cost-orientated pricing allowed by COSITU
Cost of network components
Operation and maintenance costs
Amortization rules
Equipment price trends
Cost of capital
Cost of functional support
Identifiable direct and indirect costs
Other common costs
Routing table
Cost distribution
Unit endogenous cost of services
Tax components
Universal service obligations
Cost-orientated endogenous tariffs
Tariff rebalancing
USO simulation

## Slide 20: “Bottom-up” or “Top-down”
The difference between these two methods lies in the way the cost of network components is determined:
  Bottom-up (“scorched node” or “earth node”): a fictitious network is worked out from an an estimate of traffic needs based on statistical data;
  Top-down: the existing network is the source of all information.
COSITU accommodates both, the initial stage for the bottom-up method being completed outside the model.

## Slide 21: Full costs or incremental costs
The fully distributed costing method allocates all costs to all services,
The incremental costing method allocates a cost variation to the variation - from a previously established balance - in traffic volume that caused it,
Important: In terms of strict compliance with the rules of cost orientation, the incremental costing method requires complete rotation on all services and an additional allocation of common costs to balance operation (real or fictitious); in which case it is much the same as fully distributed costing.

## Slide 22: Full costs or incremental costs
In a market where several players are competing, it is in the interests of a service provider to apply the incremental costing method, without rotation, to a given service if that provider is already competitive in the other services (“value chain” theory),
Costing a service by the incremental costing method without rotation amounts to transferring the fixed costs of that service to the other other services (cross-subsidy!),
But economically speaking it is acceptable as long as it produces neither an increase in the price of the other services nor anti-competitive arbitrage, which make the market less efficient.

## Slide 23: Full costs or incremental costs
Whatever the methods used to determine costs and traffic, the COSITU model can accommodate them,
COSITU has, however, been optimized for use of real information from the accounts and technical data of real network operators with a view to equitable allocation of costs to the services that generate them, collectively or separately,
COSITU is unaffected by technological choice, addressing directly the services sold – retail or wholesale.

## Slide 24: Adjusted depreciation(1/3)
Linear depreciation is the rule most widely applied in the accounts of telecommunication operators.
It is nevertheless possible to take account of the natural evolution of the price of equipment in the specific market and adjust the depreciation accordingly.

## Slide 25: Adjusted depreciation (2/3)
Currency depreciation must also be taken into account:
where:
  C0 is the value of one SDR in the national currency in the year of acquisition;
  Cn is the value of one SDR in the national currency in year N;
statistically, the age of the equipment of an ordinary telecommunication network is D/2 (half the lifetime).

## Slide 26: Adjusted depreciation (3/3)
ACC=AMO*((1+)D/2 /(1-)D/2 –1)
  where:
    ACC = adjustment to current costs
    AMO = amortization allowance
     = annual average growth rate in the price of equipment
     = average annual rate of currency depreciation
    D = depreciation period

## Slide 27: Efficiency (1/2)
Efficiency is calculated by combining the following factors:
  installed capacity;
  utilized capacity;
  average annual growth rate in number of subscribers;
  replenishment period.

## Slide 28: Efficiency (2/2)
    K’= Max(0 ;K - Ku*[(1+)N-1] )
where :
  K ’ is the idle capacity;
  K is the difference between the installed capacity and the utilized capacity;
  Ku is the utilized capacity;
  τ is the annual average growth rate in the number of subscribers;
  N is the necessary extension time.

## Slide 29: Causality
The cost of the local loop is not sensitive to variation in traffic volume,
It is a basic investment which serves the global network,
The cost of the local loop must be recovered as customary through all the services.

## Slide 30: Operating and maintenance costs
Cost of inputs
  Purchases and variations in stock;
  Transport;
  Outside services
Personnel costs
Taxes and levies
Other charges
Financial and similar charges
Operating provisions

## Slide 31: Cost of capital
Combined effect of debt and equity
Creditors demand interest
Owners demand dividends
The ratio
gives an idea of current return on equity
However, investors often demand a return in keeping with conditions prevailing on the international financial market.
net_profit / equity

## Slide 32: Cost of capital
The Capital asset pricing model (CAPM) gives an indication of how to determine a minimum return on equity in a given market:

## Slide 33: Calculating BETA
The BETA of a stock corresponds to the slope of regression of its profitability as compared to that of the market, in other words, by definition:

## Slide 34: BETA of major European groups

## Slide 35: Evolution of risk premium in European market

## Slide 36: Evolution of risk premium in emerging market countries

## Slide 37: BETA: conclusions
The following shows that the CAPM is useful in calculating expected returns on equity only if there is abundant and reliable data pertaining to the market in question.
COSITU does not rely only on this approach, given the specificities of developing countries,
It has an additional approach, which is essentially a comparative one.

## Slide 38: Some basic facts
Markets in developing countries are exposed to adverse circumstances of all kinds, the effects of which are, for the most part, measured in terms of monetary risk,
Most loans on these markets (in the telecommunication sector) are in convertible currencies,
New investors in these markets also have investments in international financial markets.

## Slide 39: Consequences
The interest rate on hard currency debts must be adjusted for the risk premium of the issuing markets and for local conditions using the currency depreciation rate,
The expected rate-of-return must also be adjusted, on the basis of indications from the international financial market or the owners’ market of origin.

## Slide 40: Calculating the risk premium linked to currency depreciation
n = average duration of loan
ε = currency depreciation
iF = risk – free money rate

## Slide 41: Returns on equity: Europe

## Slide 42: Global interest rates

## Slide 43: Example
Taking a telecommunication company expecting a return on equity of 6.6% in Europe;
Assuming an interest rate of 5.8% over ten years;
In order for the enterprise to have an interest in investing in the market of a developing country where the differential currency depreciation rate is 3.5% per annum and to obtain the same return on capital in Euros over ten years, its expected rate of return in the local currency would need to be 10.93%.

## Slide 44: The cost of capital: conclusion
COSITU is able to calculate, assuming a preponderant risk of inflation for telecommunication companies in developing countries (sector risk ~ market risk -> BETA ~ 1), the essential components of the cost of capital as adjusted to local conditions.
Thereafter the traditional formula for the cost of capital applies:

## Slide 45: Special costs
Some special costs are easy to single out even where the operator does not have analytical cost accounting:
  Study of products and services
  Charging
  Advertising
  Distribution network
  Customer service
  International activities
  National activities
  Provisions for bad debts

## Slide 46: Routing table
The routing table is an essential instrument for cost-orientated charging,
It allows allocation to every service, according to the intensity of demand it places on each one, part of the resources needed for its production,
The cost driver used by COSITU is traffic volume (adjusted by the geographical correction coefficient) for network component cost allocation.

## Slide 47: Unit costs and reference costs
On the basis of the routing table, COSITU allocates to services their share of each cost component,
The resulting cost of a service is divided by the corresponding real traffic volume in order to obtain the unit cost of the service,
At this stage, the COSITU server allows an online comparison with other telephone network operators,
The costs here are endogenous intrinsic costs which do not take into account the specific requirements of States.

## Slide 48: Moving from costs to tariffs

## Slide 49: Other tariff elements
The regulatory authority may impose constraints on the prices practised by a telecommunication service provider:
  Profit tax
  Contribution to universal service obligations (USO)
  Access deficit.

## Slide 50: Profit tax (1/2)
An operator’s profits are distributed between:
  Shareholders, through return on capital
  The State, through statutory taxation of profits.
Shareholders often demand an after-tax return on capital.

## Slide 51: Profit tax (2/2)

## Slide 52: Contribution to universal service obligations
A State may require a deduction from an operator’s revenue for the purpose of financing USO costs.
USOs may or may not be combined with the access deficit.
Where applicable,

## Slide 53: Access deficit (1/4)
An access deficit may occur when the regulatory authority opposes cost-based adjustment of the following components:
  The connection charge
  The monthly subscription
  The price per minute of a local call
  The price per minute of a trunk call.

## Slide 54: Access deficit (2/4)
In redistributing the access deficit, it must be borne in mind that only local users pay the connection charge and monthly subscription.
The charge per minute for outgoing calls should be reduced by:

## Slide 55: Access deficit (3/4)
The amount of the access deficit is obtained by the following formula:

## Slide 56: Access deficit (4/4)
If D > 0, the access deficit is reallocated to all telecommunication services provided by the operator,
If D ≤ 0, there is no deficit. The surplus may be allocated to local and trunk calls in order to reduce and rebalance their tariffs.

## Slide 57: Generic formula for distribution of other tariff elements
Once calculated, the profit tax, the access deficit and the contribution to universal service obligations must be allocated to the appropriate services,
The generic formula for this purpose is:

## Slide 58: COSITU assumptions
National transit offered if the third parties to be interconnected can be accessed inside the same tariff area (« Hot potatoe routing »),
National traffic to/from international via a direct link to international transit centre,
For certain specific applications, the model may need slight external reprocessing; the necessary elements are available inter alia in the report on unit costs.

## Slide 59: "Hot potato" routing
The partners in a peering agreement can meet at several geographical locations
To ensure parity of costs incurred, backbones adopt the "hot potato" routing mechanism
ISP Y
ISP X
A
B

## Slide 60: Interconnection of ISPs and mobiles
pape-gorgui.toure@itu.int
Note – The views expressed in this paper are those of the author and do not necessarily represent the opinions of ITU and its membership

## Slide 61: Technical requirements for interconnection
Definition of interfaces in accordance with ITU-T recommendations (e.g. R2, SS7);
Creation of a physical link
  Belonging to one of the parties;
  In co-ownership in accordance with the “half-circuit” regime;
  Composed of two one-way special bundles.

## Slide 63: Fixed network Access and switching
Switching
Access

## Slide 64: Mobile network Acces and switching
Access
Switching

## Slide 65: Application of COSITU to mobile networks
Notions of capacity and growth in mobile communications:
  BSC access capacity;
  utilized capacity;
  BSC traffic growth adjusted to growth of utilized capacity;
Determination of average monthly subscription taking into account the weight of prepaid services.

## Slide 66: Specific responsibilities of NRAs
The interconnection interfaces must be clearly specified and publicly available,
Should be part of the specifications common to all operators and be recognized during the licence awarding process,
The basic principles for calculating interconnection charges, including those relating to discounts for volume, should be public and common to all operators,
The effect of the application of USO policies should be borne by all network operators on an equitable basis,
The main objective of interconnection should be to maximize the economic advantages of externalities and reduce service costs/prices.

## Slide 67: Internet telephony
There are three ways of accessing the telephone network via the Internet:
  A dedicated link (including cyber cafes) with the ISP: no interconnection with other national operators;
  A domestic call terminating on a set of modems of an ISP connected to the Internet
  A national call to a VoIP server connected to the Internet.
The costs of providing an end-to-end service are different in each of the above situations.

## Slide 68
ISP
ISP INTERNET BACKBONE
ONATEL
NETWORK
Telephone
Computer
with a
modem
Boundary
Telephone
Internet data Servers
Workstation
Router
Internet
CIT Voice server
with
TCP/IP capabilities
R2 or SS7 circuits
Modems
Router
unidirectional
telephone
lines
Workstation
A
B
C
Telephone

## Slide 69: Avoid regulatory arbitrage
Countries banning Internet telephony may deprive their economies of major opportunities,
But VoIP must not be introduced outside the general regulatory framework solely on account of the technology used,
The economic efficiency of VoIP could be reduced if the rules of cost orientation are not applied to all segments of the network, wherever necessary,
Wherever there is an access deficit, equitable allocation of the USO costs to all network operators, including VoIP providers, will be decisive for the general growth of the service.

## Slide 70: Types of VoIP calls
There are different kinds of VoIP calls:
  C1: a national end-user calling via link A (computer-to-computer/telephone);
  C2: a national end-user calling via link B (telephone-to-telephone);
  C3: an international ISP calling via link A (computer-to-computer termination: the connection must first be established locally);
  C4: an international ISP calling via link B (computer/telephone-to-telephone termination).

## Slide 71: Fraudulent links
If the VoIP gateway of the ISP or the mobile network is connected to the network through subscriber lines and terminates calls on the latter at the price of a domestic call, the interconnection interface would no longer be in conformity with interconnection rules,
This can be done by deviating normal telephone lines from their normal functions,
To avoid this, type “A” links should be dedicated outgoing, and consumption of type “C” links should be regularly monitored.

## Slide 73: Analysis of C1 type calls (computer-to- computer/telephone)
The end user pays the price of a national call in order to access the ISP’s modems,
If there is an access deficit, the call will be subsidized but since it is an end-to-end domestic call, the Internet access will be treated as a value-added service, so no measures are needed for outgoing VoIP calls using this link,
However, a business-rate monthly subscription should be applied to the lines of this bundle. To avoid fraud, the lines should be dedicated outgoing.

## Slide 75: Analysis of type C2 calls (telephone to telephone)
Type “B” links obey the interconnection rules,
The telephone network operator will bear the cost of an outgoing national call, the endogenous cost of which can easily be calculated with COSITU,
It takes account not only of CAPEX, OPEX and the costs of capital, but also taxes and part of the USO costs,
Depending on who collects the customer’s payments (direct/cascade method), there may be several types of arrangements between TPH and VoIP providers.

## Slide 76
ISP
ISP INTERNET BACKBONE
ONATEL
NETWORK
Telephone
Computer
with a
modem
Boundary
Telephone
Internet data Servers
Workstation
Router
Internet
CIT Voice server
with
TCP/IP capabilities
R2 or SS7 circuits
Modems
Router
unidirectional
telephone
lines
Workstation
A
B
C
Telephone

## Slide 77: Analysis of type C3 calls (computer-to-computer termination: the connection must first be established locally)
In order to avoid fraud of any kind, telephone calls from the VoIP provider to the TPH provider will have to be prohibited.
But if the call is generated by the local TPH customer, a VoIP incoming international call may be generated (e.g. netmeeting calls),
In this case the VoIP is a value-added service,
No implications for interconnection rules.

## Slide 78
ISP
ISP INTERNET BACKBONE
ONATEL
NETWORK
Telephone
Computer
with a
modem
Boundary
Telephone
Internet data Servers
Workstation
Router
Internet
CIT Voice server
with
TCP/IP capabilities
R2 or SS7 circuits
Modems
Router
unidirectional
telephone
lines
Workstation
A
B
C
Telephone

## Slide 79: Analysis of type C4 calls (computer/telephone-to-telephone termination)
Normal call termination,
The TPH operator will receive the price of an incoming national call, depending on where the latter terminates:
  single transit if the call terminates in the tariff area where the interconnection point is located;
  double transit if it terminates outside that area.
COSITU can easily calculate the bases of these tariffs,
If this type of call is terminated on the TPH network via a type “C” link, the result will be a fraudulent situation because the price of domestic calls will in all likelihood be largely subsidized wherever there is an access deficit (see COSITU).

## Slide 80
ISP
ISP INTERNET BACKBONE
ONATEL
NETWORK
Telephone
Computer
with a
modem
Boundary
Telephone
Internet data Servers
Workstation
Router
Internet
CIT Voice server
with
TCP/IP capabilities
R2 or SS7 circuits
Modems
Router
unidirectional
telephone
lines
Workstation
A
B
C
Telephone

## Slide 81: The AFRICOM case

## Slide 82: Actual prices

## Slide 83: Cost orientated tariff basis

## Slide 84: Cost based tariff basis

## Slide 85: Status of VoIP providers in Afriland
The USO policy choices of the public authorities generate an access deficit of USD 151 million for Africom,
Given the size of the deficit, all telephone service providers in Afriland should bear a fair share of it,
If these service providers operate a network, whatever the technology, they must have operator status and be subject to statutory USO constraints,
This should apply to Afriland VoIP providers.

## Slide 86: Equalization charge
Afriland’s USO policy creates a transfer of charges from domestic calls to international calls and domestic calls to national calls,
The charge transferred to the outgoing international service is equal to the difference between the cost-orientated tariffs and the cost-based tariffs: USD 0.37 - USD 0.20 = USD 0.17,
This additional charge, clear of all inefficiency costs and due solely to USO policy, is called the “equalization charge”,
It should be applied to all international telephone service providers not participating in USO costs through the interconnection mechanism, in order to avoid regulatory arbitration: e.g. cyber cafes,
The proceeds of the equalization charge are a resource belonging to the State which the incumbent operator may not claim.

## Slide 87: Monthly subscription
Type “A” link telephone lines must not be subsidized. Africom should apply a monthly subscription charge of USD 22 instead of the current USD 5.

## Slide 88: Link “B” interconnection charges
From | To | Via | Africom must keep
Africom | International or National | National | USD 0.1693
International | National | Africom | USD 0.2735
National 1 | National 2 | Africom | USD 0.1013
National | International | Africom | USD 0.2735
National | Africom single | Africom | USD 0.1266
National | Africom double | Africom | USD 0.2486

## Slide 89: Example 1: Africom customer to international customer via ISPTEL
Termination charge Afriland-ISPTEL to Euroland-ISPTEL: USD 0.10,
Endogenous cost of Afriland-ISPTEL: USD 0.15
Minimum tariff when an Africom customer calls a Euroland customer via ISPTEL: 0.1693 + 0.15 + 0.10 = USD 0.4193
Africom keeps USD 0.1693 and gives USD 0.25 to ISPTEL and its other partners.

## Slide 90: Example 2: International call from a cybercafé
Endogenous costs of Afriland-ISPTEL from a cybercafé, including the latter’s costs: USD 0.12,
Termination charge Afriland-ISPTEL to Euroland-ISPTEL: USD 0.10,
Minimum charge when cybercafé customer calls a Euroland customer via ISPTEL 0.17 + 0.12 + 0.10 = USD 0.39
ISPTEL pays USD 0.17 to the Afriland department of finance.

## Slide 91: Example 3: ISPTEL routes a call which has to be terminated by Africom
For example, ISPTEL terminates an international call in the tariff area of the interconnection point:
  ISPTEL pays Africom USD 0.1266
ISPTEL terminates an international call outside the tariff area of the interconnection point:
  ISPTEL pays Africom USD 0.2486
If 60% of the traffic terminated is “single transit”, ISPTEL and Africom could negotiate a single termination charge equal to: 0.1266 * 0.6 + 0.2486 * 0.4 = USD 0.1754