## Slide 1
Access Network Costing

## Slide 2: Conceptual Phases
Identifying the fundamentals of the access network in terms of:

## Slide 3: 1.Usage
Local Loop has Multi functionality:
Call termination
Call origination
Internet
Fax
Etc

## Slide 4: Continued
Facilities, in large measure are dedicated to subscribers.
Intense competition, since prime goal of new entrants is to develop substantial subscriber base.
Interconnection at points of the access network is optional.

## Slide 5: 2. Economics of Costing
Based on the principles of LEC
C = ƒ(Ed/Nd)-ß
Where
C is unit cost;
E is total expenditure;
N is number of lines;
D is a distance factor; and
ß is the efficiency factor as appropriately estimated.

## Slide 6: 3. Principal Cost driver/s
Since distance is an important cost driver on the access network, country is zoned in terms of:
Urban
Sub-urban
Rural
Remote rural
The zoning matrix is not cast in stone and can be altered to suit the circumstances of the country

## Slide 7: 4.Network Boundary
Clear demarcation of the access network from the conveyance network in order to identify the relevant network components.
At p2 Diagram 1, identifies the access network comprising transmission components that link the MDF (at a remote or local switch) to customer premises.

## Slide 8: 5. Network Technology
Most likely, in proportions of Copper,fibre, coax, or wireless technology as appropriate
At diagram 3. p2, The for demonstrative purposes, the model concentrates on copper, being the dominant access technology in developing countries and therefore segments the access network in terms of: Feeder (primary and sub-primary extensions); distribution and service access (drop, building, entrance and network interface)

## Slide 9: 6. Network Efficiency
Since the unit cost of the access network is invariably traffic insensitive, network efficiency is circumscribed largely by economies of scale and to a lesser extent by factors relating to OPEX and capital cost.

## Slide 10: 7. Accounting Modality
Total Cost =
Annualized: direct costs + indirect costs + common cost + capital cost (inclusive of interest on debt and return to equity) + tax and exogenous expenses.
Such cost should be fully recovered by rentals or one off purchases.

## Slide 11: Detail Costing Iterations
Estimating LEC Unit Access Cost
&
Access deficit/surplus

## Slide 12: Step 1.
Collect network information re technology.
Specify formula for estimating unit cost (LEC).
Specify bases for derivation of efficiency factor/s.
Specify qualitative and quantitative formula for assessment of access deficit. i.e.difference. between cost per line and charge per line.

## Slide 13: Step 2.
Collect from operator/s data re: customer connections and collate such in terms of:
Urban
Sub-urban
Rural
Remote rural.
Note that this classification is optional.

## Slide 14: Step 3.
Collect and classify data in terms of connections per zone to different types of switches
E.g. Urban and sub-urban customers are likely to be connected to LS, rural customers to remote switches and remote rural customers may be served with radio connections.

## Slide 15: Step 4
Simulate average distance of connection per customer in each geographic zone.
The average of customer radius.
This information may be accessed from the operator.

## Slide 16: Step 5
Collection of data to profile network facilities re:
Number of line cards
Non-sensitive parts of switch
Number, size and average distance of dedicated single pair of cables between customer premises and distribution point.
Number, size and average distance re multi-pair cables connecting DP to cable junction.
Number, size and average distance re: multi-pair cables connecting CJs.

## Slide 17: Step 5 Continued
Number of pillars for connections using RSS/RSUs
Number, size and average distance of multi-pair cables connecting last CJ/Pillar to MDF.
Number and type of other equipment comprising the line side of connecting switch used exclusively for access.
Average trench length per geographic Area.
Number of service sharing trench. See (Tables I & II).

## Slide 18: Step 6
Establish accounting format re:
Direct cost whether based on current or adjusted historical costing.
Specify methodology for allocating shared costs.
Specify methodology for arriving at factor/s for common costs.
Specify methodology for estimating efficient OPEX.
Specify methodology for estimating opportunity cost of Capital.

## Slide 19: Step 7
Estimate total component investment cost by zone: (Table III)

## Slide 20: Step 8
Estimate demand per zone in terms of current demand, Da and expected demand, Dp.
Da = Ln + Ln*
Where Ln is number of existing lines in the zone.
Ln* is the unfulfilled request for line installation in same zone.

## Slide 21: Step 8 Continued
Estimate:Potential/Expected demand, Dp:
Dp = Daά
Where ά is the long run growth factor derived on the basis of time series or other credible forecasting method as supplied to the regulator by the operator.
Total demand is therefore:
Dt = Da + Daά
= Da (1+ά).

## Slide 22: Step 9: Adjustment for Efficiency
Installed capacity over a specific time period is a function of current installed lines plus a factor for growth. i.e.
Optimal efficiency is:
Installed capacity (C)/total number of lines (Dt) = 0.
Where USO and or political imposition are/is applicable the optimal efficiency becomes;
Installed Capacity (including provision for USO) (C! )/Total number of lines (Dt) = 0

## Slide 23: Step 9 Cost Adjustment
Where:
C!/ Dt = λ
If, for example, λ = 1.15 then the cost of C! should be adjusted by 15% or a factor thereof,

## Slide 24: Step 10
Area | C!(1-λi) | Dt | C!(1-λi)/Dt
Urban | C!(1-λ i)u | Dtu | C!(1-λ i)u/ Dtu
Sub Urban | C!(1-λ i)s | Dts | C!(1-λ i)s / Dts
Rural | C!(1-λ i)r | Dtr | C!(1-λ i)r/Dtr
R/rural | C!(1-λ i)R | DtR | C!(1-λ i)R/ DtR

## Slide 25: Step 11: Estimate Average Unit Cost
Average unit cost may be derived by estimating the weighted average unit cost Wg for all zones:
Wg = {[C!(1-λ i)u/ Dt ]w1, [C!(1-λ i)s/ Dt ]w2,
[C!(1-λ i)r/ Dt ]w3, [C!(1-λ i)R/ Dt ]w4}/4
Where w1 – w4 are the respective weights assigned to the different zones.

## Slide 26: Step 12. Derive Unit Subscription
By allocating other cost, Þ e.g.:
Bad debt
Tax (if not included in direct cost)
Etc.
So Unit Subscription Cost Sc is
Sc= Wg+Þ

## Slide 27: Step 13
Estimating Access deficit/Access Surplus @.
@ = Wg+Þ/Current Access charge
If @ > 1 the rebalancing factor is the value of @.
If @ is < 1 the access charge reduction factor is the value of @.