## Slide 1: IPCablecom Security
Eric Rosenfeld, CableLabs
Sasha Medvinsky, Motorola
Simon Kang, Motorola
ITU IPCablecom Mediacom Workshop
March 13, 2002
Geneva, Switzerland

## Slide 2: Agenda
IPCablecom Overview
How it Works
Services and Capabilities
Security Goals of IPCablecom
IPCablecom Security Architecture
Security Mechanisms & Component
Summary

## Slide 3: What is IPCablecom?
IPCablecom is a set of standards that define protocols and functional requirements for the purpose of providing Quality-of-Service (QoS) enhanced secure communications using the Internet Protocol (IP) over the cable television Hybrid Fiber Coax (HFC) J.112 network

## Slide 4: IPCablecom Framework
Broadband Modem Physical Layer
Media Access Control
Internet Protocol
IPCablecom Protocols
Voice/Video Telephony
Conferencing
Video/Data
Applications
J.112
IPCablecom

## Slide 5: IPCablecom How it Works
IPCablecom
Servers
PSTN
HFC
J.112
Cable Modem
CMTS
(J.112 AN)
Cable IP Network
Internet
Upgrade to
IPCablecom
+ MTA
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: IPCablecom Architecture
Managed IP Backbone
(QoS Features)
(Headend, Local, Regional)
PSTN
Media Gateway
Signaling Gateway
Call Management
Server
HFC access
network
(J.112)
MTA
Embedded MTA
CMTS
HFC access
network
(J.112)
Cable
Modem
MTA
Embedded MTA
CMTS
Media Gateway
Controller
OSS Back Office
Media
Servers
Announcement Servers
Conference Mixing Bridges
...
Billing
Provisioning
Problem Resolution
DHCP Servers
TFTP Servers
Key Distribution Center (KDC)
Cable
Modem

## Slide 7: IPCablecom : What Equipment?
Home:
  Embedded Multimedia Terminal Adapter (MTA) -- cable modem with RJ-11 jacks
Headend:
  Cable Modem Termination System (CMTS): J.112 AN
  IPCablecom Servers: Call Management Server (CMS), Record Keeping Server (RKS), Device Provisioning Server, Key Distribution Center (KDC)
  Gateways: To link IP calls to backbone or PSTN

## Slide 8: And now the security…

## Slide 9: Why do we need security?
Threats to the IPCablecom Network
  Threats exist because:
    Shared network
    Access in the users home
    Valued functionality
  Types of threats:
    Network attacks
    Theft of service
    Eavesdropping
    Denial of Service

## Slide 10: Security Services provided by J.112
Baseline Privacy Interface + (BPI+)
  Privacy between the Cable Modem and CMTS
    DES encryption
  Protection from theft of Service
    Authentication of Cable Modems via X.509 digital certificates
  Enable secure code download to the Cable Modem
    Authentication of Cable Modem software image via X.509 Code Verification Certificate

## Slide 11: BPI+ Applicability to IPCablecom
Embedded MTAs rely on Cable Modem for secure code download
Privacy of J.112 QoS messages prevents some denial of service attacks
Theft of Service protection doesn’t apply:
  CPEs behind a CM are not authenticated
  IP Telephony servers also not authenticated
Additional security at application layer is needed to protect IPCablecom services

## Slide 12: IPCablecom Security Objectives
End-to-end secure communication
  Must be at least as secure as PSTN networks
Protection for the user
  Ensure privacy of media sessions
Protection for the operator
  Combat theft-of-service
  Protect infrastructure
Comprehensive plan
  Who/What needs to protect and why?
  When/Why do we protect this information?
  How will we incorporate security?

## Slide 13: IPCablecom Security Objectives
Use open standards whenever possible
Conduct a risk assessment
Provide a reasonable level of security
Specify Interface security
  No device or operator network security
    Assume operators must have reasonable network management security policy
Require J.112 networks with BPI+ enabled

## Slide 14: IPCablecom Security Architecture

## Slide 15: Security Mechanisms
Kerberos
  Centralized network authentication via a Key Distribution Center (KDC)
  Public Key Initialization (PKINIT)
    Digital Certificates are used to authenticate the MTA to the KDC and KDC to MTA
  Key Management
    Allows MTAs and CMSs to agree on cryptographic keys for secure communications

## Slide 16: Security Mechanisms
IPsec
  IP-layer security protocol (IETF standard)
  Encapsulating Security Payload (ESP)
    Transport mode for end-to-end security
    Privacy/authentication/integrity of payload
      3DES, HMAC SHA1 or HMAC MD5
  Initial Authentication & Key Management provided by:
    Kerberos+PKINIT for MTAs
    Internet Key Exchange (IKE) with pre-shared keys for infrastructure components (CMS, CMTS, RKS, Gateways)

## Slide 17: Security Mechanisms
SNMPv3 security
  SNMPv3 is used to monitor & manage MTAs
  Initial Authentication & Key Management
    Kerberos+PKINIT
  Message Authentication & Integrity
    HMAC MD5 algorithm
  Privacy (optional)
    DES algorithm

## Slide 18: Security Mechanisms
Call Signaling Security
  NCS, TCAP/IP, ISTP, and TGCP Protocols
  Protocol security provided by IPsec
  Mix of authentication & key management technologies:
    IKE with pre-shared keys for servers
      Default for IPsec, comes bundled with off-the-shelf implementations
    Kerberos+PKINIT for MTAs
      Needed to address scalability issues on the CMS-MTA interface

## Slide 19: Security Mechanisms
RTP/RTCP (Media Stream)
  Initial Authentication
    Each end-point (MTA or MG) authenticated by the Call Management Server
  Key Management
    Via IPsec-secured Network-based Call Signaling (NCS)
  Privacy
    Advanced Encryption Standard (AES)
  Authentication & Integrity (optional)
    MMH (Multilinear Modular Hash)

## Slide 20: Key Distribution Center (KDC)
The only standalone security component in IPCablecom
Acts as a trusted third-party authentication service
Implements:
  Kerberos version 5
  PKINIT w/X.509 digital certificates

## Slide 21: Multimedia Terminal Adapter
X.509 Digital Certificates for authentication
  IP Telephony Root CA Certificate
  MTA Manufacturer CA Certificate
  MTA Device Certificate
    MTA Private Key
FIPS 140-1 Cryptographic Module
  Level 1 required (minimal physical security)
  Additional physical security recommended for higher value services
Random Number Generator
AES, MMH, IPsec, Kerberos+PKINIT
Embedded J.112 CM with BPI+

## Slide 22: Device Provisioning Server
Authentication & Key Management
  Kerberos+PKINIT authentication
Integrity & Privacy
  SNMPv3 security
    Authentication
      HMAC MD5
    Privacy (optional)
      DES

## Slide 23: PSTN Gateways
Media Gateway Controller (MGC)
  IPsec,IKE w/pre-shared keys for call signaling
Media Gateway (MG)
  AES, MMH for media stream
  IPsec, IKE w/pre-shared keys for call signaling
Signaling Gateway (SG)
  IPsec, IKE w/pre-shared keys for call signaling

## Slide 24: Other Components
Cable Modem Termination System (CMTS)
  J.112 Access Node (AN) w/BPI+
  IPsec w/pre-shared keys and RADIUS authentication for QoS interface with CMS
Call Management Server (CMS)
  IPsec w/pre-shared keys
  IPsec w/Kerberized Key Management for MTAs
Record Keeping Server (RKS)
  IPsec w/pre-shared keys for billing events

## Slide 25: On-Net to Off-Net Media Path
PSTN
Cable
Modem
MTA
Media
Gateway
Hi Mom. How
are you today?
HmDMSmB7HTKgEwLE3aSmttcBYAizqPicdTZKyXxVp7A4GxaPw/BH7kwYtuKxEr3nPS70i15nB+z7miTw2TXwrc+pYGO+FNvIScRQIrlaOqwYUMLF+5LjagzZSlbX8rrw+Y2uE21YZJxIirVuTX/tZI9af16nz75VcF5x0N4YRAjtjwpo3GW0CK+B4ihcg/6
MTA Encrypts
MG Decrypts
Hi Mom. How
are you today?
CMTS
RTP / RTCP
AES, MMH

## Slide 26: Summary
IPCablecom provides QoS-enhanced secure communications
Security is a major component and is integrated into the architecture
A range of security protocols and services are used
IPCablecom security architecture is fully defined in the J.170 recommendation

## Slide 27: For More Information…
Eric Rosenfeld
CableLabs
PacketCable Security Architect
e.rosenfeld@cablelabs.com
Sasha Medvinsky
Motorola
Senior Staff Engineer
smedvinsky@motorola.com
Simon Kang
Motorola
International Regulatory and Standards Specialist
simonkang@motorola.com