## Slide 1
IP Cablecom and MEDIACOM 2004
Prediction and Monitoring of
Quality for VoIP services Vincent Barriac – France Télécom R&D SG12 Q.16 Rapporteur

## Slide 2: Voice Quality on IP networks (1)
The main Voice Quality impairments related to the transmission on IP networks are :
an important transmission delay (essentially caused by the use of low bit rate coders) :
  echo when the loop delay exceeds 40 ms,
  no interactivity possibility beyond 400 ms of one way delay,
the variation of transmission delay (due to packet loss, but not perceptible if less than 30 ms),
IP Cablecom and MEDIACOM 2004

## Slide 3: Voice Quality on IP networks (2)
Voice Quality impairments related to the transmission on IP networks are :
the loss of information (due to packet loss) :
  Perceptible and annoying from 2 or 3 % of loss,
  difficult to support above 10 %,
  unbearable above 20 %,
signal distortion (caused by the use of low bit rate coders) :
  E.g. :G.711 better than G.729, itself better than G.723.1.
IP Cablecom and MEDIACOM 2004

## Slide 4: The principal metrics for voice quality on IP networks
1) End-to-end transmission delay,
2) Speech quality,
3) Packet loss rate,
4) Variation of transmission delay (or jitter),
5) Annoyance due to echo (electrical or acoustical).
IP Cablecom and MEDIACOM 2004

## Slide 5: Problems for the evaluation of voice quality in IP networks
Voice quality is time variant («unguaranteed quality»)
Causes : non constant packet path (and thus transmission time) and network load (and thus packet loss rate)
Consequences : classical subjective and objective assessment methods must evolve to adapt
  Subjective : continuous scoring,
  Objective : new parameters to characterise and supervise, new measurement tools to develop.
IP Cablecom and MEDIACOM 2004

## Slide 6: How to measure voice quality ?
Two types of tools :
Non-intrusive (I.N.M.D.) : on real communication without reference signal, better for the supervision of QoS inside networks,
End-to-end intrusive : on test calls with reference signal, better fitted for the measurement of quality as perceived by end users.
PSTN
NAS/VoIP gateway
IP
Gatekeeper
Telephone
H.323
Terminal
I.N.M.D.
End to end
measurement unit
End to end
measurement unit
End to end
measurement unit
End to end
measurement unit
IP Cablecom and MEDIACOM 2004

## Slide 7: End-to-end assessment :PESQ
Intrusive measurement performed on speech signal.
Output : MOS score (from 1 to 5)
One way measurement :
  does not take into account propagation times,
  not applicable for conversational situations (echo, double talk).
Independent on speaker (male ou female) and language.
Takes in consideration propagation delay variations, and thus is applicable to transmission via packet networks (ex. : VoIP).
Independent on the measurement interface :
  requires only PCM files at 8 or 16 kHz.
Standardised Model (P.862 Recommendation) validated on many subjective databases, recognised as a reliable and cheap alternative to subjective tests.
IP Cablecom and MEDIACOM 2004

## Slide 8: Non-intrusive monitoring : INMDs
Measurement performed on real communications (speech signal + signalling/protocol)
Output : call detailed reports
Network interface : T1/E1 (measurement on all time slots and both directions)
P.561 Recommendation
  specifies the required parameters (speech level, noise level, echo, round trip delay), measurement ranges and accuracies
  to be updated during the 2001-2004 study period to take into account new interfaces (Ethernet) and new parameters (mainly related to VoIP)
IP Cablecom and MEDIACOM 2004

## Slide 9: Single ended models
Measurement performed on speech signal (need for a discrimination between types of signal)
Non-intrusive measurement (no reference signal)
Input : standard PCM files (as for P.862)
Output : MOS score (idem)
Trained on subjective databases including conditions with VoIP impairments
Standardisation process running under Q.9/12 (4 or 5 candidate algorithms)
IP Cablecom and MEDIACOM 2004

## Slide 10: Prediction of end-to-end quality 1 : the E-model
ITU-T G.107 Recommendation
Transmission planning tool
Subjective effects of all impairments are additive
The E-Model output is a score (R) between 0 and 100
Takes into account :
  Transmission delay and echo (speaker, listener and sidetone)
  Levels (SNR, noise, loudness ratings)
  Packet loss
  Low bit rate coding (Ie factors)
IP Cablecom and MEDIACOM 2004

## Slide 11: E-model Voice Quality Categories according to G.109 Recommendation
R : transmission quality index calculated with the E-model (G.107)
IP Cablecom and MEDIACOM 2004

## Slide 12: Prediction of end-to-end quality 2 : the call clarity index (CCI)
ITU-T P.562 Recommendation
Inspired by the CATNAP/SUBMOD model
Based on loudness ratings
Takes into account the P.561 parameters :
  Transmission delay and echo
  Levels (SNR, noise)
New models similar to the CCI and adapted to the VoIP context are being developed and will be soon standardised under Q.16/12.
IP Cablecom and MEDIACOM 2004