## Slide 1
Notes: Presentation gibt Überblick
Goals achieved in 2001
Current activities
Outlook

## Slide 2: Aurora Activities
Standardisation of DSR Front-End including Compression
  DSR Front-End Standard (WI007) published in Feb 2000
  Advanced Front-End (WI008) selected in Feb 2002 Approval of Standard planned for Mid 2002
DSR Front-End Extension for Tonal-Language Recognition and Speech Reconstruction (WI 030)
Definition of Applications and Protocols
  Architecture definition, Client /Server protocol
  Liaison to other Standardisation bodies Contribution to other Standardisation Groups
Notes: Status der FE Standardisierung
Standard 1
Standard 2
Current Activities in Speech Reconstruction
Current Activities in Application and protocol group

## Slide 3: Aurora Participants
Participants
  Alcatel, Comverse, Ericsson, France Telecom, Hewlett Packard, Hutchinson, IBM, Microsoft, Mitsubishi, Motorola, Nokia, Nuance, Qualcomm, Siemens, Speech Works, Texas Instruments, Verbaltek, VoiceSignals, e. a.
Chairman of Aurora: David Pearce, Motorola
Notes: Wide Range of Participants
active
passive

## Slide 4
Aurora WI008 Front-End System Overview, Requirements
Application
Noise Reduction
Feature Extraction
Speaker Independent (SI)
Phoneme Reference
Word Model
Grammar
Trans-action
Front -End / Terminal
Back -End / Server
Transmission channel 3G, IP, ITU, etc.
Language independent, Low Delay, Medium Complexity, Datarate < 4.8 kbit /sec, support 8k,11k and 16k Sample Rate
Noise Robust, Match WI007 Performance for Clean Speech
High Performance (25% / 50% Reduction of WER to WI007)
WI008 Front-End
Notes: Review
What is DSR
Which Requirements were set ? 25 % Reduction for Well Matched Training / Test 50 % Reduction for Mismatched Training / Test

## Slide 5
Aurora WI008 Front-End Competition
First Submission with Performance Results on Small Vocabulary Databases in Jan 2001
  6 Candidates from Nokia, Ericsson, Qualcomm/OGI/ICSI, Motorola and Alcatel/France-Télécom
Final Submission with Performance Results on Small and Large Vocabulary Databases in Jan 02
  2 Candidates from Qualcomm/OGI/ICSI and Motorola/France-Télécom/Alcatel
Notes: History

## Slide 6
Aurora WI008 Front-End Selection
Small vocabulary databases (10 digits)
  Real world SDC Databases and synthetic TI-Digits Database with artificially added Noise
  Word-Based Recognizer, Pre-tuned but then fixed
Large vocabulary database (5000 Words)
  Wall Street Journal Database with artificially added Noise
  Phoneme-based Recognizer with language model
Totally 93 Test sets with Different Languages, Noise levels, Microphones, Noise types and different Mismatch between Training and Test
Selection Criteria: Absolute Recognition Performance
Notes: Hidden Competition
Back End was fixed
Selection Criteria
Broad Test set
Recognition Accuracy
Disqualification Criteria
Complexity

## Slide 7
Front-End Standard
Overall best Performance: Absolute Accuracy 84.82 % (weighted sum of all Test-Sets with Files ranging from 0 - 20dB SNR + Clean Data)
Best Performance in most of the Test-Sets
Operational Features: Complexity /Ram /Rom: ~ 12.55 wMops /3.8 /3.7kWords Terminal Latency: 63 msec Datarate: 4.8 kbit/sec 39 Features
Notes: Consistent Performance over all Test Sets

## Slide 8: Front-End Standard Signal Processing in the Terminal
Terminal Front-End
to channel
Feature Extraction
Feature Compression
Framing, Bit-Stream, Error Protection
input signal
Feature Extraction
Noise Reduction
Waveform Processing
Cepstrum Calculation
Blind Equalization
11 and 16 kHz Extension
input signal
to feat. comp.
Notes: <number>
<footer>
<header>
<date/time>
Feature Extraction – calculation of cepstral features
Feature Compression – data reduction by using vector quantization
Framing, Bit-Stream Formatting, Error Protection
Noise Reduction – input signal de-noising
Waveform Processing – additional waveform-based de-noising
Cepstral Calculation – calculation of cepstral features
Blind Equalization – on-line cepstral mean removal
11 and 16 kHz Extension – processing of 11 and 16 kHz signals
Combination with VAD is possible

## Slide 9: Front-End Standard Signal Processing in the Server
Decoding, Error Mitigation and Decompression
Bit-Stream Decoding, Error Mitigation
Feature
Decompression
Speech
Engine
with
Feature
Interface
from channel
Notes: <number>
<footer>
<header>
<date/time>
Feature Extraction – calculation of noise robust cepstral features from input signal
Feature Compression – compress cepstral features by using vector quantization
Framing, Bit-Stream Formatting, Error Protection – data processing for channel transmission
Noise Reduction – input signal de-noising
Waveform Processing – additional waveform-based de-noising
Cepstral Calculation – calculation of cepstral features
Blind Equalization – on-line cepstral mean removal
11 and 16 kHz Extension – processing of 11 and 16 kHz signals
VAD – voice activity detection for non-speech frame dropping

## Slide 10: Front-End Standard Overall Performance
Notes: <number>
<footer>
<header>
<date/time>
LVCSR results will increase furthermore ?
Optimisation
Number of Mixtures
Beam Threshhold
Explain Absolute Accuracy
Explain Relative Accuracy

## Slide 11: Front-End Standard Compression and Encoding /Decoding
Compression: Split VQ of pairwise grouped Cepstral Features with 6 /8 bit Resolution per Pair
Framing, Bit-Stream and Error Protection
  CRC Code generated for a Frame-Pair
Mulitframe format, synchronisation sequence, header field and error protection are as in ETSI ES 201 108 (WI007)
Frame packet stream includes VAD bit (Wi008 only)
Error Mitigation Scheme based on CRC and first derivative of feature set
Notes: <number>
<footer>
<header>
<date/time>
Simple Scheme
Easy to Implement
Small Complexity
Sufficient Error Protection

## Slide 12
Aurora WI0030 Overview, Goals
New work item (WI 030) “DSR front-end extension for tonal language recognition and Speech Reconstruction” since Jun 01
  Improved Recognition in Tonal-Languages
  Server-based Speech Reconstruction for Verification Purpose
Notes: Major Requirement from Application
- Verification for legal purpose
- Improve Recognition for Tonal Languages

## Slide 13
Aurora WI0030 Goals, Activities
Goals
  Update Rate 10msec, Minimum Set of additional Features
  Datarate < 1000 bits /sec
Definition of Requirements and Test-Set for “Intelligibility”
Definition of Requirements for “Tonal-Language Recognition evaluation”
Currently IBM & Motorola are mainly contributing
Notes: Work in Progress

## Slide 14
Aurora Applications and Protocols Goals , Activities
Goals
  Exploit and Reuse existing Protocols as far as possible
  Start with DSR Model first but keep it open for further Extensions (Multimodal I/O)
Activities
  Bring DSR into 3GPP
  Approve Extensions necessary for DSR within 3GPP, IETF , ...
  Define Transport and Session Protocol Requirements
  Define Meta information needed
  Define Extensions for Multimodal Operation

## Slide 15
Aurora Applications and Protocols Transport and Session Control
Meta Information VAD, DMTF, BargeIn and Speech Segments in DTX Mode Codec Negotitaion
Transport Protocol (work in progress) Use RTP, definition of RTP payload for DSR
Session Protocol (work in progress) Agreement to use SIP /SDP as it is adopted by 3GPP Extensions for Codec negotiations
Notes: Meta Information InBand
Codec negotiation per SDP

## Slide 16
Aurora Applications and Protocols Liaison to other Standardization bodies
3GPP
  DSR was launched into 3GPP in July 2001 (Goal: bring DSR into Release 5), now probably Release 6
  DSR has achieved state 1 (some questions to be solved)
    comparison between AMR based SR and DSR based SR
    other open issues: service examples, billing, ...
    New Subgroup in 3GPP: Speech Enabled Services
  Approve Extensions necessary for DSR within 3GPP, IETF ,
ITU - T SG16
  agreement to avoid duplication of work