## Slide 1: Interoperability & QoS Implications of ISO TC215 WG2.1
Todd Cooper
(t.cooper@ieee.org)
Chairman, IEEE 1073
Technical Director, MDCIG / IEEE-ISTO
President, Breakthrough Solutions

## Slide 2: Overview
ISO TC215 Interoperability & QoS
TC215 WG 2.1 X73 Standards
QoS for Point-of-Care Medical Device Communication

## Slide 3: ISO TC 215 Interoperability
Interoperability : ability of two or more systems
or components to exchange information and
to use the information that has been exchanged.
      source : IEEE Standard Computer Dictionary : A
      Compilation of IEEE Standard Computer
      Glossaries, IEEE, 1990
Functional interoperability
    Shared Architectures, Methods & Frameworks
Semantic interoperability
Shared data types, terminologies, codings

## Slide 4: ISO TC 215 Interoperability
WG 1: EHR architecture and modeling
WG 2: Messaging architecture & methods
WG 3: Terminology Methods
WG 4: Shared security architecture
WG 5: Shared health card framework

## Slide 5: ISO TC 215 Interoperability
For Quality of Service :
WG 1 - Health indicators conceptual framework
WG 2 - Quality indicators for health
information made available on the
Internet

## Slide 6: ISO TC215 Health Informatics
Focus is primarily on Level 7 Interoperability
Medical Device Communications covers all 7 layers.

## Slide 7: ISO TC215 Health Informatics

## Slide 8: ISO/IEEE/CEN X73 Process
Establish Work Plan for Standard
(incl. resolution of all issues between IEEE, ISO, and CEN)
Develop and Ballot Draft Using IEEE Process
Standard fails ISO DIS/FDIS ballot
Completed Published Standard
Ballot Approved IEEE Document
Using ISO Process (DIS/FDIS)
Draft passes IEEE ballot
Publish ISO/IEEE/CEN Standard
Draft passes ISO DIS/FDIS ballots

## Slide 9: ISO/IEEE 11073 Standards
 Provide real-time plug-n-play interoperability for patient-connected medical devices
X73 Charter:
…leveraging off-the-shelf technologies, scaling across a wide range of system complexities, and supporting commercially viable implementations.
 Facilitate the efficient exchange of vital signs and medical device data, acquired at the point-of-care, in all health care environments

## Slide 10: ISO/IEEE 11073 Standards
Primary focus is on…
 Point-of-Care (POC)…
 Medical Device…
 Communications
ISO/IEEE 11073 Health informatics –
Point-of-care medical device communications - …

## Slide 11: ISO/IEEE 11073 Standards
X73’s architecture ensures…
True interoperability across all 7-layers:
From the connector to the end application!
 QoS mechanisms designed to support the strong requirements placed on regulated medical devices
 Maintainability as communications technology and applications change

## Slide 12: ISO/IEEE 11073 Standards

## Slide 13: ISO/IEEE 11073 Standards
Medical Device Data Language (MDDL):
Semantics needed to communicate a device’s application status and control information.
Consists of three main components:
  Nomenclature (1073.1.1.1)
  Domain Information Model (DIM) (1073.1.2.1)
  Device Specializations (1073.1.3.x)

## Slide 14: ISO/IEEE 11073 Standards
Nomenclature:
A set of numeric codes that identify every
item that is communicated between systems.

## Slide 15: ISO/IEEE 11073 Standards
Domain Information Model:
An object oriented data model that specifies objects, attributes, attribute groups, event reports, and services that may be used to communicate device data and to control / configure the reporting of information.
Does not imply a specific implementation technology
Objects include Medical Device System, Virtual Medical Device, Numeric, Enumeration, Real-Time Sample Array, Battery, Scanners, Alert Monitor, …

## Slide 16: ISO/IEEE 11073 Standards
Domain Information Model Subject Areas

## Slide 17: ISO/IEEE 11073 Standards

## Slide 18: ISO/IEEE 11073 Standards
Generalized application profile standards …
A generic (non-device specific) set of data and services needed to initiate, configure, and maintain communication.
Connect ~ Disconnect, Create ~ Delete, Get ~ Set, Event Report, Invoke, etc.
Standard Services: ACSE, ROSE, CMISE, ASN.1, MDER (based on BER+), Etc.
Beginning work on XML & Web Services profile

## Slide 19: ISO/IEEE 11073 Standards
Domain Information Model
Abstract Syntax
(ASN.1)
Transfer Syntax
(MDER)
‘On-the-Wire’
Format

## Slide 20: ISO/IEEE 11073 Standards
Generalized application profile standards …
Profiles:
Specific set of capabilities tailored for a class of communication needs / architectures
Limits the options that are available
Remaining options must be discovered and in some cases negotiated when a connection is made (enabling plug-n-play interoperability!)

## Slide 21: ISO/IEEE 11073 Standards

## Slide 22: ISO/IEEE 11073 Standards
IrDA-Based Cable Connected (1073.3.2)
IrDA-Based Infrared Wireless (1073.3.3)
RF Wireless – high emphasis on QoS!
IP-Based (Ethernet)
Available (point-to-point) transport standards…
Transport standards (LANs) under consideration…
Key: Shared IT infrastructure with guaranteed QoS

## Slide 23: ISO/IEEE 11073 Standards
Examples: LAN Access Points,
Wired-to-Wireless Transport Gateways,

## Slide 24: ISO/IEEE 11073 Standards
Objective: Interoperability between different application-layer protocols
+
Bi-Directional Transparency
Example: HL7 / IEEE Gateway: IEEE 1073.6.1.1 … HL7 - Observation Reporting Interface!

## Slide 25: ISO/IEEE 11073 Standards
1073
Network
HL7
Network
1073
System
HL7/1073
Gateway
HL7
System
1073
System
HL7
System
HL7-IEEE JWG Project Scope:
Identification and definition of interfaces to support interoperability between HL7 and 11073 based systems for Point-Of-Care testing / monitoring use cases.

## Slide 26: ISO/IEEE 11073 Standards
X73 – Real-time plug-n-play interoperability across all 7-layers
From
Device-to-device up to
Device-to-EMR

## Slide 27: ISO/IEEE 11073 Standards
X73 includes QoS management support:
Negotiated Bandwidth at association
 Start-up configuration minimizes network usage to that which is needed for client applications.
 Management Information Bases (MIBs) provide dynamic visibility to communications performance
 State models and confirmed delivery provide a high level of reliability for medical data transfer

## Slide 28: ISO/IEEE 11073 Standards
Drivers of X73 QoS:
Regulated industry: “Safe & Effective”
 Clinical Use Cases for devices – esp. real-time requirements: User needs & expectations!
 Transport and service profile technologies (LAN based vs. point-to-point)
 System wide topologies (local vs. wide area)
 Non-clinical stakeholders (…finance)

## Slide 29: ISO/IEEE 11073 Standards
Key X73 QoS considerations:
Reliability – FMEA, error detection & mitigation
 Latency – from device detection to end annunciation for the data client
 Priority – Not all medical device data has the same communications priority
 Bandwidth – Allocation and dynamic management

## Slide 30: ISO/IEEE 11073 Standards
X73 Data Categorization:
Alerts (both physiological & technical)
 Real-time Waveforms
 Real-time Parameters (Breath-to-breath)
 Non-RT Parameters (battery level, metric label)
 Non-RT Event (low battery)
 Controls
 History / Archival
 Web Browsing

## Slide 31
Data Type | Bandwidth | Priority | Reliability | Latency
Alerts | Lo (64B/Al.), Intermittent | Highest | Hi | 3 sec
RT-Waves | Hi (120 to 4KB/s/chan) Predictable | High | Hi | <RT> or CS=3 sec
RT-Param’s | Lo-Med, Predictable | High | Hi | 3 sec
Non-RT Param’s | Lo (20B/p), Unpredict. | High | Hi | ---
Non-RT Events | Lo-Med, Unpredict. | Medium | Hi | PoC: 3 sec CS: 5 sec
Controls | Lo, Unpredict. | Medium | Hi | PoC: 3 sec CS: 5 sec
History / Archive | Hi, Bursty, Unpredict. | Low | Med->Hi | Push: >5 sec; Pull: < 5 sec
Web Browsing | Hi, Bursty, Unpredict. | Low | Med->Hi | 3-5 sec

## Slide 32: ISO/IEEE 11073 Standards
X73 QoS Issues:
Latency:
  Prioritization support
  Shared Bandwidth management architecture
  (across multiple manufactures / devices)
Reliability:
Prioritization policies – guaranteed B/W
Network fault detection & Annunciation
 Graceful system performance degradation
 Co-existence Management (esp. RF wireless)

## Slide 33: ISO/IEEE 11073 Standards
And what about…
Remote Control: a virtual plug-n-play remote control network!
Global access: Real-time vital signs viewing across the world (w/security, authentication, …)

## Slide 34: ISO/IEEE 11073 Standards
Conclusions…
X73 are the only comprehensive point-of-care medical device communication standards on the horizon!
 Need additional pilot projects to show capabilities of X73 protocols
 Health care providers and management organizations must demand medical device interoperability using X73
 We welcome support in adding security, web services, and rigorous LAN-based QoS support to our standards