## Slide 1: Explanation of ENUM (RFC 2916)
Patrik Fältström
Area Director, Applications Area, IETF

## Slide 2: Problem we want to solve
<number>
ENUM

## Slide 3: Problem statements
How do network elements (gateways, SIP servers etc) find services on the Internet if you only have a telephone (E.164) number?
How can subscribers define their preferences for incoming communications?

## Slide 4: Today, many addresses
tel:+46-8-971234
mailto:paf@example.com
tel:+46-706051234
sip:paf@example.com

## Slide 5: With ENUM, only one
tel:+46-8-971234
mailto:paf@example.com
tel:+46-706051234
sip:paf@example.com
tel:+46-706051234
Give this number to friends:
+46-8-971234
ENUM

## Slide 6: Technical solution
<number>
ENUM

## Slide 7: Solution in short
Put domain names derived from telephone numbers in the global domain name system, DNS
IETF ENUM Working Group created to solve the problem of using the DNS for:
  domain name in
  [Numbers re-formatted as domain names]
  URI out
  [mailto, sip, tel, http or other URI scheme]
Solution: NAPTR records
Use the URI’s for the communication

## Slide 8: ENUM in a nutshell
take phone number
+46-8-6859131
turn into domain name
1.3.1.9.5.8.6.8.6.4.e164.arpa.
return list of URI’s
sip:paf@cisco.com
ask the DNS
mailto:paf@cisco.com

## Slide 9: ENUM use in more detail
“Call setup”
Sip
sip:paf@cisco.com
Query
1.3.1.9.5.8.6.8.6.4.e164.arpa.?
Dial
+4686859131
DNS-Server
Sip server
Gateway
Response
sip:paf@cisco.com

## Slide 10: Example
DNS-Server
Internet
PSTN
Called party
Calling party
SIP-Server
SIP-Server
Gateway
Gateway

## Slide 11: VoIP via SIP to VoIP
DNS-Server
“ENUM”
SIP-Server
SIP-Server
Gateway
Gateway

## Slide 12: VoIP via PSTN to PSTN
DNS-Server
“ENUM”
SIP-Server
SIP-Server
Gateway
Gateway

## Slide 13: Step 1
Take an E.164 number and create a fully qualified domain name in a single highly defined and structured domain
+46-8-971234
+468971234
4.3.2.1.7.9.8.6.4.e164.arpa.
The input to the
NAPTR algorithm

## Slide 14: Step 1, Explanation
Each digit can become a definable and distributed “zone” in DNS terms
Delegation can (doesn’t have to) happen at every digit, including at last digit
Zones such as country codes, area codes or primary delegated blocks of numbers can be delegated as well as individual numbers
DNS defines authoritative name servers for NAPTR/service resource records

## Slide 15: Step 2
Lookup NAPTR RR’s in DNS, and apply NAPTR/ENUM algorithm
  4.3.2.1.7.9.8.6.4.e164.arpa.
  !^.*$!mailto:spam@paf.se!
  !^+46(.*)$!ldap://ldap.telco.se/cn=0\1!
Use rewrite rules using regular expressions which operate on the E.164 number (+468971234)

## Slide 16: Regular Expressions
For ENUM, the NAPTR regexp field may yield an (unchanged) URL
!<regexp>!<string>!
  “Match <regexp> on original E.164, and apply rewrite rule <string>”
^ - Match beginning
$ - Match end
. - Match any character
.* - Match any number of any character
() - Grouping, \n in <string> is replaced with group number ‘n’ in <regexp>

## Slide 17: Step 2 in detail
$ORIGIN 4.3.2.1.7.9.8.6.4.e164.arpa.
IN NAPTR 10 10 ”U” ”mailto+E2U” ”!^.*$!mailto:spam@paf.se!”
IN NAPTR 20 10 ”U” ”ldap+E2U” ”!^+46(.*)$!ldap://ldap.telco.se/cn=0\1”
Note that no line break should be in the records

## Slide 18: Status / Issues

## Slide 19: Status (done)
RFC 2916 published in September 2000
The domain e164.arpa delegated to RIPE NCC
  RIPE NCC appointed by the IAB according to RFC 2916
ITU SG2/WP1/2 liaison statement:
  Member state can inform ITU on entry of numbers in ENUM tree

## Slide 20: Status (done)
Instructions to RIPE NCC
  Any “request” not coming from TSB is to be forwarded to TSB
  If TSB says no, no delegation is to be done
  All evaluation of any “request” is to be done by TSB
  RIPE NCC is only creating and evaluating the technical data which they need for the actual delegation
  RIPE NCC is to communicate with TSB
  RIPE NCC is to make public any communication regarding a “request”

## Slide 21: Status (not done)
Delegation of domains below e164.arpa to managing entities that are appointed by member states
  A few “requests” have been passed to TSB, which have responded very quickly
National issues are not resolved
  We have not heard that issues related to verification of holder of E.164 number are resolved anywhere

## Slide 22: Issues

## Slide 23: Issue 1: Competition
The DNS requires a unique root
  More on this later
In DNS, we have a question on how to have competition in general, since one commercial company “had too large a market share”
Competition for registrations of DNS records is ensured using a registry/registrar model:
  One registry which runs the DNS server
    Competition at this level is handled when choosing the registry, because that can only be one organization
  Many registrars which the customer talk with
    Registrars decide for example price for a registration

## Slide 24: Issue 2.1: Unique root
Why is a unique root used in ENUM?
  Say I have phone number +468971234
  I can choose between a.com and b.com
  I choose b.com, and get the DNS domain
    4.3.2.1.7.9.8.6.4.b.com.
  Axel is to call me
  He knows my phone number, +468971234, only
  How is he to know that it is in b.com and not a.com I have my data?
General issues in RFC 2836
We need a “Golden Tree” for E.164 numbers

## Slide 25: Issue 2.2: Selection of root
Address and Routing Parameters Area
See contribution from ISOC
See http://www.iana.org/arpa-dom/
  in-addr.arpa
    IPv4-addresses
  ip6.arpa
    IPv6-addresses
  e164.arpa
    E.164 numbers

## Slide 26: Issue 3: Alternatives?
The implementation of a globally unique ENUM tree provides ample opportunity for competition at the national level
Having ENUM using domain e164.arpa means that one still have:
  Ability to have dialing plans in other domains
  Competition regarding registration according to registry/registrar model on all levels in DNS tree
  Competition when selecting the registries
  Competition regarding services

## Slide 27: 3.1 Alternative Dial plans
A user very seldom dial an E.164 number on his phone
    Inside Cisco, people dial 58509 to me
    Outside Cisco, from Sweden, people must dial 0014085258509
Not all dialed numbers are E.164 numbers
People use dialing plans
Dialing plan information can be resolved by the use of same technology as ENUM

## Slide 28: 3.2 Registry / Registrar
A registry runs the DNS server for a specific domain name
  one domain -> one registry
A customer contacts a registrar when he want to have things registered, not the registry
Registrar verify customer data, do billing, and send data to registry when delegation is to be done, changed or cancelled
  See next slide…

## Slide 29: 3.3 Selection of registry
Registries are needed which runs the DNS
  On a country code level
  Inside a country code, according to local policy
The model we use today with DNS is
Holder of a domain
Registry
Registrar
Registrar
Registrar
Registrant
Holder of a domain

## Slide 30: 3.4 Services
A customer in ENUM announces what services he subscribes to
  Examples:
    Email
    Web homepage
    SIP service (VoIP)
    Telephony
Each one of these services can be handled by separate contracts between customer and service provider
These contracts have nothing to do with the announcement via ENUM of their existence

## Slide 31: The big picture…
RIPE-NCC
IETF/IAB
Registry for country
Registrar for country
Registrar for country
Registrar for country
ENUM Service provider
ENUM Service provider
ENUM Service provider
Customer
Service provider
for telephony
Service provider
for email
Service provider
for email
Service provider
for email
Service provider
for telephony
Service provider
for telephony
ITU-T TSB

## Slide 32
Patrik Fältström
paf@cisco.com