## Slide 1: ASN.1 The solution for efficient communication between systems
Olivier DUBUISSON olivier.dubuisson@francetelecom.com
ITU-T ASN.1 Rapporteur http://asn1.elibel.tm.fr

## Slide 2: ASN.1: What is it?
Abstract Syntax Notation number One
International standard : ITU-T X.680 to X.683 | ISO/IEC 8824-1 to 4
Describes data exchanged between two communicating applications
Several associated standardized encodings, such as:
  efficient (binary) encoding: Packed Encoding Rules (PER)
  canonical encoding for digital signatures: Distinguished Encoding Rules (DER)
  XML encoding rules (XER)
Mature, long record of reliability and interoperability
ASN.1 is a critical part of our daily lives; it's everywhere, but it works so well it's invisible!
More information: http://asn1.elibel.tm.fr/introduction

## Slide 3: Example of an ASN.1 module
Module-order DEFINITIONS AUTOMATIC TAGS ::=
BEGIN
Order ::= SEQUENCE {
header Order-header,
items SEQUENCE OF Order-line }
Order-header ::= SEQUENCE {
reference NumericString (SIZE (12)),
date NumericString (SIZE (8)) -- MMDDYYYY --,
client Client,
payment Payment-method }
Client ::= SEQUENCE {
name PrintableString (SIZE (1..20)),
street PrintableString (SIZE (1..50)) OPTIONAL,
postcode NumericString (SIZE (5)),
town PrintableString (SIZE (1..30)),
country PrintableString (SIZE (1..20)) DEFAULT "France" }
Payment-method ::= CHOICE {
check NumericString (SIZE (15)),
credit-card Credit-card,
cash NULL }
Credit-card ::= SEQUENCE {
type Card-type,
number NumericString (SIZE (20)),
expiry-date NumericString (SIZE (6)) -- MMYYYY -- }
Card-type ::= ENUMERATED {cb(0), visa(1), eurocard(2), diners(3), american-express(4)}
-- etc
END

## Slide 4: ASN.1 and the telecom industry
Intelligent network
GSM
UMTS (3G cellphones)
Voice over IP
Interactive television
Videoconference
SET, C-SET (secured electronic transaction: e-commerce, m-commerce)
Computer-supported telecommunications applications
...

## Slide 5: ASN.1 in other domains
Intelligent transportation
Radio-frequency identification (RFID)
ATN (Aeronautical Telecommunication Network)
Embedded systems
Financial operations (ASC X.9, ISO TC 68)
Control of manufacturing systems
And a lot of other application domains: see http://asn1.elibel.tm.fr/uses
Fully integrated in the formal languages SDL and TTCN

## Slide 6: To find more information
ASN.1 website: http://asn1.elibel.tm.fr
        ASN.1 - Communication Between Heterogeneous Systems (Olivier Dubuisson, Morgan Kaufmann, 2001) download : http://asn1.elibel.tm.fr/book
        ASN.1 Complete (John Larmouth, Morgan Kaufmann, 2000) download : http://www.oss.com/asn1/larmouth.html

## Slide 7: ITU-T ASN.1 Project
Hosted by Study Group 7
Promote ASN.1 to all ITU-T study groups and also to other standardization organizations (ISO, ETSI, ECMA, W3C, IETF…)
Help users understand and write ASN.1 specifications
Provide tools and ensure quality of the specifications to be published
First actions:
  Free ASN.1 module database
  Object identifier (OID) repository: http://asn1.elibel.tm.fr/oid
Website: http://www.itu.int/ITU-T/asn1
Open FTP area for information exchange and associated open e-mail exploder,

## Slide 8: ASN.1 Consortium
Group of ASN.1 users (people and companies), specifiers and tool-vendors
Share resources and information
Promote ASN.1 (towards newspaper and journals, companies, universities…)
No standardization work
Three forums:
  Industry forum
  Standardization forum
  Academic forum
Website: http://www.asn1.org