## Slide 1
Security in cdma2000
Frank Quick QUALCOMM, Incorporated Chair, 3GPP2 TSG-S WG4 (Security)

## Slide 2
Overview
The 3GPP2 organization (www.3gpp2.org)
The cdma2000 family of standards
Wireless Security
Security Architectures in cdma2000

## Slide 3: 3GPP2 Membership
ARIB Association of Radio Industries and Business (Japan)
CWTS China Wireless Telecommunication Standard Group (China)
TIA Telecommunications Industry Association (NAFTA countries: USA, Canada, Mexico)
TTA Telecommunications Technology Association (Korea)
TTC Telecommunication Technology Committee (Japan)

## Slide 4: Membership, cont’d
Market Representation Partners
  CDMA Development Group
  MWIF
  IPv6
Observers
  TSACC
  ACIF
  ETSI

## Slide 5: Purpose of 3GPP2
The purpose of 3GPP2 is to prepare, approve and maintain globally applicable Technical Specifications and Technical Reports for a 3rd Generation Mobile System based on the evolving ANSI-41 Core Network and the cdma2000 radio access technologies.
These specifications include support for 3G Networks based on both Internet Protocol and evolved ANSI-41, including interoperability between these networks and mobile station.
3GPP2 also takes into account the emerging ITU recommendations on interworking between IMT-2000 family members.
Serving the CDMA Community via Smooth Evolution of cdma2000 from 2G to 3G while Expanding 2.5G Capabilities
Notes: Purpose of slide: Introduce the founding principals which lead to the creation of cdma2000.
The purpose of cdma2000 was to advance IS-95 based on the requirements defined under the IMT-2000 requirements of ITU. The basic requirements were to provide high speed data services for Indoor, Indoor to Outdoor/Pedestrian, and Vehicular environments.
Given IS-95 is a FDD based technologies, technical proposals were also introduced which defined TDD modes of operation as well. These were adopted by WG-IV of TR45.5 and included in the cdma2000 RTT proposal to ITU-R.
The cdma2000 RTT proposal, as defined, meets the IMT-2000 requirements while maintaining backward compatibility to what the industry terms “cdmaOne”, which is a complete family of standards.
Many existing services such as - speech coders, packet data, circuit data, fax, SMS, OTA, were identified as capabilities already available with the IS-95 family of standards and were included in the requirements for cdma2000 to be evolved and inclusive in the 3rd generation of cdma2000 capabilities.

## Slide 6: Process
3GPP2 publishes technical specifications as a cooperative effort of all partner members
  TSGs develop technical specifications
  TSGs’ outputs reviewed and approved by Steering Committee per 3GPP2 procedures
Partners apply national standardization processes to standardize results of work
  Ownership and copyright of these output documents is shared between the Organizational Partners.
Resulting in globally developed standards for use on a region by region basis

## Slide 7: 3GPP2 Organizational Structure

## Slide 8: History
Prior to 2001, 3GPP2 relied on the TIA’s Ad Hoc Authentication Group (AHAG) for security needs.
  AHAG was formed in 1991 to handle encryption-related work in accordance with US and Canadian law.
  Recent changes in export laws make international meetings on security much simpler.
TSG-S WG4 (Security) was formed in August 2001.
  WG4 will assume most of the work previously done by AHAG.
  AHAG continues as a TIA support group.

## Slide 9: CDMA Air Interface Standards (TIA)
J-STD-008
TSB74
IS-2000 (CDMA2000
Rev 0)
July 1999
IS-2000-A (CDMA2000
Rev A)
IS-856 (1xEV-DO)
October 2000
March 2000
IS-2000-C (CDMA2000
Rev C)
(Summer 2002)
IS-2000-B (CDMA2000
Rev B)
(Spring 2002)
IS-95-A
IS-95-B
May 1995
March 1999
Systems in Commercial Operation
Standard Completed
Standard Development in Progress
(expected date of completion)

## Slide 10: cdma2000 Overview
IS-2000/C.S0001-0005 through revision B (alias 1x, 3x):
  Unified operation on 1 or 3 1.25 MHz channels
  Improved voice and data performance
IS-856/C.S0024 (alias HDR, HRPD, 1xEV-DO)
  Up to 2.4 Mb/s burst data rate on a 1.25 MHz channel
  Direct Internet access
Future:
  IS-2000-C and later: improved data and voice (EV-DV)
  Enhanced HDR

## Slide 11: IS-2000/C.S0001-0005 (1x-3x)
Direct sequence spreading:
  1.25 MHz bandwidth per physical channel, 1 or 3 channels.
Forward Link
  Orthogonal modulation using 64 or 128 Walsh codes (depending on rate set in use).
Reverse Link
  Pilot-aided coherent modulation, spreading sequence offset channelization.
General voice and data services
  up to 307 kb/s (1x), 1.04 Mb/s (3x) per supplemental data channel
Network
  PSTN and Internet service connections
  ANS-41 MAP for mobility management and security

## Slide 12: 1x-3x Network
Home System
Visited System
Home
Location
Register
Authentication
Center
PSTN Switch
+
VLR
Security Parameters
Key Management
Subscription profiles
Authorization control
Location registration
Local authentication
Mobility management
Radio Access
Network
SS7
(voice and other circuit-switched services)

## Slide 13: Future All-IP Network
Not just a replacement for SS7.
Internet-based network signaling, likely including:
  Mobile IP for location registration and data delivery.
  Presence servers may replace HLRs.
  SIP for call/session establishment.
  Internet security protocols.
New security challenges:
  The network is directly exposed to Internet attacks.
  Weak security in one operator’s system may jeopardize the entire system.
TSG-S WG4 is establishing security requirements for the all-IP Network.

## Slide 14: IS-856/C.S0024 (1xEV-DO)
IS-2000 Compatible RF parameters and components.
  Network planning.
  Dual-mode 1x/1xEV-DO terminals supported.
High-performance data service.
  CDMA/TDMA hybrid with demand assignment.
  Up to 2.4576 Mb/s FL burst rate, 153.6 kb/s RL.
Network: direct Internet access
  Mobile IP for mobility with fixed IP address.
  “simple IP” for mobility with locally assigned IP address.
  AAA/Radius security model.

## Slide 15: 1xEV-DO Network
Home System
Visited System
MIP
Home Agent
AAA-H
PDSN +
MIP
Foreign Agent
Subscription data
Authorization
Security Parameters
Key Management
Location registration
PDSN access control
Mobility management
Radio Access
Network
Internet
RAN-AAA
RAN access control
AT
PDA, laptop, etc.

## Slide 16: Security Elements
Access Control (bilateral)
Key management
Data and identity privacy
Provisioning

## Slide 17: Access Control
Protection of System Resources against Unauthorized Use.
Authentication
  Terminal authentication
    Prevent fraudulent use of the network
      Proof of subscription identity
      Proof of sender identity and message integrity
  Network authentication
    Prevent false base station attacks on user information
Authorization
  Authentication is a pre-requisite for Authorization.
  Service Access Rights based on Subscription data are passed from home system (HLR or AAA) to serving system

## Slide 18: Key Management
IS-2000/C.S0001-0005:
  Relies on symmetric keys for all security.
  A root authentication key forms the base security association.
  Session keys are derived from the root key during authentication.
IS-856/C.S0024:
  Uses public-key agreement to establish airlink session keys.
  Uses symmetric keys for Radius authentication.

## Slide 19: Authentication Methods
Message authentication
  A method where each message includes identification and proof of identity.
  This method is required on random-access channels.
  Requires a long-term security association
Connection authentication
  A method where identity is proven once, and all subsequent data includes proof that it comes from the same source.
  Useful where a connection is established, including a session-related security association.

## Slide 20: IS-2000 Authentication
Challenge-Response Authentication
  Rev B and earlier:
    Legacy authentication based on IS-95.
  Rev C and later:
    AKA (same as UMTS authentication), plus:
    Optional UIM authentication procedure to prove presence of a valid UIM, preventing rogue shell attacks.
Message Integrity Checks
  Keyed SHA-1-based hash of message contents.
  Cryptosync based on time and other data to prevent replay attacks.

## Slide 21: IS-2000-C Authentication (AKA)
mobile
visited system
home system
Registration request
Authentication vector request
AV(challenge, response, BS
Challenge, BS authentication
Response
Registration request
authentication, CK, IK, UAK)
Compute response, CK,
IK, UAK using root key K
Compute response,
CK, IK, UAK
using root key K
Access request
(MAC using IK or UAK)
Registration response
Registration response

## Slide 22: IS-856 Authentication
RAN:
  Initial connection establishment is neither authenticated nor encrypted.
  Session establishment includes Diffie-Hellman key negotiation.
  Subsequent RAN-domain messages can be authenticated and/or encrypted using the negotiated keys.
  PPP/LCP setup follows session establishment.
  RAN user identity is optionally authenticated by CHAP via the RAN-AAA.
  Data integrity protection (encryption, keyed MAC) prevents packet insertion or similar theft of service.
PDSN:
  Separate PPP/LCP instance created.
  CHAP and/or MIP authentication of PDSN user identity via the home AAA server.
  RAN security ensures integrity of the PPP connection.

## Slide 23: IS-856 Authentication
mobile
visited system
(RAN/PDSN)
home RAN (via PDSN)
RAN session establishment
(Diffie-Hellman key agreement)
(optional) CHAP authentication
PDSN session establishment
CHAP or MIP authentication
Access request
(MAC using D-H key)
home ISP (via PDSN)

## Slide 24: IS-2000 Privacy
Identity privacy:
  Temporary mobile station identifier (TMSI) is assigned by the serving system.
User data privacy:
  IS-2000-B and later use 128-bit Rijndael algorithm (AES).
    Stream cipher mode
    Cryptosync based on time and other data to prevent replay attacks.
  IS-2000 encryption keys:
    64-bit keys from legacy authentication.
    128-bit keys from AKA.

## Slide 25: IS-856 Privacy
Identity privacy:
  When encryption is available, user identities are sent only after encryption is invoked.
User data privacy:
  Over-the-air encryption
    Protects against packet insertion, session hijacking, and data eavesdropping within the wireless system.
    Does not address the greater Internet privacy risks once the data leaves the wireless network.
  Internet security protocols (IPsec, SSL, etc.) are necessary for end-to-end security.

## Slide 26: Provisioning
Installation of subscription data in the mobile and network.
  Symmetric key security requires at least one key provisioned.
Provisioning is a major operational concern.
  High cost
  High impact on customer satisfaction
  Operator solutions will vary depending on business models.

## Slide 27: Provisioning Methods
Manufacturer provisioning
  Keys are installed by the manufacturer, and securely communicated to the operator’s AC or AAA.
Manual provisioning
  User or service representative enters the key via a keypad or provisioning device.
Over-the-air Service Provisioning (OTASP)
  Unprovisioned devices are hotlined to special service numbers/URLs; secure protocols are used to install keys.
Removable UIM
  Like GSM SIM; keys are in a removable “token” provided separately from the terminal and installed by the user.
(In approximate order of prevalence in cdma2000 deployments)

## Slide 28: In Conclusion:
Cdma2000 standards support a full set of security features for:
  Fraud prevention
  User privacy
Future evolution to all-IP networks poses new security challenges.
Actual system security is only as good as the operators make it.