| ITU - Telecommunications Standardization Sector STUDY GROUP 16 Video Coding Experts Group (Question 15) _________________ Sixth Meeting: Seoul, South Korea, 2-6 November, 1998 | Document Q15-F-29 Filename: q15f29.doc Generated: 29 Oct 1998 |
| --- | --- |

| Question: | Q.15/SG16 |
| --- | --- |
| Source: | Max Luttrell, Adam H. Li, Matthew Fong, John D. Villasenor Department of Electrical Engineering University of California Los Angeles, CA 90095, USA J.H. Park Samsung Electronics Company South Korea | Tel: Fax: Email: | 1 310 825-0228 1 310 825-7928 villa@icsl.ucla.edu |
| Title: | Simulation Results for Modified Error Resilient Syntax with Data Partitioning and RVLC |
| Purpose: | Proposal |

_____________________________

# Abstract

We expand the data-partitioning based error-resilient video coding techniques presented in documents Q15-C-36 and Q15-E-19 and present simulation results performed in accordance with the common conditions outlined in document Q15-E-50.  Depending on the sequence and error pattern, data partitioning generally offers a PSNR improvement of several dB.  The data partitioning scheme also does not drop frames, which improves over the anchor’s dropping of approximately 10-20 frames out of 900.

# Proposed Structures

We propose a data partitioning based scheme, first described in document Q15-C-36, in which we split the bitstream into packets.  The packet consists of a resynchronization marker, and is followed by some header information.  After this, the packet is filled with motion vector (MV) and DCT information until a packet-length threshold has been exceeded, at which point the packet is terminated.  Figure 1 depicts the proposed packet structure.

## Figure 1: Packet structure of proposed data partitioning syntax

In order to implement the proposal, we have used two schemes. The first scheme, denoted “variable MB”, is similar to the slice structure mode of H.263+.  After the Resynchronization Marker (RM) and packet header information, the RVLC-coded motion vector (MV) and VLC-coded DCT coefficients (DCT) are filled in for as many macoblocks as possible given the remaining packet length.  This results in a pseudo-fixed-length packet in which we have a variable number of macroblocks.

The second scheme, denoted “variable GOB”, in which MV and DCT information for a variable amount of GOBs is placed in the packet given the packet length.  This scheme is similar to the GOB synch mode in H.263+.  In this case, we again have a pseudo-fixed-length packet, but with a variable number of GOBs.  Figure 2 outlines the proposed schemes.

| variable MB |  |
| --- | --- |
| variable GOB |  |

### Figure 2: Proposed Schemes

# Decoding Method

In this section we describe the method used to decode the video bitstream including all employed error concealment techniques.  The decoding method is the same for both schemes described in section 2, the only difference being the number of macroblocks encoded in the MV and DCT regions.  It is helpful to refer to Figure 1 when reading this section.  Decoding is the same regardless of whether the mux is used.  Since our method allows for decoding information even in the presence of errors, we are not using the error indication supplied by the mux in these simulations and decode packets known to have failed the CRC check.

- Scan the bitstream for a PSC.  When we receive a PSC, we assume we have a picture header immediately following it.

- Decode the picture header (PH).  This is the same as in the reference TMN H.263+ decoder.  As in TMN, if we detect an error in the PH, we use the information from the last known error-free picture header. Note: since we use the Resynchronization Marker (RM), we have the advantage of not having to discard GOB 0 as in TMN.

- Scan for the next RM.  The next RM should immediately follow the PH.  If not, we assume an error, and discard the rest of this packet.

Repeat the following until next PSC detected:

- Immediately following the RM is the packet sequence number (PN).  Two cases:

- If we have just received a PSC and PH, we know PN should be 1. If it is not 1, we correct it to 1 and continue decoding of the packet.

- If we have not just received a PSC and PH, PN should be the previous packet’s PN+1.  There are two cases:

- no error in previous packet: set to  PN+1

- error in previous packet: use the value read

- Immediately following PN is MB index.  Two cases:

- If we have just received a PSC and PH, we know first MB index should be 0.  If it is not 0, we correct it to 0 and continue decoding of the packet.

- If we have not just received a PSC and PH, we know what first MB index should be based on the previous packet.  There are two cases:

- no error in previous packet: set to value predicted from previous packet

- error in previous packet: set to value read

- Scan for next Header Marker (HM).  This yields the length of the RVLC-coded header.  If it exceeds the length of the maximum RVLC codeword, this is an error and the packet is discarded.

- Decode the HM. Decoding is only performed in the forward direction. If an error detected, the whole packet is discarded until next RM.

- Scan for Motion Marker (MM).  If we find an RM first, error is detected and the packet is discarded.

- Decode the Motion Vectors (MV).  This is done in the forward and backward direction.  We retain all motion vectors decoded without error in both the forward and backward direction.  In the “one GOB” scheme described above, the length is too short for backward decoding and is thus not performed.

- Scan for next RM.

- Decode the DCT coefficients.  As it is VLC coded, not RVLC, we only decode in the forward direction.  If an error is detected anywhere, the entire DCT coefficients are set to 0, the intuitive meaning of which is that the error residual information is lost.

# Simulation Method

The simulations were performed in accordance with the test conditions agreed upon in document Q15-E-50 with one exception.  In simulations in which the mux was used, we were not using the error indication supplied by the mux, and therefore did not need the 16 bit CRC supplied by AL3.  We instead used AL1 which does not supply a CRC.  We present results for both the AL1 case and the AL3 case.

We have run simulations for the foreman, hall, container, news, silent, and glasgow sequences at channel bitrates of 32kbps and 64kbps for the DECT and wideband CDMA error patterns respectively.  For the DECT error patterns, the first 80 bytes were moved to the end of the error pattern according to discussions on the email reflector.  For the 32kbps and 64kbps simulations, we use a pseudo-fixed length threshold of 350 and 700 bits respectively.  We report results for both sending the data through a mux, and for applying the errors directly to the video bitstream.  For the mux case, we used the mux software contributed by Gary Sullivan (Q15-F-16) with a modified AUDIO_PACKET_SIZE of 23.  For applying the errors directly to the video bitstream, 75% of the channel bitrate was used for video transmission.

We calculated the PSNR of the reconstructed frames by the method agreed upon in the document Q15-E-50.  Accordingly, the PSNR is calculated between each frame of the source sequence at the full frame rate and the corresponding reconstructed frame.  Figure 3 illustrates an example of the calculation method in which the coder coded every second frame, and the 4th frame was dropped due to error.

| frame number | 0 | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| was it coded? | X |  | X |  | X |  | X |
| was it decoded correctly? | X |  | X |  |  |  | X |
| (PSNR calculated based on frame # | 0 | 0 | 2 | 2 | 2 | 2 | 6 |

Figure 3: Example of PSNR Calculation

We report results for both proposed schemes as well as for the anchor models.  For both sets of results, the same error concealment techniques were used.

# Conclusions

The proposed method shows significant performance gains over the anchor model, which varies with sequence and error pattern, and drops many fewer frames for all sequences/error patterns.  It shows the most improvement in cases with bad channel error conditions, which is the intended application of this error resilient mode of operation.  It also offers good performance in cases where no multiplexer Error Indication information is available, which is useful for some application environments.  We feel the method shows significant performance gains.

# Results

# Table 1: 64kbps/32kbps error-free channel

| 64kbps error free channel |
| --- |
|  | Anchor Model ( MB refresh ) | H.263+ ( Frame refresh ) |
| sequence | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | Total Video Bytes | Payload and Overhead Bytes for Video | Total Video Packets | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | Total Video Bytes | Payload and Overhead Bytes for Video | Total Video Packets |
| foreman | 25.96 | 36.45 | 36.87 | 721201 | 777929 | 8104 | 25.97 | 36.47 | 36.85 | 725207 | 781963 | 8108 |
| hall | 31.54 | 36.53 | 41.41 | 541376 | 598188 | 8116 | 32.29 | 40.78 | 42.93 | 548598 | 605515 | 8134 |
| container | 32.37 | 40.17 | 39.94 | 540726 | 597482 | 8108 | 34.23 | 40.58 | 39.99 | 544285 | 601125 | 8120 |
| news | 29.18 | 37.53 | 38.7 | 541418 | 598125 | 8101 | 30.58 | 37.53 | 38.61 | 548620 | 605467 | 8121 |
| silent | 30.63 | 37.14 | 38.92 | 360995 | 417695 | 8100 | 30.93 | 37.13 | 38.49 | 366195 | 422916 | 8103 |
| glasgow | 24.63 | 35.33 | 37.55 | 418742 | 475533 | 8113 | 24.67 | 35.36 | 37.61 | 428770 | 485736 | 8138 |

| 64 kbps error free channel |
| --- |
|  | Data Partitioning ( variable GOB ) | Data Partitioning ( variable MB ) |
| sequence | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | Total Video Bytes | Payload and Overhead Bytes for Video | Total Video Packets | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | Total Video Bytes | Payload and Overhead Bytes for Video | Total Video Packets |
| foreman | 25.93 | 36.42 | 36.83 | 729754 | 771775 | 6003 | 25.81 | 36.38 | 36.77 | 731296 | 779890 | 6942 |
| hall | 32.27 | 40.77 | 42.97 | 552334 | 588671 | 5191 | 31.95 | 40.73 | 42.93 | 552669 | 591771 | 5586 |
| container | 34.22 | 40.59 | 39.96 | 547624 | 579649 | 4575 | 33.40 | 40.6 | 39.98 | 551347 | 589644 | 5471 |
| news | 30.55 | 37.53 | 38.57 | 552467 | 588636 | 5167 | 30.42 | 37.47 | 38.54 | 552750 | 591719 | 5567 |
| silent | 30.98 | 37.15 | 38.53 | 370456 | 399443 | 4141 | 30.92 | 37.11 | 38.49 | 371514 | 402811 | 4471 |
| glasgow | 24.70 | 35.39 | 37.59 | 438572 | 470247 | 4525 | 24.65 | 35.38 | 37.55 | 441266 | 476077 | 4973 |

| 32 kbps error free channel |
| --- |
|  | Anchor Model ( MB refresh ) | H.263+ ( Frame refresh ) |
| sequence | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | Total Video Bytes | Payload and Overhead Bytes for Video | Total Video Packets | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | Total Video Bytes | Payload and Overhead Bytes for Video | Total Video Packets |
| hall | 28.90 | 34.89 | 39.53 | 271650 | 328378 | 8104 | 29.34 | 39.07 | 41.46 | 281246 | 338184 | 8134 |
| silent | 26.42 | 34.93 | 37.18 | 183752 | 240452 | 8100 | 28.49 | 35.72 | 37.28 | 190953 | 247674 | 8103 |
| news | 27.06 | 35.68 | 36.91 | 271697 | 328404 | 8101 | 27.96 | 35.84 | 36.94 | 281596 | 338443 | 8121 |
| container | 30.01 | 38.71 | 37.94 | 273743 | 330457 | 8102 | 30.91 | 38.80 | 37.90 | 280869 | 337709 | 8120 |

| 32 kbps error free channel |
| --- |
|  | Data Partitioning ( variable GOB ) | Data Partitioning ( variable MB ) |
| sequence | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | Total Video Bytes | Payload and Overhead Bytes for Video | Total Video Packets | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | Total Video Bytes | Payload and Overhead Bytes for Video | Total Video Packets |
| hall | 29.37 | 39.10 | 41.50 | 286028 | 319733 | 4815 | 29.17 | 39.04 | 41.51 | 286381 | 322137 | 5108 |
| silent | 28.65 | 35.79 | 37.36 | 196996 | 223792 | 3828 | 28.63 | 35.77 | 37.33 | 197635 | 224256 | 3803 |
| news | 28.03 | 35.86 | 36.99 | 287583 | 321113 | 4790 | 27.95 | 35.83 | 37.00 | 289352 | 324261 | 4987 |
| container | 30.79 | 38.85 | 37.94 | 284819 | 316970 | 4593 | 30.56 | 38.83 | 37.91 | 286294 | 319187 | 4699 |

# Table 2: WCDMA error pattern, sent through mux, 64kbps channel

|  | Anchor( MB refresh ) | H.263 +( Frame refresh ) | Difference |
| --- | --- | --- | --- |
|  | WCDMA-1 |  |
| sequence | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) |
| foreman | 900 | 0 | 19.17 | 33.28 | 33.08 | 903 | 0 | 19.26 | 33.12 | 33.11 | 0.09 |
| hall | 888 | 12 | 20.30 | 21.68 | 27.31 | 887 | 13 | 24.32 | 35.96 | 39.09 | 4.02 |
| container | 900 | 0 | 22.33 | 35.95 | 35.51 | 900 | 0 | 22.41 | 36.28 | 34.92 | 0.08 |
| news | 900 | 0 | 22.13 | 25.41 | 31.84 | 900 | 0 | 23.02 | 30.76 | 34.53 | 0.89 |
| silent | 900 | 0 | 24.62 | 35.79 | 37.85 | 900 | 0 | 26.22 | 36.05 | 37.62 | 1.6 |
| glasgow | 897 | 3 | 19.94 | 31.94 | 35.7 | 891 | 9 | 19.56 | 31.18 | 34.82 | -0.38 |
|  | WCDMA-2 |  |
| foreman | 900 | 0 | 20.34 | 34.12 | 34.47 | 900 | 0 | 20.63 | 34.22 | 33.70 | 0.29 |
| hall | 900 | 0 | 26.63 | 36.08 | 41.14 | 900 | 0 | 26.46 | 39.2 | 41.86 | -0.17 |
| container | 901 | 0 | 25.71 | 38.12 | 36.88 | 900 | 0 | 24.64 | 37.98 | 36.49 | -1.07 |
| news | 900 | 0 | 23.72 | 32.01 | 35.24 | 874 | 26 | 23.81 | 32.33 | 35.52 | 0.09 |
| silent | 900 | 0 | 27.74 | 36.59 | 38.39 | 900 | 0 | 27.42 | 35.69 | 36.77 | -0.32 |
| glasgow | 900 | 0 | 20.79 | 33.04 | 36.01 | 900 | 0 | 20.85 | 32.86 | 36.40 | 0.06 |
|  | WCDMA-3 |  |
| foreman | 899 | 1 | 19.76 | 32.64 | 32.57 | 898 | 2 | 20.92 | 34.22 | 34.13 | 1.16 |
| hall | 901 | 0 | 21.46 | 22.45 | 27.91 | 900 | 0 | 24.45 | 33.49 | 37.01 | 2.99 |
| container | 894 | 6 | 24.22 | 37.72 | 37.19 | 892 | 8 | 20.80 | 34.73 | 34.11 | -3.42 |
| news | 900 | 0 | 22.27 | 18.99 | 19.29 | 900 | 0 | 22.71 | 27.07 | 28.94 | 0.44 |
| silent | 900 | 0 | 25.53 | 36.07 | 38.04 | 899 | 1 | 27.39 | 36.24 | 37.67 | 1.86 |
| glasgow | 900 | 0 | 21.27 | 33.5 | 36.49 | 900 | 0 | 20.50 | 32.69 | 35.76 | -0.77 |
|  | WCDMA-4 |  |
| foreman | 900 | 0 | 24.50 | 36.03 | 36.36 | 900 | 0 | 24.85 | 36.07 | 36.54 | 0.35 |
| hall | 900 | 0 | 30.35 | 36.42 | 41.36 | 900 | 0 | 30.80 | 40.65 | 42.84 | 0.45 |
| container | 900 | 0 | 28.78 | 38.42 | 37.81 | 900 | 0 | 32.70 | 40.34 | 39.63 | 3.92 |
| news | 900 | 0 | 28.47 | 36.48 | 38.14 | 900 | 0 | 29.37 | 36.61 | 38.28 | 0.9 |
| silent | 900 | 0 | 30.22 | 37.09 | 38.89 | 900 | 0 | 30.31 | 37.04 | 38.39 | 0.09 |
| glasgow | 896 | 4 | 23.79 | 34.85 | 37.29 | 896 | 4 | 23.95 | 34.77 | 37.44 | 0.16 |
|  | WCDMA-5 |  |
| foreman | 900 | 0 | 24.59 | 36.09 | 36.39 | 900 | 0 | 24.49 | 36.09 | 36.39 | -0.1 |
| hall | 900 | 0 | 30.29 | 36.37 | 41.33 | 900 | 0 | 30.70 | 40.59 | 42.73 | 0.41 |
| container | 900 | 0 | 29.85 | 39.65 | 39.27 | 900 | 0 | 29.91 | 38.87 | 38.3 | 0.06 |
| news | 900 | 0 | 27.87 | 35.40 | 37.64 | 879 | 21 | 28.30 | 36.28 | 37.8 | 0.43 |
| silent | 900 | 0 | 30.16 | 37.09 | 38.83 | 900 | 0 | 30.12 | 36.82 | 38.09 | -0.04 |
| glasgow | 900 | 0 | 23.42 | 34.60 | 37.10 | 900 | 0 | 23.99 | 34.91 | 37.35 | 0.57 |
|  | WCDMA-6 |  |
| foreman | 900 | 0 | 24.38 | 35.50 | 35.85 | 900 | 0 | 24.73 | 36.26 | 36.66 | 0.35 |
| hall | 900 | 0 | 30.15 | 36.42 | 41.35 | 900 | 0 | 30.43 | 40.4 | 42.62 | 0.28 |
| container | 900 | 0 | 30.04 | 39.84 | 39.25 | 900 | 0 | 31.58 | 39.85 | 39.07 | 1.54 |
| news | 900 | 0 | 28.03 | 36.84 | 38.43 | 900 | 0 | 28.41 | 36.55 | 38.03 | 0.38 |
| silent | 900 | 0 | 30.19 | 36.99 | 38.81 | 900 | 0 | 30.24 | 37.01 | 38.38 | 0.05 |
| glasgow | 900 | 0 | 24.14 | 35.02 | 37.33 | 900 | 0 | 23.81 | 34.96 | 37.4 | -0.33 |

| Transmitted over AL-1 Mux |
| --- |
|  | Data Partitioning ( Variable GOB ) | Difference | Data Partitioning ( variable MB ) | Difference |
|  | WCDMA-1 |  |
| sequence | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) |
| foreman | 901 | 0 | 22.07 | 34.16 | 34.30 | 2.90 | 901 | 0 | 20.74 | 33.53 | 33.66 | 1.57 |
| hall | 900 | 0 | 25.91 | 38.93 | 41.76 | 5.61 | 901 | 0 | 26.24 | 37.93 | 39.71 | 5.94 |
| container | 903 | 0 | 27.05 | 37.84 | 37.32 | 4.72 | 903 | 0 | 27.99 | 38.98 | 37.92 | 5.66 |
| news | 901 | 0 | 24.38 | 30.76 | 35.10 | 2.25 | 902 | 0 | 25.79 | 33.2 | 36.07 | 3.66 |
| silent | 901 | 0 | 27.74 | 36.22 | 37.65 | 3.12 | 905 | 0 | 27.66 | 36.02 | 37.55 | 3.04 |
| glasgow | 900 | 0 | 21.08 | 32.59 | 35.73 | 1.14 | 901 | 0 | 20.53 | 32.20 | 35.54 | 0.59 |
|  | WCDMA-2 |  |
| foreman | 900 | 0 | 23.31 | 34.29 | 35.14 | 2.97 | 901 | 0 | 21.44 | 35.01 | 35.23 | 1.10 |
| hall | 900 | 0 | 27.07 | 38.66 | 42.14 | 0.44 | 900 | 0 | 27.78 | 39.55 | 41.99 | 1.15 |
| container | 901 | 0 | 29.47 | 39.45 | 38.42 | 3.76 | 900 | 0 | 30.00 | 39.79 | 39.01 | 4.29 |
| news | 900 | 0 | 26.63 | 33.39 | 36.27 | 2.91 | 901 | 0 | 26.43 | 30.76 | 32.63 | 2.71 |
| silent | 900 | 0 | 28.5 | 36.48 | 37.79 | 0.76 | 900 | 0 | 28.27 | 36.26 | 37.37 | 0.53 |
| glasgow | 901 | 0 | 21.74 | 32.75 | 35.97 | 0.95 | 901 | 0 | 21.54 | 33.25 | 36.16 | 0.75 |
|  | WCDMA-3 |  |
| foreman | 900 | 0 | 22.39 | 35.1 | 35.22 | 2.63 | 900 | 0 | 20.93 | 34.31 | 34.49 | 1.17 |
| hall | 900 | 0 | 26.09 | 38.16 | 41.69 | 4.63 | 903 | 0 | 27.00 | 39.28 | 42.09 | 5.54 |
| container | 900 | 0 | 24.15 | 35.14 | 37.78 | -0.07 | 902 | 0 | 26.48 | 38.74 | 38.42 | 2.26 |
| news | 900 | 0 | 24.51 | 32.11 | 35.29 | 2.24 | 903 | 0 | 26.20 | 31.31 | 35.14 | 3.93 |
| silent | 900 | 0 | 28.25 | 36.32 | 37.9 | 2.72 | 901 | 0 | 28.45 | 36.55 | 37.99 | 2.92 |
| glasgow | 900 | 0 | 21.83 | 33.62 | 36.7 | 0.56 | 902 | 0 | 21.87 | 33.49 | 36.56 | 0.60 |
|  | WCDMA-4 |  |
| foreman | 901 | 0 | 25.55 | 36.32 | 36.7 | 1.05 | 900 | 0 | 25.26 | 36.21 | 36.51 | 0.76 |
| hall | 900 | 0 | 31.13 | 40.58 | 42.8 | 0.78 | 900 | 0 | 31.05 | 40.55 | 42.87 | 0.70 |
| container | 900 | 0 | 32.70 | 40.33 | 39.65 | 3.92 | 900 | 0 | 32.69 | 40.48 | 39.8 | 3.91 |
| news | 901 | 0 | 29.61 | 37.18 | 38.42 | 1.14 | 900 | 0 | 29.72 | 36.95 | 38.3 | 1.25 |
| silent | 900 | 0 | 30.67 | 37.02 | 38.39 | 0.45 | 901 | 0 | 30.55 | 37.04 | 38.36 | 0.33 |
| glasgow | 900 | 0 | 24.02 | 35.07 | 37.33 | 0.23 | 900 | 0 | 24.05 | 35.01 | 37.43 | 0.26 |
|  | WCDMA-5 |  |
| foreman | 900 | 0 | 25.15 | 36.08 | 36.36 | 0.56 | 900 | 0 | 25.40 | 36.13 | 36.59 | 0.81 |
| hall | 900 | 0 | 31.24 | 40.5 | 42.81 | 0.95 | 900 | 0 | 30.94 | 40.40 | 42.81 | 0.65 |
| container | 900 | 0 | 33.25 | 40.45 | 39.77 | 3.40 | 900 | 0 | 32.87 | 40.50 | 39.88 | 3.02 |
| news | 900 | 0 | 30.03 | 36.99 | 38.3 | 2.16 | 900 | 0 | 29.48 | 36.21 | 37.82 | 1.61 |
| silent | 900 | 0 | 30.49 | 37 | 38.37 | 0.33 | 900 | 0 | 30.53 | 37.03 | 38.39 | 0.37 |
| glasgow | 900 | 0 | 23.51 | 34.55 | 36.98 | 0.09 | 900 | 0 | 24.15 | 35.09 | 37.38 | 0.73 |
|  | WCDMA-6 |  |
| foreman | 900 | 0 | 24.79 | 36.05 | 36.41 | 0.41 | 900 | 0 | 24.59 | 36.18 | 36.32 | 0.21 |
| hall | 900 | 0 | 30.62 | 40.44 | 42.83 | 0.47 | 900 | 0 | 31.17 | 40.61 | 42.8 | 1.02 |
| container | 900 | 0 | 33.58 | 40.47 | 39.83 | 3.54 | 900 | 0 | 32.84 | 40.47 | 39.85 | 2.80 |
| news | 900 | 0 | 30.17 | 37.28 | 38.46 | 2.14 | 900 | 0 | 29.39 | 35.57 | 37.73 | 1.36 |
| silent | 900 | 0 | 30.61 | 37.01 | 38.4 | 0.42 | 900 | 0 | 30.06 | 37.03 | 38.38 | -0.13 |
| glasgow | 900 | 0 | 24.43 | 35.23 | 37.51 | 0.29 | 900 | 0 | 24.1 | 34.88 | 36.96 | -0.04 |

|  | Data Partitioning using AL3 mux | Difference |
| --- | --- | --- |
|  | WCDMA-1 |  |
| Sequence | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) |
| foreman | 900 | 0 | 18.3 | 32.27 | 31.94 | -0.87 |
| hall | 900 | 0 | 23.68 | 37.68 | 41.35 | 3.38 |
| container | 900 | 0 | 25.77 | 38.18 | 37.33 | 3.44 |
| news | 899 | 1 | 22.84 | 28.48 | 33.17 | 0.71 |
| silent | 898 | 2 | 24.67 | 34.99 | 36.87 | 0.05 |
| glasgow | 899 | 1 | 18.19 | 30.52 | 34.72 | -1.75 |
|  | WCDMA-2 |  |
| foreman | 901 | 0 | 19.87 | 33.00 | 33.35 | -0.47 |
| hall | 900 | 0 | 25.13 | 38.52 | 41.49 | -1.50 |
| container | 900 | 0 | 26.35 | 38.7 | 37.33 | 0.64 |
| news | 900 | 0 | 23.33 | 29.28 | 33.88 | -0.39 |
| silent | 900 | 0 | 26.67 | 36.06 | 37.36 | -1.07 |
| glasgow | 899 | 1 | 19.42 | 31.69 | 35.09 | -1.37 |
|  | WCDMA-3 |  |
| foreman | 900 | 0 | 19.35 | 33.33 | 33.09 | -0.41 |
| hall | 900 | 0 | 24.81 | 38.37 | 41.5 | 3.35 |
| container | 900 | 0 | 23.81 | 37.28 | 36.59 | -0.41 |
| news | 900 | 0 | 24.08 | 27.68 | 33.18 | 1.81 |
| silent | 900 | 0 | 25.35 | 35.69 | 37.31 | -0.18 |
| glasgow | 899 | 1 | 19.95 | 32.01 | 35.54 | -1.32 |
|  | WCDMA-4 |  |
| foreman | 900 | 0 | 24.39 | 35.93 | 36.11 | -0.11 |
| hall | 900 | 0 | 30.16 | 40.39 | 42.75 | -0.19 |
| container | 900 | 0 | 32.28 | 40.37 | 39.66 | 3.50 |
| news | 900 | 0 | 28.69 | 35.94 | 37.69 | 0.22 |
| silent | 900 | 0 | 30.10 | 36.98 | 38.34 | -0.12 |
| glasgow | 900 | 0 | 23.73 | 34.72 | 37.25 | -0.06 |
|  | WCDMA-5 |  |
| foreman | 901 | 0 | 23.87 | 35.44 | 35.82 | -0.72 |
| hall | 900 | 0 | 29.95 | 40.21 | 42.64 | -0.34 |
| container | 900 | 0 | 32.16 | 40.39 | 39.67 | 2.31 |
| news | 900 | 0 | 28.08 | 34.46 | 37.13 | 0.21 |
| silent | 900 | 0 | 29.75 | 36.90 | 38.26 | -0.41 |
| glasgow | 900 | 0 | 23.81 | 34.82 | 37.17 | 0.39 |
|  | WCDMA-6 |  |
| foreman | 900 | 0 | 24.55 | 35.72 | 35.95 | 0.17 |
| hall | 900 | 0 | 29.9 | 40.47 | 42.78 | -0.25 |
| container | 900 | 0 | 32.39 | 40.42 | 39.69 | 2.35 |
| news | 900 | 0 | 29.09 | 35.66 | 37.73 | 1.06 |
| silent | 900 | 0 | 29.95 | 36.96 | 38.28 | -0.24 |
| glasgow | 900 | 0 | 23.75 | 34.96 | 37.28 | -0.39 |

# Table 3: WCDMA error pattern, not sent through mux, 64kbps channel

|  | Anchor | Data Partitioning | Difference |
| --- | --- | --- | --- |
|  | WCDMA-1 |  |
| sequence | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | decoded frames | drop frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) |
| foreman | 880 | 20 | 19.03 | 33.11 | 32.73 | 900 | 0 | 22.18 | 34.98 | 34.99 | 3.15 |
| hall | 885 | 15 | 20.61 | 31.07 | 36.19 | 900 | 0 | 24.1 | 36.59 | 38.59 | 3.49 |
| container | 876 | 24 | 21.42 | 35.11 | 33.39 | 900 | 0 | 25.03 | 36.77 | 35.38 | 3.61 |
| news | 889 | 11 | 19.58 | 22.34 | 27.97 | 900 | 0 | 23.79 | 31.78 | 35.75 | 4.21 |
| silent | 871 | 29 | 20.79 | 32.67 | 34.69 | 900 | 0 | 27.89 | 36.27 | 37.66 | 7.1 |
| glasgow | 879 | 21 | 20.68 | 32.41 | 36.03 | 900 | 0 | 20.58 | 31.86 | 35.31 | -0.1 |
|  | WCDMA-2 |  |
| foreman | 872 | 28 | 19.42 | 32.88 | 33.42 | 900 | 0 | 22.65 | 35.16 | 34.65 | 3.23 |
| hall | 883 | 17 | 22.95 | 30.9 | 36.62 | 901 | 0 | 28.37 | 38.94 | 42.08 | 5.42 |
| container | 883 | 17 | 22.75 | 34.19 | 34.2 | 900 | 0 | 29.67 | 39.33 | 38.69 | 6.92 |
| news | 870 | 30 | 21.24 | 27.08 | 32.03 | 900 | 0 | 27.28 | 34.82 | 37.22 | 6.04 |
| silent | 892 | 8 | 24.49 | 35.5 | 37.33 | 900 | 0 | 29.12 | 36.65 | 38.02 | 4.63 |
| glasgow | 887 | 13 | 21.38 | 33.3 | 36.51 | 901 | 0 | 22.65 | 33.88 | 36.62 | 1.27 |
|  | WCDMA-3 |  |
| foreman | 870 | 30 | 19.69 | 32.29 | 31.97 | 900 | 0 | 23.13 | 35.19 | 35.51 | 3.44 |
| hall | 894 | 6 | 21.61 | 30.46 | 37.42 | 900 | 0 | 26.09 | 38.77 | 41.11 | 4.48 |
| container | 879 | 21 | 22.83 | 34.01 | 34.94 | 900 | 0 | 29.03 | 38.97 | 38.56 | 6.2 |
| news | 892 | 8 | 21.09 | 26.69 | 32.21 | 900 | 0 | 27.46 | 31.01 | 34.73 | 6.37 |
| silent | 889 | 11 | 22.56 | 29.07 | 28.31 | 900 | 0 | 27.73 | 35.73 | 37.9 | 5.17 |
| glasgow | 890 | 10 | 21.45 | 33.27 | 35.83 | 900 | 0 | 22.33 | 33.68 | 36.49 | 0.88 |
|  | WCDMA-4 |  |
| foreman | 898 | 2 | 23.63 | 34.97 | 35.35 | 900 | 0 | 25.61 | 36.24 | 36.7 | 1.98 |
| hall | 899 | 1 | 29.07 | 36.34 | 41.25 | 900 | 0 | 30.97 | 40.49 | 42.84 | 1.9 |
| container | 900 | 0 | 30.49 | 39.99 | 39.27 | 900 | 0 | 32.55 | 40.4 | 39.63 | 2.06 |
| news | 898 | 2 | 25.31 | 28.27 | 35.17 | 900 | 0 | 29.48 | 36.22 | 37.92 | 4.17 |
| silent | 896 | 4 | 29.56 | 37.03 | 38.73 | 900 | 0 | 30.67 | 37.06 | 38.42 | 1.11 |
| glasgow | 900 | 0 | 24.32 | 35.18 | 37.46 | 900 | 0 | 24.39 | 34.9 | 37.32 | 0.07 |
|  | WCDMA-5 |  |
| foreman | 897 | 3 | 24.48 | 36.02 | 36.37 | 900 | 0 | 25.09 | 36.21 | 36.45 | 0.61 |
| hall | 897 | 3 | 29.71 | 35.94 | 40.77 | 900 | 0 | 31.35 | 39.51 | 42.6 | 1.64 |
| container | 895 | 5 | 29.88 | 39.83 | 39.55 | 900 | 0 | 33.32 | 40.42 | 39.72 | 3.44 |
| news | 876 | 24 | 26.58 | 32.81 | 36.59 | 900 | 0 | 28.82 | 36.14 | 37.72 | 2.24 |
| silent | 899 | 1 | 29.48 | 36.47 | 38.23 | 900 | 0 | 30.42 | 37.01 | 38.36 | 0.94 |
| glasgow | 900 | 0 | 24.17 | 34.98 | 37.39 | 900 | 0 | 24.4 | 35.13 | 37.46 | 0.23 |
|  | WCDMA-6 |  |
| foreman | 899 | 1 | 24.59 | 35.96 | 36.32 | 900 | 0 | 25.42 | 36.16 | 36.51 | 0.83 |
| hall | 899 | 1 | 29.4 | 35.04 | 40.59 | 900 | 0 | 30.86 | 40.57 | 42.84 | 1.46 |
| container | 895 | 5 | 28.51 | 37.97 | 37.56 | 900 | 0 | 33.46 | 40.34 | 39.76 | 4.95 |
| news | 898 | 2 | 24.83 | 34.94 | 37.37 | 900 | 0 | 30.07 | 35.57 | 37.36 | 5.24 |
| silent | 899 | 1 | 29.97 | 37.04 | 38.75 | 900 | 0 | 30.39 | 37.01 | 38.38 | 0.42 |
| glasgow | 899 | 1 | 23.85 | 34.92 | 37.22 | 901 | 0 | 24.32 | 35.01 | 37.45 | 0.47 |

<<plots of PSNR vs. frame number for all simulations>>

# Table 4: DECT error pattern, sent through mux, 32kbps channel

|  | Anchor( MB refresh ) | H.263+ ( Frame refresh ) | Difference |
| --- | --- | --- | --- |
|  | DECT 1.4km/h 4dB |  |
| sequence | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) |
| hall | 387 | 513 | 15.46 | 15.99 | 21.95 | 366 | 534 | 15.69 | 16.2 | 22.26 | 0.23 |
| silent | 357 | 543 | 5.48 | 6.77 | 5.7 | 335 | 565 | 6.96 | 7.93 | 6.86 | 1.48 |
| news | 340 | 560 | 8.65 | 6.1 | 5.65 | 317 | 583 | 10.67 | 8.35 | 8.19 | 2.02 |
| container | 364 | 536 | 4.71 | 5.92 | 6.29 | 341 | 559 | 4.95 | 6.14 | 6.5 | 0.24 |
|  | DECT 1.4km/h 10dB |  |
| hall | 752 | 148 | 9.55 | 10.98 | 9.78 | 748 | 152 | 19.57 | 29.53 | 33.32 | 10.02 |
| silent | 726 | 174 | 5.49 | 6.77 | 5.7 | 725 | 175 | 14.8 | 19.14 | 18.9 | 9.31 |
| news | 746 | 154 | 8.69 | 6.12 | 5.66 | 729 | 171 | 14.84 | 15.68 | 15.55 | 6.15 |
| container | 745 | 155 | 4.73 | 5.95 | 6.31 | 745 | 155 | 12.71 | 16.55 | 16.9 | 7.98 |
|  | DECT 1.4km/h 20dB |  |
| hall | 899 | 1 | 7.47 | 9.35 | 7 | 900 | 0 | 22.24 | 30.84 | 32.03 | 14.77 |
| silent | 898 | 2 | 20.66 | 34.34 | 36.28 | 898 | 2 | 26 | 35.28 | 36.88 | 5.34 |
| news | 898 | 2 | 20.45 | 25.77 | 31.54 | 898 | 2 | 22.88 | 31.45 | 34.37 | 2.43 |
| container | 899 | 1 | 22.81 | 36.83 | 36.4 | 897 | 3 | 24.22 | 36.49 | 35.63 | 1.41 |
|  | DECT 1.4km/h 22dB |  |
| hall | 900 | 0 | 4.63 | 7.61 | 5.41 | 900 | 0 | 22.33 | 30.65 | 31.83 | 17.7 |
| silent | 900 | 0 | 20.56 | 34.05 | 36.42 | 899 | 1 | 26.51 | 35.45 | 37 | 5.95 |
| news | 899 | 1 | 21.78 | 25.84 | 31.81 | 900 | 0 | 23.86 | 31.84 | 34.66 | 2.08 |
| container | 899 | 1 | 24.31 | 37.31 | 36.99 | 899 | 1 | 24.8 | 36.75 | 35.79 | 0.49 |
|  | DECT 14km/h 4dB |  |
| hall | 477 | 423 | 4.58 | 7.58 | 5.38 | 498 | 402 | 4.58 | 7.58 | 5.38 | 0 |
| silent | 506 | 394 | 5.47 | 6.75 | 5.68 | 499 | 401 | 5.47 | 6.75 | 5.68 | 0 |
| news | 426 | 474 | 8.62 | 6.08 | 5.63 | 440 | 460 | 8.62 | 6.08 | 5.63 | 0 |
| container | 437 | 463 | 10.47 | 12.1 | 11.52 | 456 | 444 | 10.47 | 12.08 | 11.51 | 0 |
|  | DECT 14km/h 10dB |  |
| hall | 882 | 18 | 12.44 | 13.7 | 14.05 | 874 | 26 | 12.43 | 13.68 | 14.01 | -0.01 |
| silent | 875 | 25 | 11.57 | 12.33 | 11.89 | 879 | 21 | 12.23 | 12.96 | 12.54 | 0.66 |
| news | 889 | 11 | 12.68 | 8.8 | 9.1 | 860 | 40 | 11.7 | 9.24 | 9.27 | -0.98 |
| container | 876 | 24 | 12.1 | 15.31 | 13.93 | 877 | 23 | 12.1 | 15.3 | 13.92 | 0 |
|  | DECT 14km/h 20dB |  |
| hall | 897 | 3 | 24.58 | 34.43 | 39.28 | 893 | 7 | 25.07 | 38.02 | 40.94 | 0.49 |
| silent | 900 | 0 | 20.5 | 25.66 | 26.29 | 901 | 0 | 24.69 | 32.46 | 33.5 | 4.19 |
| news | 900 | 0 | 20.15 | 31.31 | 34.28 | 901 | 0 | 22.27 | 32.46 | 35.26 | 2.12 |
| container | 900 | 0 | 4.74 | 5.94 | 6.31 | 893 | 7 | 16.71 | 24.07 | 23.39 | 11.97 |
|  | DECT 14km/h 22dB |  |
| hall | 900 | 0 | 25.37 | 34.72 | 39.4 | 900 | 0 | 25.61 | 37.64 | 40.44 | 0.24 |
| silent | 900 | 0 | 20.78 | 25.75 | 26.37 | 900 | 0 | 25.45 | 32.82 | 33.97 | 4.67 |
| news | 900 | 0 | 21.97 | 32.28 | 34.83 | 900 | 0 | 24.1 | 33.58 | 35.96 | 2.13 |
| container | 900 | 0 | 4.74 | 5.94 | 6.31 | 893 | 7 | 17.88 | 24.7 | 24.21 | 13.14 |

| Transmitted using AL-1 Mux |
| --- |
|  | Data Partitioning ( Variable GOB ) | Data Partitioning ( Variable MB ) |
|  | DECT 1.4km/h 4dB |  |
| sequence | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) |
| hall | 570 | 330 | 6.56 | 10.15 | 8.24 | -8.9 | 629 | 271 | 15.32 | 32.69 | 36.68 | -0.14 |
| silent | 541 | 359 | 7.71 | 8.18 | 7.18 | 2.23 | 537 | 363 | 9.16 | 9.82 | 8.76 | 3.68 |
| news | 574 | 326 | 14.29 | 22.88 | 27.89 | 5.64 | 625 | 275 | 14.54 | 13.68 | 13.37 | 5.89 |
| container | 565 | 335 | 6.28 | 6.82 | 7.17 | 1.57 | 617 | 283 | 14.76 | 27.75 | 29.63 | 10.05 |
|  | DECT 1.4km/h 10dB |  |
| hall | 825 | 75 | 16.86 | 25.23 | 25.27 | 7.31 | 858 | 42 | 21.14 | 36.17 | 39.39 | 11.59 |
| silent | 812 | 88 | 16.11 | 22.52 | 22.67 | 10.62 | 802 | 98 | 17.32 | 27.04 | 27.91 | 11.83 |
| news | 833 | 67 | 15.38 | 14.81 | 16.28 | 6.69 | 842 | 58 | 20.03 | 24.57 | 29.98 | 11.34 |
| container | 839 | 61 | 17.28 | 27.41 | 27.07 | 12.55 | 835 | 65 | 16.23 | 23.24 | 22.95 | 11.5 |
|  | DECT 1.4km/h 20dB |  |
| hall | 899 | 1 | 26.43 | 37.5 | 40.44 | 18.96 | 901 | 0 | 26.34 | 37.88 | 40.31 | 18.87 |
| silent | 897 | 3 | 25.96 | 34.75 | 35.06 | 5.3 | 896 | 4 | 26.18 | 35.35 | 36.92 | 5.52 |
| news | 900 | 0 | 25.41 | 32.15 | 35.14 | 4.96 | 900 | 0 | 26.34 | 33.23 | 35.91 | 5.89 |
| container | 899 | 1 | 27.05 | 37.98 | 37.25 | 4.24 | 899 | 1 | 27.44 | 38.26 | 37.33 | 4.63 |
|  | DECT 1.4km/h 22dB |  |
| hall | 900 | 0 | 26.84 | 38.52 | 41.19 | 22.21 | 900 | 0 | 27.06 | 38.73 | 41.35 | 22.43 |
| silent | 899 | 1 | 26.39 | 35.4 | 36.95 | 5.83 | 902 | 0 | 26.61 | 35.43 | 37 | 6.05 |
| news | 900 | 0 | 25.99 | 33.42 | 35.57 | 4.21 | 899 | 1 | 26.32 | 33.47 | 35.73 | 4.54 |
| container | 899 | 1 | 27.72 | 38.12 | 37.43 | 3.41 | 901 | 0 | 27.98 | 38.31 | 37.43 | 3.67 |
|  | DECT 14km/h 4dB |  |
| hall | 779 | 121 | 4.79 | 7.67 | 5.43 | 0.21 | 799 | 101 | 13.14 | 28.35 | 31.92 | 8.56 |
| silent | 742 | 158 | 5.78 | 6.97 | 5.89 | 0.31 | 684 | 216 | 12.19 | 25.55 | 28.97 | 6.72 |
| news | 815 | 85 | 8.78 | 6.11 | 5.66 | 0.16 | 788 | 112 | 12.19 | 19.97 | 22.65 | 3.57 |
| container | 774 | 126 | 4.91 | 5.94 | 6.31 | -5.56 | 783 | 117 | 5.34 | 6.37 | 6.74 | -5.13 |
|  | DECT 14km/h 10dB |  |
| hall | 896 | 4 | 15.04 | 25.96 | 30.95 | 2.6 | 900 | 0 | 18.22 | 33.83 | 37.81 | 5.78 |
| silent | 900 | 0 | 15.04 | 28.9 | 33.64 | 3.47 | 893 | 7 | 19.27 | 29.81 | 32.82 | 7.7 |
| news | 904 | 0 | 14.39 | 20.28 | 25.15 | 1.71 | 907 | 0 | 16.74 | 22.94 | 27.61 | 4.06 |
| container | 899 | 1 | 9.96 | 11.26 | 11.71 | -2.14 | 914 | 0 | 16.54 | 28.96 | 29.34 | 4.44 |
|  | DECT 14km/h 20dB |  |
| hall | 900 | 0 | 25.25 | 37.68 | 40.63 | 0.67 | 901 | 0 | 25.65 | 38.2 | 41.17 | 1.07 |
| silent | 900 | 0 | 25.95 | 35.2 | 36.67 | 5.45 | 900 | 0 | 26.13 | 35.1 | 36.76 | 5.63 |
| news | 900 | 0 | 23.68 | 31.5 | 34.52 | 3.53 | 902 | 0 | 24.74 | 32.23 | 35.49 | 4.59 |
| container | 902 | 0 | 23.27 | 35.23 | 34 | 18.53 | 901 | 0 | 26.17 | 37.74 | 36.41 | 21.43 |
|  | DECT 14km/h 22dB |  |
| hall | 900 | 0 | 26.78 | 38.1 | 41.19 | 1.41 | 903 | 0 | 27.04 | 38.66 | 41.33 | 1.67 |
| silent | 900 | 0 | 26.91 | 35.39 | 36.98 | 6.13 | 900 | 0 | 26.73 | 35.3 | 36.82 | 5.95 |
| news | 901 | 0 | 25.75 | 32.13 | 34.89 | 3.78 | 901 | 0 | 25.59 | 32.88 | 35.55 | 3.62 |
| container | 900 | 0 | 26.49 | 37.3 | 36.06 | 21.75 | 902 | 0 | 28.12 | 38.36 | 37.19 | 23.38 |

| Data Partitioning, transmitted using AL-3 Mux |
| --- |
| DECT 1.4km/h 4dB |
| sequence | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) |
| hall | 230 | 670 | 10.85 | 21.44 | 21.17 | -4.61 |
| silent | 211 | 689 | 6.88 | 7.25 | 6.23 | 1.4 |
| news | 227 | 673 | 15.17 | 18.36 | 19.34 | 6.52 |
| container | 224 | 676 | 4.73 | 5.93 | 6.3 | 0.02 |
| DECT 1.4km/h 10dB |
| hall | 659 | 241 | 17.93 | 25.87 | 25.24 | 8.38 |
| silent | 587 | 313 | 12.6 | 13.84 | 12.81 | 7.11 |
| news | 662 | 238 | 19.72 | 25.15 | 29.05 | 11.03 |
| container | 655 | 245 | 10.78 | 15.52 | 15.6 | 6.05 |
| DECT 1.4km/h 20dB |
| hall | 896 | 4 | 26.33 | 38.46 | 41.22 | 18.86 |
| silent | 880 | 20 | 25.69 | 35.26 | 36.8 | 5.03 |
| news | 894 | 6 | 25.73 | 32.23 | 35.28 | 5.28 |
| container | 894 | 6 | 26.17 | 37.16 | 36.28 | 3.36 |
| DECT 1.4km/h 22dB |
| hall | 900 | 0 | 26.9 | 38.69 | 41.32 | 22.27 |
| silent | 892 | 8 | 26.05 | 35.3 | 36.85 | 5.49 |
| news | 898 | 2 | 25.83 | 32.57 | 35.36 | 4.05 |
| container | 899 | 1 | 26.85 | 37.3 | 36.49 | 2.54 |
| DECT 14km/h 4dB |
| hall | 158 | 742 | 4.58 | 7.58 | 5.38 | 0 |
| silent | 108 | 792 | 5.46 | 6.75 | 5.68 | -0.01 |
| news | 120 | 780 | 8.61 | 6.08 | 5.62 | -0.01 |
| container | 116 | 784 | 4.69 | 5.91 | 6.28 | -5.78 |
| DECT 14km/h 10dB |
| hall | 749 | 151 | 13.48 | 18.1 | 15.43 | 1.04 |
| silent | 620 | 280 | 12.9 | 32.16 | 34.02 | 1.33 |
| news | 717 | 183 | 15.78 | 22.83 | 27.98 | 3.1 |
| container | 681 | 219 | 15.62 | 29.95 | 30.04 | 3.52 |
| DECT 14km/h 20dB |
| hall | 900 | 0 | 24.25 | 37.93 | 40.94 | -0.33 |
| silent | 896 | 4 | 25.09 | 34.83 | 36.4 | 4.59 |
| news | 900 | 0 | 22.83 | 30.18 | 34.13 | 2.68 |
| container | 900 | 0 | 24.56 | 37.02 | 35.47 | 19.82 |
| DECT 14km/h 22dB |
| hall | 900 | 0 | 25.53 | 38.29 | 41.19 | 0.16 |
| silent | 899 | 1 | 26.39 | 35.19 | 36.72 | 5.61 |
| news | 900 | 0 | 24.67 | 31.67 | 35.04 | 2.7 |
| container | 900 | 0 | 26.75 | 38.02 | 36.48 | 22.01 |

# Table 5: DECT error pattern, not sent through mux, 32kbps channel

|  | Anchor | Data Partitioning | Difference |
| --- | --- | --- | --- |
|  | DECT 1.4km/h 4dB |  |
| sequence | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | decoded frames | dropped frames | PSNR (Y) | PSNR (Cb) | PSNR (Cr) | (PSNR (Y) |
| hall | 452 | 448 | 4.64 | 7.62 | 5.42 | 523 | 377 | 4.6 | 7.61 | 5.42 | -0.04 |
| silent | 408 | 492 | 6.13 | 7.56 | 6.52 | 570 | 330 | 15.91 | 30.12 | 33.12 | 9.78 |
| news | 442 | 458 | 10.25 | 7.54 | 7.12 | 554 | 346 | 9.79 | 6.44 | 5.93 | -0.46 |
| container | 415 | 485 | 15.09 | 25.03 | 23.87 | 549 | 351 | 16.12 | 26.14 | 25.94 | 1.03 |
|  | DECT 1.4km/h 10dB |  |
| hall | 710 | 190 | 6.19 | 9.73 | 7.62 | 805 | 95 | 11.89 | 16.09 | 14.71 | 5.7 |
| silent | 686 | 214 | 16.65 | 19.54 | 22.41 | 811 | 89 | 19.79 | 31.15 | 33.95 | 3.14 |
| news | 747 | 153 | 10.88 | 7.81 | 7.43 | 811 | 89 | 17.99 | 20.6 | 24.59 | 7.11 |
| container | 667 | 233 | 7.82 | 8.7 | 9.11 | 817 | 83 | 14.09 | 20.65 | 20.44 | 6.27 |
|  | DECT 1.4km/h 20dB |  |
| hall | 884 | 16 | 17.68 | 31.3 | 35.58 | 898 | 2 | 26.69 | 38.33 | 41.09 | 9.01 |
| silent | 892 | 8 | 17.67 | 33.15 | 35.97 | 896 | 4 | 25.71 | 35.15 | 36.83 | 8.04 |
| news | 888 | 12 | 18.97 | 23.77 | 29.03 | 898 | 2 | 25.93 | 33.21 | 35.75 | 6.96 |
| container | 883 | 17 | 24.04 | 36.99 | 35.86 | 897 | 3 | 26.83 | 37.48 | 36.35 | 2.79 |
|  | DECT 1.4km/h 22dB |  |
| hall | 889 | 11 | 20.98 | 33.08 | 37.61 | 899 | 1 | 27.01 | 38.38 | 41.14 | 6.03 |
| silent | 891 | 9 | 17.88 | 33.32 | 35.99 | 899 | 1 | 26.13 | 35.28 | 36.93 | 8.25 |
| news | 886 | 14 | 21.04 | 24.97 | 27.21 | 900 | 0 | 26.32 | 33.6 | 35.91 | 5.28 |
| container | 892 | 8 | 24.21 | 36.97 | 36.72 | 900 | 0 | 27.93 | 38.25 | 37.48 | 3.72 |
|  | DECT 14km/h 4dB |  |
| hall | 463 | 437 | 14.17 | 19.87 | 23.5 | 766 | 134 | 4.93 | 7.89 | 5.72 | -9.24 |
| silent | 381 | 519 | 10.05 | 15.38 | 14.75 | 726 | 174 | 5.76 | 6.92 | 5.84 | -4.29 |
| news | 462 | 438 | 11.36 | 9.92 | 9.55 | 793 | 107 | 9.07 | 6.22 | 5.72 | -2.29 |
| container | 417 | 483 | 12.08 | 14.26 | 14.51 | 761 | 139 | 14.54 | 29.67 | 28.05 | 2.46 |
|  | DECT 14km/h 10dB |  |
| hall | 728 | 172 | 15.7 | 21.24 | 27.06 | 896 | 4 | 5.66 | 8.26 | 5.92 | -10.04 |
| silent | 682 | 218 | 7.15 | 9.15 | 8.05 | 886 | 14 | 8.62 | 10.61 | 9.58 | 1.47 |
| news | 672 | 228 | 8.96 | 6.19 | 5.76 | 896 | 4 | 10.63 | 7.84 | 7.6 | 1.67 |
| container | 678 | 222 | 10.06 | 11.03 | 11.71 | 896 | 4 | 9.05 | 9.44 | 9.55 | -1.01 |
|  | DECT 14km/h 20dB |  |
| hall | 881 | 19 | 19.33 | 22.78 | 28.3 | 901 | 0 | 25.35 | 37.14 | 39.97 | 6.02 |
| silent | 872 | 28 | 18.97 | 23.44 | 26.84 | 900 | 0 | 24.14 | 34.98 | 36.28 | 5.17 |
| news | 876 | 24 | 14.78 | 21.91 | 25.66 | 900 | 0 | 23.73 | 30.86 | 34.68 | 8.95 |
| container | 857 | 43 | 20.79 | 34.32 | 33.39 | 901 | 0 | 24.63 | 35.88 | 35.06 | 3.84 |
|  | DECT 14km/h 22dB |  |
| hall | 894 | 6 | 19.77 | 22.91 | 28.43 | 900 | 0 | 25.86 | 37.83 | 39.79 | 6.09 |
| silent | 877 | 23 | 18.72 | 23.74 | 27.46 | 900 | 0 | 23.8 | 34.02 | 35.89 | 5.08 |
| news | 891 | 9 | 19.51 | 26.19 | 31.3 | 900 | 0 | 25.14 | 32.29 | 35.29 | 5.63 |
| container | 864 | 36 | 23.37 | 36.51 | 36.2 | 901 | 0 | 26.55 | 37.65 | 36.78 | 3.18 |

# PSNR Plots